## Slide 1: Beam-beam Studies for HL-LHC
A.Valishev (Fermilab/US LARP) for WP2 Task 2.5
Joint LARP CM20 – HiLumi Meeting
April 8-10, 2013
Contributors: D.Banfi, A.Burov, S.Fartoukh, B.Muratori, K.Ohmi, S.Paret, T.Pieloni, J.Qiang, D.Shatilov, S.White, F.Zimmermann

## Slide 2: ICFA Mini-Workshop on Beam-Beam Effects in Hadron Colliders. CERN Mar. 18-22 2013
http://indico.cern.ch/event/beam-beam-2013
Program – 4 ½ days, 52 talks 58 registered participants
Beam-beam experience in hadron colliders
Beam-beam experience in lepton colliders
Single Particle Effects I - head-on beam-beam effects
Single Particle Effects II - parasitic beam-beam effects
Beam-beam compensation schemes
Strong-strong beam-beam effects
Theory and simulations
Operational aspects of beam-beam effects
Studies for future Projects

## Slide 3: HL-LHC Beam-Beam Study
Evaluate beam-beam for HL-LHC scenarios, identify minimum requirements – b*, crossing scheme
Evaluate limitations
Luminosity leveling techniques
Develop self-consistent simulations of beam-beam with other dynamical effects
  Interplay with machine impedance (A.Burov)
  Crab cavity, noise, offset, etc. (S.Paret)
Support new ideas

## Slide 4: Methods
Analytical calculations, where possible
Weak-strong
  Tune footprint (very fast)
  Dynamic Aperture (fast)
  Full-scale multi-particle simulation of intensity and emittance life time (slow)
Strong-strong
  Self-consistent multi-effect simulation (short reach as far as the number of turns, slowest)

## Slide 5: Simulation Tools
Weak-strong
  SixTrack. Well-tested code, the backbone of tracking studies for LHC design.
  Lifetrac. Many years of use for electron machines and Tevatron. Well-tested 6D beam-beam with crossing angle and crab cavity.
Strong-Strong
  BeamBeam3D. Many users – LBNL, FNAL, BNL
  COMBI. Good for multi-bunch simulations

## Slide 6: Study Topics
Evaluate the options for HL-LHC
  Choice of basic options – b*, crossing scheme
  Luminosity leveling techniques
  Imperfections, mitigation of beam-beam
Develop self-consistent simulations of the beam-beam phenomena with other dynamical effects
  Interplay with machine impedance
  Crab cavity, noise, offset, etc.
Support new ideas

## Slide 8: HL-LHC Base Beam-Beam Parameters
Np=2.2x1011, e=2.5 mm
q=590 mrad = const
b*=15cm = const
x ~= 0.02 (3 IPs)
A/s = 12.5
Level with crab only

## Slide 9: Frequency Map Analysis
b*=15 cm, Np=2.2×1011
q=590 mrad
Dp/p=0
Lifetrac: full HL-LHC lattice (element-by-element, sextupoles)
+ beam-beam (head-on & long-range), 211 turns

## Slide 10: Frequency Map Analysis of HL-LHC options
b*=15cm q=590mrad Dp/p=1.1e-4
b*=15cm q=590mrad Dp/p=2.2e-4
D.Shatilov, A.Valishev

## Slide 11: From FMA to Dynamical Aperture
b*=15cm q=590mrad Dp/p=0
sz=7.5cm
b*=33cm q=590mrad Dp/p=0
sz=4cm
D.Shatilov, A.Valishev
Linear HL-LHC lattice (no sextupoles) + beam-beam (head-on & long-range)
DA based on 106 tracking turns, FMA – 213 turns

## Slide 12: From FMA to Dynamical Aperture
b*=40cm q=360mrad Dp/p=0
sz=4cm
D.Shatilov, A.Valishev
Linear HL-LHC lattice (no sextupoles) + beam-beam (head-on & long-range)
DA based on 106 tracking turns, FMA – 213 turns
b*=15cm q=590mrad Dp/p=1.1e-4
sz=7.5cm

## Slide 13: From FMA to Dynamical Aperture
b*=40cm q=360mrad Dp/p=0
sz=4cm
D.Shatilov, A.Valishev
Linear HL-LHC lattice (no sextupoles) + beam-beam (head-on & long-range)
DA based on 106 tracking turns, FMA – 213 turns
b*=33cm q=590mrad Dp/p=1.1e-4
sz=4cm

## Slide 14: DA Studies Sixtrack vs. Lifetrac
S.White, A.Valishev
HL-LHC lattice without magnetic errors (only chroma sextupoles)
DA based on 106 tracking turns. Np=2×1011, e=2.5mm

## Slide 15: DA Studies Sixtrack vs. Lifetrac

## Slide 16: DA Studies – Intensity Scan
D.Banfi, A.Valishev
HL-LHC lattice without magnetic errors (only chroma sextupoles)
DA based on 106 tracking turns. b*=0.15m, q=590 mrad, e=2.5mm

## Slide 17: Conclusion for Baseline
Weak-strong studies predict the scenario OK
Work in progress:
  Effect of multipole errors
  Multiparticle tracking

## Slide 18: Evolving HL-LHC Baseline S.Fartoukh
 | LHC nominal | HL-LHC 25 ns
# Bunches | 2808 | 2808
p/bunch [1011] | 1.15 (0.58A) | 2.2 (1.11 A)
gex,y [mm] | 3.75 | 2.5
eL [eV.s] | 2.5 | 2.5
sz [cm] | 7.5 | 7.5
sdp/p [10-3] | 0.1 | 0.1
b* [cm] | 55 | 15 ( 10)
X-angle [mrad] | 300 (10.0 s) | 590 ( 720) (12.5 s)
Lumi loss factor | 0.83 | 0.31
Peak lumi [1034] (with full Piwinsky angle) | 1.0 | 7.4
Virtual lumi [1034] (w/o Piwinsky angle) | 1.2 | 21.9
Tleveling [h] @ 5E34 | n/a | 9.0
#Pile up @5E34 | 25 | 140
Main HL-LHC beam & optics parameters
Time evolution of main parameters
(assuming no emittance growth)
 Only the b* profile will actually depend on the details of the leveling technique (bb limit, if any?)
Beam current
b* (assuming
no bb limit)
Lumi
Int. Lumi

## Slide 19: Evolving HL-LHC Baseline S.Fartoukh
 b* leveling seems to be the main option but leading a b-b tune shift of up to DQbb=0.033 for 3 experiments (IR1, IR5 & IR8)
Parameters | Leveling with c.-c. | Leveling with b*
# bunches | 2808 | 
bunch charge [1011] | 2.2 | 
emittance [mm] | 2.5 | 
r.m.s. bunch length [cm] | 7.5 | 
full X-angle [mrad] | 590 | 
initial b* [cm] | 15 | 72
c.-c. initial voltage [MV] | - 6.6 (“anti-crabbing”) | 12.5 (“full crabbing”)
initial Piwinsky angle | 4.76 | 0
initial lumi loss factor | 0.21 | 1.0
levelled lumi [1034cm-2s-1] | 5.0 | 
initial luminous region [cm] | 1.1 | 5.3
initial bb tune shift for 3 IRs (IR1, IR5 & IR8) | 0.016 (0.011+2×0.0025) | 0.033 (3×0.011)

## Slide 20: HL-LHC new Beam-Beam Parameters
Np=2.2x1011, e=2.5 mm
q=590 mrad = const
b*=7215cm
  A/s = 2612.5
x = 0.033 (3 IPs) initially, 0.014 at the end of fill
Level with b*

## Slide 21: DA for Beginning of Fill
HL-LHC lattice without magnetic errors (only chroma sextupoles)
DA based on 106 tracking turns. b*=0.15m, q=590 mrad, e=2.5mm
BB tune shift of x = 0.033 is ok even with A/s = 12.5 !
with full crab on, no imperfections though

## Slide 22: Multiparticle Tracking - Beginning of Fill
tN>500 hr, te=18 hr, tL=150 hr

## Slide 23: Cause of Emittance Growth
7th order does not seem to be a problem…
7th order
10th order
13th order

## Slide 24: Can X-Angle (Crab Voltage) be reduced?
HL-LHC lattice without magnetic errors (only chroma sextupoles)
DA based on 106 tracking turns. b*=0.15m, q=480 mrad, e=2.5mm
q=480 mrad (Crab Voltage 10 MV) corresponds to A/s = 10
at end of fill with Np=0.95x1011 x=0.014 – OK, IF emittance growth is contained!

## Slide 25: Summary of DA for full crab ON
Large margin at beginning of fill – easy to reduce x-angle
15% margin at end of fill with q=480 mrad should allow some emittance growth
What happens at intermediate steps?

## Slide 26: Will the New Option Work with 50ns?
HL-LHC lattice without magnetic errors (only chroma sextupoles)
DA based on 106 tracking turns.
In actual simulation: b*=0.15m, q=590x3 mrad
b*=1.5m q=590 mrad corresponds to A/s = 35
with Np=3.5x1011 e=3 mm x=0.043? (0.03) – preliminary OK!

## Slide 27: Study Topics
Investigate the options for HL-LHC
  Choice of basic options – b*, crossing scheme
  Luminosity leveling techniques
  Imperfections, mitigation of beam-beam
Develop self-consistent simulations of the beam-beam phenomena with other dynamical effects
  Interplay with machine impedance
  Crab cavity, noise, offset, etc.
Help understand the experimental data from LHC as it becomes available
  Also use RHIC for beam-beam experiments
Support new ideas

## Slide 28: Effects of Noise K. Ohmi

## Slide 29: Beam-Beam and Impedance S. White (Toohig Fellow) and X. Buffat

## Slide 30: Beam-Beam and Impedance S. White (Toohig Fellow) and X. Buffat

## Slide 31: Beam-Beam and Impedance S. White (Toohig Fellow) and X. Buffat

## Slide 32: Study Topics
Investigate the options for HL-LHC
  Choice of basic options – b*, crossing scheme
  Luminosity leveling techniques
  Imperfections, mitigation of beam-beam
Develop self-consistent simulations of the beam-beam phenomena with other dynamical effects
  Interplay with machine impedance
  Crab cavity, noise, offset, etc.
Help understand the experimental data from LHC as it becomes available
  Also use RHIC for beam-beam experiments
Support new ideas

## Slide 33: Circular Modes and Flat Beams for LHC
A special type of coupled beam optics can convert planar betatron modes into circular modes
For circular modes, the Space Charge tune shift is determined by the maximal emittance, being independent of the minimal one
After acceleration, the beam can be transferred into the planar state, becoming flat – gain in luminosity
With flat beams, leveling can be done with b* in the crossing plane – no need for crab cavity

## Slide 34: Luminosity Scenario with Flat Beams
A.Burov, A.Valishev
 | LHC nominal | HL-LHC 25 ns | HL-LHC Flat
# Bunches | 2808 | 2808 | 2808
p/bunch [1011] | 1.15 (0.58A) | 2.2 (1.11 A) | 2.2 (1.11 A)
eL [eV.s] | 2.5 | 2.5 | 2.5
sz [cm] | 7.5 | 7.5 | 7.5
sdp/p [10-3] | 0.1 | 0.1 | 0.1
gex,y [mm] | 3.75 | 2.5 | 4.0, 0.4
b* [cm] (baseline) | 55 | 15 | 55, 15
X-angle [mrad] | 285 | 590 (12.5 s) | 318 (10 s)
Lumi loss factor | 0.84 | 0.30 | 0.85
Peak lumi [1034] | 1.0 | 7.4 | 19.7
Virtual lumi [1034] | 1.2 | 24.0 | 23.6
Leveling |  | Crab cavity | bx=11m down

## Slide 35: Summary
Baseline HL-LHC scenario has been studied
  No bb-imposed show-stoppers so far
  Good agreement between two codes
  To do: effect of imperfections, multiparticle
New scenario challenging in terms of bb
  Preliminary results very encouraging – x=0.033 can be sustained
  Crossing angle = CC voltage can be reduced ~20% assuming zero emittance growth
Multi-physics effects – good progress, more work needed

## Slide 36: Asknowledgments
Many thanks to G.Arduini, D.Banfi, X.Buffat, A.Burov, S.Fartoukh, W.Herr, B.Muratori, S.Paret, T.Pieloni, J.Qiang, F.Schmidt, D.Shatilov, R.Tomas, S.White, F.Zimmermann…