## Slide 1: RF Modeling of the LHC Crab Cavity
Zenghai Li
SLAC

## Slide 2: Outline
RF Dipole Cavity (SLAC-ODU design)
  Cavity shape optimization
  FPC and HOM coupler design
DQW Cavity Simulation (BNL design)
  FPC comparison – small vs large port opening
  Surface fields and multipole field components
Multipacting simulation
Summary

## Slide 3: RF Dipole – SLAC-ODU Design
Iris aperture (diameter) (mm) | 84
Transverse dimension (mm) | 281
Vertical dimension (mm) | 281
RT (ohm/cavity) | 433
VT (MV/cavity) | 3.34
Bs (mT) | 55.6
Es (MV/m) | 33.4
Multipole b3 (mT.m)/m2 (for Vt=10MV) | 486
Multipole b5 (mT.m)/m4 (for VT=10MV) | 2.2e6
Cavity shape optimization
Pole surface curved to reduce b3 component
Transverse Inner dimension fit within 281mm

## Slide 4: Field Multipole Component
bn definition

## Slide 5: RF Dipole – SLAC – ODU Design
E B
HOM coupler
  deflecting plane (H-plane): ridged waveguide
  Other plane (V-plane): selective waveguide stub+coax
FP Coupler
  Coupling through symmetrizing waveguide stub

## Slide 6: FPC coupler – SLAC-ODU Design
Outer diameter: 62 mm
Inner diameter: 27 mm
On symmetrizing stub waveguide
No field enhancement

## Slide 7: Ridged Waveguide & Selective Coupling HOM Couplers
Ridged waveguide coupler for H-dipole and accelerating modes – operating mode below cutoff
Selective WG-stub-coaxial coupler for V-dipole and accelerating modes – no filter needed

## Slide 8: Alternative 3-Stage High-Pass Filter HOM Coupler
Good isolation of the operating mode (400MHz)
Lowest HOM is around 600 MHz. Good transmission above 570 MHz
With improved pass-band transmission and operating mode isolation

## Slide 9: 3-Stage High-Pass Filter HOM Coupler
Hook shaped antenna HOM coupler
Strong damping achieved for all the important modes
High B field on the HOM antenna is similar in amplitude as on the cavity wall
Cleaning, assembly, beam power handling? (beam power due to lowest acc mode (I=0.5AM): ~16*Qext)
E and B fields of operating mode
Showing rejection from the HOM coupler

## Slide 10: HOM damping with a 3-stage HOM HOM coupler
Strong damping achieved

## Slide 11: Impedance: (R_T/Q)*Qext*k (3 stage filter HOM coupler)

## Slide 12: Impedance
Transverse impedance referred in this file is RT

## Slide 13: Ridged Waveguide Coupler: Qext & Impedance
H-HOM coupler couples to both H-dip and Acc modes
V-HOM coupler couples to both V-dip and Acc modes
(preliminary)

## Slide 14: BNL DQW Cavity Simulation- FPC coupler
small FPC
large FPC
FPC coupling: 2.5e6
FPC coupling: 1.1e6

## Slide 15: Cavity with HOM high-pass filter
Z. Li @ 2nd Joint HiLumi LHC-LARP Annual Meeting
Modified from BNL HOM filter for 56 MHz SRF Quarter Wave Cavity
66 mm
66 mm

## Slide 16: BNL DQW Cavity Simulation – small FPC opening
same HOM small FPC
E B
Peak surface B field at the rounding of HOM port
diff HOM small FPC

## Slide 17: BNL DQW Cavity Simulation – large FPC opening
E B
Peak surface B field at the rounding of HOM port
Field asymmetric due to large FPC opening, symmetrizing needed

## Slide 18: BNL DQW Cavity Parameters
Parameters | same HOM small FPC | same HOM large FPC
Frequency (MHz) | 398 | 396
Qext | 2.5e6 | 1.1e6
RT (ohm/cavity) | 400 | 
VT (MV/cavity) | 3.34 | 3.34
Bs (mT) | 88 | 81
Es (MV/m) | 37.4 | 37.6
Electric center offset (mm) | 0.03 | 1.67
Multipole b3 (mT.m)/m2 (for VT=10MV) | 1074 | 1096
Multipole b5 (mT.m)/m4 (for VT=10MV) | 1.7e5 | 8.9e4

## Slide 19: BNL Design Multipacting - preliminary

## Slide 20: MP on End-plate and FPC coupler
MP on end-plate
Similar to the original prototype
MP at FPC

## Slide 21: FPC MP Improvement
MP at FPC improved with full rounding

## Slide 22: MP in Waveguide HOM Coupler
Significant MP between the (small curvature) ridged waveguide
(scan not complete )
Same V,
different y position
(partial result)

## Slide 23: MP in Waveguide HOM Coupler
Vertical groove not effective in suppressing MP
(scan not complete)
Same V,
different y position
(partial result)

## Slide 24: MP in Waveguide HOM Coupler
Slanted groove not effective in suppressing MP
(scan not complete)
(partial result)

## Slide 25: WG HOM Coupler MP mitigation
Larger curvature ridged gap minimizes the MP region
Small bump on one side of ridge further suppresses MP resonances

## Slide 26: Summary
RF Dipole crab cavity
  Cavity shape optimized to reduce multipole field components
  Ridged waveguide H-coupler and selective V-coupler provide effective damping
  MP mitigation in HOM coupler studied
BNL DQWCC
  RF parameter for different FPC coupler configurations being analyzed
In progress: coupler improvements, shape optimization, full multipacting scan and mitigation