## Slide 1: Fermilab experience with SiPM readout, as viewed through NEXT colored glasses
P Rubinov, Dec 4 2012

## Slide 2: 3 basic options
All electronics outside (“just cables”)
Amplifier/buffer close to SiPM (“only amp”)
Everything inside (“ASIC”)

## Slide 3: Just Cables
We have tried this on the TB4 (long coax cables, used with up to 10+ m)
  I think this can work but
    Cable design is critical (especially for crosstalk)
    Must have EXCELLENT common mode rejection
    Signals are small, potential for noise pickup is great
  Practical issues
    Testing will be tricky- the test system will have to be large enough to reproduce real system parasitics.

## Slide 4
Fairly standard technology
Rule: if there is a picture of a cell phone on the manufacturers web page, it is inexpensive.

## Slide 5
Available
0.1in = 2.54mm
Rule: if there is a picture of a tank (or worst of all fighter!) on the web page, it
20db @1ghz per 100ft
Not too lossy! ~same as lemo
Silver plated copper: is it ok?

## Slide 8: Buffer only
The idea would be to present the SiPM with larger impedance, drive cable with lower impedance.
  Adv: less susceptible to noise, xtalk
  Dis: power traces additional, can you do this without caps?
  I have no direct experience to offer
  Many commercials chips can be had a bare die

## Slide 9: ASIC
Actually, there are 2 options here: existing “ASIC” (aka commercial chips) or new ASIC
  EASIROC (LAL Orsay), TriP-t (FNAL), many others
  Can be very powerful, but not power hungry
  I don’t know of any that do not require bypass caps!
  Reliability would be a concern, but can be very good

## Slide 11: Summary
My gut feeling is that something in the middle is often best
  Some electronics, behind some shielding?
Are there other options?
  Delay line readout?
  Some other encoding scheme?