## Slide 1: CalVision April Test Beam Analysis
Christopher Martin
UVA

## Slide 2: April Test Beam
Single Crystal test beam (PWO and BGO)
7 SiPMs, 1 MCP
120 GeV Protons
Front-End: (Upstream) Channels 4,5,6
Back-End: (Downstream) Channels 0-3 + MCP
*Filter Only Applied to the “Back-End” of the Crystal (Channels 0,1,2, & 3) While “Front-End” (Channels 4,5, & 6) experience no direct filtration
Credit: Grace Cummings
Credit: Grace Cummings

## Slide 3: A study on MIPs
Focusing on events with amplitude < 80 mV
A timing analysis accompanied by an unexpected data structure
Found this data structure is correlated to the use of filters in data collection
The exact nature of the connection is yet to be fully understood
PWO (Parallel) Unfiltered
Credit: Alexander Ledovskoy
*A’max proportional to Integrated waveform

## Slide 4
Timing Analysis Method:
PWO (par) Filtered, Channel 6: (Threshold Voltage 25.12 mV)
TMCP is found as the time of the MCP signal peak for a particular event
The waveform is integrated
The time at which the integrated waveform achieves the given threshold voltage is found (TThr)
Crafting a 2D distribution of TThr – TMCP Vs. 1/A’max of events, one can find the width of the distribution within narrow bins of amplitude
The threshold values evaluated are generated by an exponential function, the values used never may exceed 95% the maximum of a given integrated waveform’s maximum
*Threshold Values used:
*A’max proportional to Integrated waveform
Credit: Max Dubnowski

## Slide 5
The Distribution is projected about the Y-axis within a “Nominal Amplitude” range (+/- 2 mV)
Then a gaussian fit is done at the peak of the 1D projection
The width of this peak represents the timing resolution for this particular channel, at the specified threshold voltage about the Nominal amplitude
PWO (par) Filtered, Channel 6, Nominal Amplitude: 16 mV (+/- 2 mV), Threshold Voltage: 25.12 mV*ns

## Slide 6: Timing Analysis: PWO (Parallel Orientation) Unfiltered
Groupings of Front-end / Back-end Channels
Resolution improves as Nominal Amplitudes increase
Back-end Channels seem to have better resolution up until 45-63 mV

## Slide 7: Timing Analysis: PWO (Parallel Orientation) Filtered
Similar groupings of Front-end / Back-end Channels
Resolution improves on Front-end Channels at higher Nominal Amplitudes
Overall, resolution is better on Front-end Channels

## Slide 8
Backend Channels (0-3) include large discrepancies
Filtered data seems to have a worse resolution for the most part.
A Closer look at Trends:
*PWO (parallel Orientation)

## Slide 9
A Closer look at Trends:
Similarity Between Filtered/Unfiltered data sets at low Nominal Amplitudes for front-end Channels (4-6)
At higher Nominal amplitudes the trends are similar but diverge
Still Sensitive to the Filter on Front End Channels
*PWO (parallel Orientation)
*Filter Only Applied to the “Back-End” of the Crystal (Channels 0,1,2, & 3) While “Front-End” (Channels 4,5, & 6) experience no direct filtration
* Channel 5_45 mV: The Unfiltered data has better resolution

## Slide 10
A Closer Look at Channel 0 from the PWO (parallel) Filtered Data

## Slide 11
PWO (parallel) Filtered Data Set, Channel 4
*Filter Only Applied to the “Back-End” of the Crystal (Channels 0,1,2, & 3) While “Front-End” (Channels 4,5, & 6) experience no direct filtration

## Slide 12
<- PWO (Parallel) Unfiltered, Channel 0
PWO (Parallel) Filtered, Channel 0 ->

## Slide 13
<- PWO (Parallel) Unfiltered, Channel 1
PWO (Parallel) Filtered, Channel 1 ->

## Slide 14
<- PWO (Parallel) Unfiltered, Channel 2
PWO (Parallel) Filtered, Channel 2 ->

## Slide 15
<- PWO (Parallel) Unfiltered, Channel 3
PWO (Parallel) Filtered, Channel 3 ->

## Slide 16
<- PWO (Parallel) Unfiltered, Channel 4
PWO (Parallel) Filtered, Channel 4 ->

## Slide 17
<- PWO (Parallel) Unfiltered, Channel 5
PWO (Parallel) Filtered, Channel 5 ->

## Slide 18
<- PWO (Parallel) Unfiltered, Channel 6
PWO (Parallel) Filtered, Channel 6 ->

## Slide 19
Determined size of a SiPM to be 6 mm x 6 mm, approximate the size as a circle of radius mm
R < mm : “HITS”
R > mm : “NO HIT”/”MISS”
PWO (Parallel) Filtered, Channel 0: Cut on Location of Events wrt Channel 0 SiPM

## Slide 20
SiPM
2 mm
4 mm
8 mm
12 mm
More Radials cuts:
Radial Cuts are made on the distance an event occurs at wrt to the center of the SiPM
Cuts will occur in “Rings”:
  R < 2 mm
  2 mm < R < 4 mm
  4 mm < R < 8 mm
  8 mm < R < 12 mm
  R > 12 mm

## Slide 21
R < 2 mm 2 mm < R < 4 mm 4 mm < R < 8 mm
8 mm < R < 12 mm R > 12 mm
PWO (Parallel) Filtered, Channel 0: Cuts on Events occurring at Radii further from the center of the relevant SiPM

## Slide 22
(R < 8 mm)
(R > 8 mm)
PWO (Parallel) Filtered, Channel 0: An informed cut on Radius

## Slide 23
PWO (Parallel) Filtered, Channel 4: An informed cut on Radius
(R < 8 mm)
(R > 8 mm)

## Slide 24
PWO (Parallel) Filtered, Channel 4: Radial Cut on Hit/Miss
R < mm : “HITS”
R > mm : “NO HIT”/”MISS”

## Slide 25
BGO (parallel) Filtered, Channel 0: Potentially Experiencing Similar “Double Peaks”

## Slide 26
BGO (parallel) Filtered, Channel 0: Still of 2D Distribution at Threshold Voltage of 25.12 mV

## Slide 27
BGO (parallel) Filtered, Channel 0: Regime Split due to the same 8 mm radial cut
(R < 8 mm)
(R > 8 mm)

## Slide 28
BGO (parallel) Filtered, Channel 0: Regime Split due to the Hit/Miss Cut
R < mm : “HITS”
R > mm : “NO HIT”/”MISS”

## Slide 29
ntracks == 1 R < 8 mm
Threshold Voltage 25.12 mV
Left: A ~ 17.2 mV , ∆t ~ -1.2 ns Center: A~ 13 mV , ∆t ~ -0.8 ns
Right: A~ 11 mV, ∆t ~ -0.8 ns
*
PWO (Parallel) Filtered, Channel 0 : Observing Single Event Waveforms In notable regimes

## Slide 30
Single Pulses Closer to SiPM

## Slide 31
ntracks == 1 R > 8 mm
Threshold Voltage 25.12 mV
Left: A ~ 9.4 mV , ∆t ~ 1.4 ns Center: A~ 6.8 mV , ∆t ~ 2.6 ns Right: A~ 5.1 mV, ∆t ~ 3.5 ns
*
PWO (Parallel) Filtered, Channel 0 : Observing Single Event Waveforms In notable regimes

## Slide 32
Single Pulses Further from SiPM

## Slide 33
Angle (θ) is calculated wrt to the normal
Used the slopes of the track X(z) & Y(z)
Angular Distributions and Cuts
Angular studies yielded a weak angular dependence
Distribution of angles is fairly narrow about direct strikes
PWO (par) Filtered, Channel 0 ->
Credit: Grace Cummings

## Slide 34
Conclusion and Goals:
Overall, we’re experiencing this two peak structure due to the presence of the filter
There is large spatial dependence of this structure and little to no angular dependence
Next steps include:
  Exploring average waveforms at similar amplitudes for each unique regime
  Establishing an uncertainty about the timing resolution
  More in-Depth BGO studies