## Slide 1: PCB Washing Update
Sotiris Vlachos

## Slide 2: PCBs as sent Manufacturers
Final PCB treatment at Merlin before dispatch:
15% IPA + 85% Water
Water rinse
Hot air blower - No baking
Cover bords (from China) arrive ‘dirty’,

## Slide 3
Manchester
Lancaster
Sheffield
Cambridge
Sussex
Daresbury Factory
Cleaning
Station
Cleaning
Station
Daresbury QC - Sorting
Side Boards
124 per APA
Head Boards
80 per APA
NEW
NEW proposed PCB process path
NEED : 1 FTE @ DL
(will also ensure final inspection - QC and
administration – DB entries, sorting per APA)
at least 80 head boards and 124 side boards to be
processed per week
Attached:
draft versions of washing and final inspection procedures

## Slide 4: Main principles of Washing procedure
Foot and Side boards with tooth strips :
Wait for full glue curing before handling
Wash with detergent and demineralized water
Bake at 100o Celsius for 160 minutes
Pack in dry environment and leave at room temperature for 24h before using
Exact procedure to be approved by Technical Board,