## Slide 1
Experiments with Electron Cooling and Space Charge
Nilanjan Banerjee, MaryKate Duncan, John Brandt, Young-Kee Kim, Sergei Kladov, Sergei Nagaitsev, Giulio Stancari

## Slide 2: Overview
Motivation and Conceptual Design
Beam Experiments using Electron Cooling
Hardware Configuration and Status

## Slide 3
Motivation and Conceptual Design

## Slide 4: Maximizing Brightness and Intensity in ACE and Beyond
The proton program in IOTA was proposed for research into multi-megawatt hadron rings. Our research program addresses the four grand challenges of accelerator and beam physics facing the community:
Beam Quality: Space-charge, cooling
Beam Intensity: NIO, Landau damping
Beam Control
Beam Prediction
R. Ainsworth et al., Report from the Fermilab
Proton Intensity Upgrade Central Design Group, 2023.
Possible booster upgrade with RCS: @ 2 GeV injection.
R. Ainsworth et al., An Upgrade Path for the Fermilab Accelerator Complex, 2022.
Derisk new booster design by finding methods to maximize beam intensity and quality for a range of beam storage times.
J. Blazey et al, Accelerator and Beam Physics Roadmap, DOE Accelerator Beam Physics Roadmap Workshop, 2022

## Slide 5: Enhancing Beam Quality
Realize a super-periodic lattice
Allocate more space for the tune footprint.
Compensate for space charge forces
Minimize tune footprint due to space charge. Tune-shift compensation per lens is limited. Gaussian or McMillan?
Electron cooling
Cool hadrons via thermal energy exchange with co-propagating electron beam. Constrained by space-charge.
How to maximize phase-space density of stored beam and minimize beam loss in a ring for given number of turns?
Pulsed e-lens with flat transverse profile.
A. Oeftiger and O. Boine-Frankenheim, arXiv:2310.02365, 2023.
S. Nagaitsev et al., JINST 16 P03047, 2021.
McMillan e-lens
Beam intensity
Beam density
S. Nagaitsev et al., Proceedings Particle Accelerator Conference, 1995, pp. 2937-2939

## Slide 6: The Proton Program at IOTA
IOTA will be configured to recirculate 2.5 MeV protons up to .
Features:
All (skew) quadrupoles, correctors and sextupoles are independently controlled.
Rf cavity for adiabatic capture.
Single-turn injection.
Electron lens/cooler of length 0.7 m.
2.4 - 2.6 | 3 - 7 | 1 - 3 | 7
2.4 - 2.6 | 3 - 7 | 1 - 3 | 7

## Slide 7: Emittance Growth and Beam Loss
The primary sources of emittance growth and beam loss are:
Residual Gas Scattering
  Single scattering events lead to a finite lifetime. 10 mins @ 4.2 x 10-8 Torr measured in atomic hydrogen equivalents.
  Multiple scattering events lead to emittance growth independent of intensity.
  Baking can reduce residual pressure and increase lifetime.
Intra-Beam Scattering
Space-charge driven diffusion
  Functions of bare lattice and phase-space distribution.
No aperture restrictions
Beam Lifetime
Electron cooling can allow us to compensate for emittance growth and enforce equilibrium.
Emittance Growth

## Slide 8: Electron Cooler Design Parameters
Electron beam parameters aim to provide a cooling time of ~ 1 - 10 seconds to control equilibrium emittance at different bunch charges.
We estimated the cooling time using the Parkhomchuk model assuming:
Flat transverse distribution of the electron beam.
Ideal solenoid field.
Matched proton beam.
For the baseline design we chose two electron coolers with an order of magnitude difference in cooling time.
(mm) | (mA) | (A/m2) | (s)
18 | 80 | 78.6 | 0.79, 0.74, 0.94
14 | 1.7 | 2.76 | 12, 12, 13
18 | 80 | 78.6 | 0.79, 0.74, 0.94
14 | 1.7 | 2.76 | 12, 12, 13

## Slide 9: Simulations in PyORBIT with Space Charge and Cooling
We simulate our experiments using a transverse PIC space-charge model and the Parkhomchuk model of cooling.
Cool the core of the beam.
Can’t cool large amplitude particles.
More beam loss in bunched beam.

## Slide 10
Beam Experiments using Electron Cooling

## Slide 11: Optimization of Bare Lattice to Maximize Tune Shift
What is the maximum space-charge tune shift of stored beam we can achieve?
Optimizing the linear lattice configuration, including tunes and transverse coupling.
Increasing periodicity of the lattice.
Compensating for specific resonance driving terms using sextupoles and octupoles.
Simulated tune scans over 25 synchrotron periods for a Gaussian bunched beam with
F. Asvesta et al., in Proc. IPAC'22, pp. 2056-2059, 2022.

## Slide 12: Interplay of Space Charge and Coherent Instabilities
The 2.5 MeV protons at IOTA provide strong space-charge but weak impedance.
Measure instability growth rate and head-tail amplification in the parameter space using:
Controlled wakefields generated using the wake-building feedback system.
Electron cooling to enforce an equilibrium phase-space distribution, independent of bunch charge.
Wakefield
Amplitude (Waker)
SC Tune Shift (Electron Cooling)
ABS: A. Burov, Phys. Rev. Accel. Beams 22, 034202, 2019.
CMM: X. Buffat et al., Phys. Rev. Accel. Beams 24, 060101, 2021.
ABS
CMM Gaussian
Time (ns)
Time (ns)
Fermilab Recycler
R. Ainsworth et al., in Proc. HB'21, pp. 135-139, 2021.
O. Mohsen et al., in Proc. NAPAC'22, pp. 124-127, 2022.

## Slide 13: Tunable Landau Damping with Space Charge
Demonstrate integrable optics and Landau damping.
Danilov-Nagaitsev magnets
Octupole string
Electron cooling enables:
Single particle dynamics experiments with pencil beam and low energy spread.
Measurement of minimum tune spread required to mitigate coherent instabilities with space-charge.
A. Valishev et al., in Proc. IPAC’21, pp. 19-24, 2021.
N. Kuklev et al., in Proc. IPAC'21, pp. 1964-1967, 2021.
V. Danilov and S. Nagaitsev, Phys. Rev. ST Accel. Beams 13, 084002, 2010.
Stability Diagram: S. Antipov et. al., Phys. Rev. Lett. 126, 164801, 2021.
Instability Parameter Space
Experimental data showing decoherence due to chromatic tune spread in electron bunches.
J. Wieland, personal communication.

## Slide 14: Other Experiments
Interplay of NIO, space-charge and electron cooling
  Integrability is broken in the presence of non-linear space-charge. Practical implications?
Electron lens which also works as a cooler.
  Electron lens provide favorable scaling of detuning compared to electromagnets. Can it also work as a cooler to increase brightness?
Semi-hollow distributions for electron cooling
  Should help in cooling protons with large betatron amplitude. Limited experimental data available.
Increasing magnetic field, increases optimal current density.
Cooling rate vs electron current density
Tune diffusion in DN focusing channel with intense SC
C. Mitchell et al., JINST 15 P07019, 2020.

## Slide 15
Hardware Configuration and Status

## Slide 16: Electron Cooling in 2025

## Slide 17: Electron Lens Setup
Conceptual design of most parts exist but engineering design needs to be finalized.
G. Stancari et al, JINST 16 P05002, 2021
Electron Tracking
D. Noll and G. Stancari, Technical Memo, Fermilab, 2015. FERMILAB-TM-2598-AD-APC.
e- source
e- beam
Anode
Dispenser Cathode
Profiler
Flat beam gun
M. Bossard et al., in Proc. IPAC'23, pp. 646-649, 2023.
TEL-2 Collector
V. Shiltsev et al., Phys. Rev. ST Accel. Beams 11, 103501 , 2008.

## Slide 18: Magnetic Optics for Electron Beam
Consist of 5 solenoids and 4 toroids for bending. Gun and collector solenoids on hand. Major pending work:
Design of main solenoid
  (0.8 T, ): Superconducting or normal conducting with pancake coils?
Full tracking simulation with different profiles.
Effect of bending solenoids on proton orbit.
Conduction cooled SC solenoid
R.C. Dhuley et al 2021 JINST 16 T03009
Pancake coils in candidate design for new electron cooler in AD
A. Rossi et al., in Proc. COOL’23, Montreux, Switzerland, paper MOPPM1R3, 2023.
~3 times increase in !

## Slide 19: Electron Beam Diagnostics
Toroids: Measure beam current and losses.
Stripline BPMs: Align with the proton beam.
Profile measurement: Measure transverse profile.
Recombination Monitor: Optimize cooling performance.
Cyclotron Emission Monitor: Estimate electron density and temperature.
G. Stancari et al, JINST 16 P05002, 2021
Bz
Microwave photons
electrons
H0
H0
Bongho Kim et al., NIM A, 899, 22-27, 2018.
C. Habfast, PhD thesis, Karlsruhe U., KFK-4188, 1987.

## Slide 20: Conclusion
The IOTA 2.5 MeV proton program will study extreme beam conditions in future hadron synchrotrons and storage rings.
  Space-charge tune shift approaching -0.5. – Electron cooling and space-charge compensation.
  Adjustable wakefields of arbitrary shapes and magnitudes. – Wake-building feedback system.
We have proposed a few experiments which use electron cooling:
  Optimize bare lattice to maximize tune shift with given emittance growth and loss budget.
  Measure instability growth rate and head-tail amplification as a function of space-charge tune shift and synthetic ring impedance.
  Characterize single-particle dynamics of Non-linear Integrable Optics systems with very low chromatic tune spread and demonstrate suppression of coherent instability.
  Study NIO with intense space-charge.
Electron lens and cooling in late 2025.

## Slide 21: Appendix I: Lattices

## Slide 22: Appendix II: Space-charge simulations in multiple codes
XSuite
PyORBIT
Also, IMPACT-X, MAD_X