## Slide 1: Error Detection in Linacs with Machine Learning Techniques Jonathan Edelen, Kathryn Wolfinger, Matt Kilpatrick, Joshua Einstein-Curtis (RadiaSoft), Mike Wallbank, Dean Edstrom, Jonathan Jarvis (Fermilab)
March 14th 2024
FAST/IOTA Collaboration Meeting
Batavia IL, USA | radiasoft.net

## Slide 2: Outline
Machine learning methods
Initial demonstration at Jlab
Transitioning to FAST
Initial results
Conclusions

## Slide 3: Inverse models as a diagnostic tool
Inverse models as a diagnostic in a supervised fashion
  Direct comparison between predicted settings and actual settings informs operations of a potential anomaly
Inverse models as a diagnostic in an unsupervised fashion
  Assumptions
    model errors are caused by other beamline elements
    each beam-line element will have a unique error signature
Inverse models for tuning
  Minimize error between predicted settings and actual settings by varying quads
  Right: model error as a function of quad strength error

## Slide 4: Inverse Model Anomaly Detection at CEBAF
Data collected during two different operational modes.
  During normal operations
  During a dedicated machine study
Inverse model trained to predict settings from readings
  Left: Model prediction vs the ground truth for the validation data from the nominal setup
  Right: Model prediction vs the ground truth for the test data

## Slide 5: Establishing error thresholds
RMS error of the predicted settings by parameter for the machine study (left) and the nominal setup (right).

## Slide 6: A Smart Alarm System for the CEBAF Injector
Left: T-SNE was used to reduce the dataset dimensionality
  Operational data is shown in green and the study data in blue
  The model correctly flagged the study data as anomalous
  The T-SNE reduction of the data also provides a strong indication that these two datasets are distinct in nature
Right: Comparison with conventional threshold-based alarming.
  Threshold misses numerous configurations that would be undesirable by the user program

## Slide 7: Transition to the FAST LINAC
Objective(s):
  Near term: Develop model that can effectively detect anomalies in an explainable fashion → 60% complete
  Longer term: Utilize anomaly detection tools to assist in automatic tuning of the machine
Experimental plan:
  Collect data during “normal” operational conditions
  Train machine learning model on data archive
  Test machine learning on study data where parameters are intentionally varied
  Evaluate effectiveness at detecting anomalies
  Develop uncertainty metrics for machine learning model
  Deploy and test software during experimental run

## Slide 8: Transition to the FAST LINAC
Objective(s):
  Near term: Develop model that can effectively detect anomalies in an explainable fashion → 60% complete
  Longer term: Utilize anomaly detection tools to assist in automatic tuning of the machine
What actually happened:
  Collect data during “normal” operational conditions
  Train machine learning model on data archive
    Model learning not adequate
    Troubles with data alignment
    Identified potential logger issues

## Slide 9: Transition to the FAST LINAC
Objective(s):
  Near term: Develop model that can effectively detect anomalies in an explainable fashion → 60% complete
  Longer term: Utilize anomaly detection tools to assist in automatic tuning of the machine
What actually happened:
  Collect data during “normal” operational conditions
  Train machine learning model on data archive
    Model learning not adequate
    Troubles with data alignment
    Identified potential logger issues
  Collected study data for training
    Model learning not adequate

## Slide 10: Transition to the FAST LINAC
Objective(s):
  Near term: Develop model that can effectively detect anomalies in an explainable fashion → 60% complete
  Longer term: Utilize anomaly detection tools to assist in automatic tuning of the machine
What actually happened:
  Collect data during “normal” operational conditions
  Train machine learning model on data archive
    Model learning not adequate
    Troubles with data alignment
    Identified potential logger issues
  Collected study data for training
    Model learning not adequate
  Collected new study data for more training
    Model learning not adequate

## Slide 11: Transition to the FAST LINAC
Objective(s):
  Near term: Develop model that can effectively detect anomalies in an explainable fashion → 60% complete
  Longer term: Utilize anomaly detection tools to assist in automatic tuning of the machine
What actually happened:
  Collect data during “normal” operational conditions
  Train machine learning model on data archive
    Model learning not adequate
    Troubles with data alignment
    Identified potential logger issues
  Collected study data for training
    Model learning not adequate
  Collected new study data for more training
    Model learning not adequate
  Contemplate giving up
  Try to see if anomaly detection is possible even with a bad sub optimal model

## Slide 12: Transition to the FAST LINAC
Objective(s):
  Near term: Develop model that can effectively detect anomalies in an explainable fashion → 60% complete
  Longer term: Utilize anomaly detection tools to assist in automatic tuning of the machine
What actually happened:
  Collect data during “normal” operational conditions
  Train machine learning model on data archive
    Model learning not adequate
    Troubles with data alignment
    Identified potential logger issues
  Collected study data for training
    Model learning not adequate
  Collected new study data for more training
    Model learning not adequate
  Contemplate giving up
  Try to see if anomaly detection is possible even with a bad sub-optimal model
  Success! … sort of

## Slide 13: Identifying archiver issues
Time alignment efforts with archive data revealed inconsistencies
  Comparison of scripted data logging with archiver
  Study on 10-6 scanned trims and recorded BPMs for model development and testing

## Slide 14: Initial model training results
We trained a model on only the 10-06 study data. Then, we applied that model to the archiver data and study data. The following plots show the error of the model predictions.
  Note, we are considering an archiver timeframe on 10-06 when dedicated study data was collected and an archiver timeframe on 10-13 when no dedicated study was run.

## Slide 15: Understanding the training and testing data
Training data collected from the data logger between studies ~ Oct 13
Testing data collected from script during machine studies on Oct 6
Bar plots showing the median and interquartile range
  BPMs (bottom left): Correctors (bottom right)
T-sne dimensionality reduction
  Example-by-example (right top)
  Model parameters (right bottom)

## Slide 16: Initial machine learning studies
Model is trained on operations data and tested on study data
  Study was conducted on 6 October: Both scripted data collection and data logger collection

## Slide 17: Predicting the trim settings from the BPMs
Prediction errors for the horizontal trims
  For the min (left) and max (right) trim setting during the study

## Slide 18: Predicting the trim settings from the BPMs
Prediction errors for the vertical trims
  For the min (left) and max (right) trim setting during the study

## Slide 19: Identification of trim errors
Use algorithm to identify trim errors
  Model trained to predict trim settings from BPM readings
  Compute error between predicted trim setting and actual trim settings
  Large model offsets make threshold determination challenging
    The changed trim has a clear signature over non changed trims
    Subtract the mean error and then find the location with the max residual
  Compare with linear matrix model

## Slide 20: Identification of trim errors
Use algorithm to identify trim errors
  Model trained to predict trim settings from BPM readings
  Compute error between predicted trim setting and actual trim settings
  Large model offsets make threshold determination challenging
    The changed trim has a clear signature over non changed trims
    Subtract the mean error and then find the location with the max residual
  Compare with linear matrix model
Use model ensemble to improve prediction and provide error bars
  Plots show median prediction with plus minus one standard deviation

## Slide 21: Detailed error detection analysis / threshold evaluation
Evaluate model performance on all test data
  ROC curve (far right) shows true positive rate vs false positive rate for varying detection thresholds
Error detection for horizontal trim examples (left) and vertical trim examples (middle)
  Color coded by which trim is changed
  Model error in dashed line
  Anomaly flag in solid line showing that the BPM is correctly identified

## Slide 22: Next steps
Iterate on model learning
  Try to improve the predictions for baseline model: planned
Improve detection algorithm
  Extend to remaining BPMs on the LINAC: planned
  Expand ensemble to include linear and other models: planned
  Try Siamese networks for stronger error discrimination: in progress
Determine deployment path
  Experiment on proton source?
  Expand to include more diagnostics?

## Slide 23: Conclusions
Neural network model was able to detect changes in the machine in different operational modes
  Improvement over matrix model
  Training data collected during normal operations (no dedicated study required to train the model)
Need to better understand the data logger issues
Understand why the method works even with a poor (in my opinion) model

## Slide 24: Disclaimer
This report was prepared as an account of work sponsored by an agency of the United States Government. Neither the United States Government nor any agency thereof, nor any of their employees, makes any warranty, express or implied, or assumes any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, apparatus, product, or process disclosed, or represents that its use would not infringe privately owned rights. Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise does not necessarily constitute or imply its endorsement, recommendation, or favoring by the United States Government or any agency thereof. The views and opinions of authors expressed herein do not necessarily state or reflect those of the United States Government or any agency thereof.