## Slide 1
Geoff Savage
30 November 2023
ND-LAr DAQ/Computing Working Group
DAQ and Computing for
ArgonCube 2x2 Demonstrator

## Slide 2: News
Searching for a 2x2 Run Coordination meeting time
  Tuesdays at 10 am CT has been suggested
  Please fill out poll Luis setup
    https://www.when2meet.com/?22413663-UqmsR
Communication
  2x2 operations Slack channel in DUNE workspace - 2x2_operations
  Email lists
Next 2x2 DAQ/Computing meeting – Thurs 14 Dec 2023 @ 10 CT
  Geoff is on vacation week of Dec 11
Other 2x2 meetings continue
  2x2 Installation – Mondays at 11
  2x2 Electronics/Electrical – Thursdays at 2
    Special topic this week – UPS for module 2

## Slide 3: Cabling (not to scale)
catwalk
Minerva LI
Quiet power
copper from server 1 rack
Power Supply
Detector Power
12-port managed switch
Minerva Readout
Quiet power
no network devices
Cryo Rack
EPP power
Computer
UPS
Network
EPP power
48-port router
SFP+ ports
UPS
Light ADC
Detector Power
12-port managed switch
Purity Monitor
Detector Power
12-port managed switch
Server1
Quiet power
Minerva DAQ servers, gateways
48-port managed switch 1 Gb copper
Server2
Quiet power
AC2x2 DAQ servers
Cryostat
Platform Rack
Detector Power
48-port managed switch
Electrical Requirements:
Fiber separates grounds.
No copper between racks on different power.
MND 102
No Power
Trunk
Fiber
x10 for
light
Fibers from racks go
back to Network Rack.
Within each rack copper
from 12-port switch to
each device.
Server3
Quiet power
AC2x2 DAQ servers
x4 for
light
Light ADC has
independent network.
10Gb copper
1Gb copper
fiber
Key:

## Slide 4: Computing Installation Status
Brief rack summary – all racks remain powered up
  Network Rack – router on UPS
  Server1 rack – Minerva readout servers
  Server2 rack – 2x2 DAQ servers
  Server3 rack – slow controls, operations
Operating installation on new Linux servers expected next week
Still a few network items to complete
  Should be transparent to users
  Server1 rack - move connections on old switch to new switch
    We have done this before at other locations
    The two switches are next to each other
  Add switch in purity monitor rack once rack is in place
  Connections to Cryo rack
    Plan is to add the Minos private network on the cryo PC to support communication with RTD Raspberry Pi from Linux or from Cryo.
    Cryo PC also has the public network connection for logins and the cryo private network managed by the Cryo group

## Slide 5: Additional DAQ/Computing Efforts
Renzo setup temporary slow controls monitoring on acd-srv04
  influxdb
  grafana
  scripts
2x2 DUNE integration
  DUNEDAQ at 2x2 – Asher and Co.
  2x2 data formats – combine 2x2 data to process with DUNE code
  DUNE timing – Armin Karcher, Dave Cussans, Geoff
Resistive wall monitor
Minerva readout
2x2 run control
LArTF test stand
  Current Linux version (SLF7) end of life in June 2024
  Need newer servers to run next Linux version (AlmaLinux9)

## Slide 6: References
2x2 Computing Summary
  https://docs.dunescience.org/cgi-bin/sso/ShowDocument?docid=29368
  Presented at the 05 October DAQ/Comp Meeting
pORC for computing racks
  https://docs.dunescience.org/cgi-bin/sso/ShowDocument?docid=29419