## Slide 1: Quantum Entanglement, Teleportation, and Entanglement Swapping Systems Coexisting with Classical Communications
Notes: Hi Jordan Thomas, a graduate student working under my advisor Prem Kumar at northwestern university. This work is done with my collaborators at international center for advanced internet research, nucrypt LLC and Ciena corporation and I’ll be talking about our recent work on quantum teleportation systems coexisting with conventional classical telecommunications traffic in the same optical fibers.

## Slide 2
Quantum-Classical Coexistence for Scalable Quantum Network Deployment
CPCC
Quantum + classical
Dark fiber quantum communications
Classical communications
Quantum
communications
“Coexistence”
Quantum and classical communications sharing fibers
-Limits the number of available fiber links
-More costly to lease, maintain, or install quantum dedicated fibers
-Can operate in arbitrary fiber links
-Cost effective
- Resource efficient
Notes: The main motivation for this work is that scaling the deployment of quantum network technology, and an eventual quantum internet, will benefit from the ability for both quantum and classical communications to coexist in the same fiber infrastructure. This will help ease the availability of fiber links between quantum node locations and reduce costs of leasing and maintaining quantum dedicated fibers.
The main challenge, particularly in standard single mode fibers, is that having both weak quantum signals and strong classical signals in the same fibers is complicated by the fact that the strong classical signals can limit. This means that without careful engineering of the system, either classical system requirements are limited in their power, sacrificing for example classical data rates, or quantum signal fidelity is degraded.

## Slide 3
Center for Photonic Communication and Computing
McCormick School of Engineering and Applied Science
Main Limitation:
Spontaneous Raman Scattering Noise
CPCC
Quantum
(sub photon level)
Classical
(μW to 100’s of mW)
Quantum + noise
Fiber
Classical
pump
Simulated based off:
Hollenbeck, D. & Cantrell, C. D. J. Opt. Soc. Am. B/Vol. 19, (2002)
Stokes
Anti-stokes
Classical Pump
Broadband spectrum
  Can’t avoid noise entirely
Many local maxima and minima of various strength
  highly depends on quantum-classical detuning

## Slide 4
Center for Photonic Communication and Computing
McCormick School of Engineering and Applied Science
Main Raman Noise Reduction Strategies
CPCC
pump
Quantum = C-band
Classical = C-band
Quantum = C-band
Classical = L-band
Quantum = O-band
Classical = C-band
Quantum = C-band
Classical = O-band
O-band
C-band
L-band
~35 THz
Loss spectrum
1. Wavelength Assignment based on Raman noise spectrum
2. Narrow spectral-temporal filtering
Notes: Place quantum signals in the lowest gain regions of the Raman spectrum
Anti-stokes detuning from the classical signal wavelength
  However, must ensure both quantum and classical signals have low loss
Narrow spectral-temporal filtering around quantum signal modes to reject multi-mode uncorrelated spRS noise

## Slide 5
What are the Least Noisy Wavelengths for Telecom Quantum-Classical Signals
CPCC
Lowest noise O-band classical channels
Lowest noise O-band quantum channels
Fermi/Caltech/Argonne:
Quantum = C-, L-band
Classical = ?
Northwestern:
Quantum = O-band
Classical = ?

## Slide 6
Investigating WDM O-band Entanglement and High-Power WDM C-band Classical Communications
CPCC
11-channel C-band Classical Source
(1549 nm-1565 nm)
O-band Entangled Photon Source Spectrum
(1280 nm-1320 nm)
signal
idler
Coexistence
NU
Starlight
Raman noise count rates
Entangled two-photon interference visibility
Impact of noise on 16 different 50-GHz filtered O-band channels across 1280 nm-1320 nm with up to 18.1 dBm C-band power
Optimized channels clearly outperform others

## Slide 7
Center for Photonic Communication and Computing
Comparison to state-of-the-art
CPCC
- Multi-wavelength and entangled photon
- 18 dBm over 48 km installed fiber
- Found that 1310 nm is generally not best wavelength to choose
- Single channel/single photon 1310 nm QKD
- Coexistence over 66 km commercial backbone fiber
21 dBm of WDM C-band power/ Tbps classical rates
1310 single photon
(single λ)
Multi-channel
C-band classical
Multi-λ channel
entangled photons
Multi-channel
C-band classical

## Slide 8
Quantum State Teleportation and Classical Communications in the Same Fiber
CPCC
Coexistence has been demonstrated with single photons, entangled photons, and Bell state measurements between single photons: can teleportation, swapping, etc. be performed alongside classical communications?
Case study: Photon encoding initial qubit and one photon of an entangled pair are transmitted to a BSM node, classical signals bypass BSM node to transmit the full length

## Slide 9
O-band Teleportation and 400-Gbps C-band Classical Communications over 10.5 km
CPCC
Classical Tx/Rx at Starlight:
400 Gbps at 1547.32 nm
Ciena WaveLogic 5 Nano 400ZR
Quantum state transfer:
5.4 km+5.1 km = 10.5 km
Classical link distance:
48 km+10.5 km = 58.5 km
Evanston Northwestern lab
1290 nm photons coexist to BSM node
Photon Pair Generation:
1300
1310
1290

## Slide 10
McCormick School of Engineering and Applied Science
Results
CPCC
Teleportation fidelities of Bob’s qubit to Alice’s ideal state with P1547 nm = 11 dBm
Raman noise vs. launch power:
Using optimized wavelengths and narrowband filtering (~8 GHz), classical signal only adds
~100 counts per mW
Nonclassical limit (F > 66.7%)
SNSPD dark count level
~100 counts/s/mW
Notes: Next, we performed teleportation with the 400G signal transmitted with 11 dBm of power. Here is an example of a 4-fold coincidence fringe as we rotate Bob’s polarization setting for Alice transmitting the diagonal and anti-diagonal state. On the right we show the results of the measured teleported qubit fidelity to Alice’s ideal qubit via quantum state tomography. We obtain an average fidelity for an arbitrary qubit of 85.6 +/- 4% with 11 dBm of power, which is well above the nonclassical limit of 2/3.

## Slide 11
Center for Photonic Communication and Computing
McCormick School of Engineering and Applied Science
Newer results: 16 km, 18 dBm power
CPCC
Hong-Ou-Mandel interference between heralded single photon and entangled photon with 8 km/8km to BSM node
8 km
8 km
P400 Gbps = 18 dBm, 16 km
In progress: investigating longer distances, higher powers, modeling
Notes: Next, we performed teleportation with the 400G signal transmitted with 11 dBm of power. Here is an example of a 4-fold coincidence fringe as we rotate Bob’s polarization setting for Alice transmitting the diagonal and anti-diagonal state. On the right we show the results of the measured teleported qubit fidelity to Alice’s ideal qubit via quantum state tomography. We obtain an average fidelity for an arbitrary qubit of 85.6 +/- 4% with 11 dBm of power, which is well above the nonclassical limit of 2/3.

## Slide 12
Center for Photonic Communication and Computing
Entanglement Swapping Coexistence
CPCC
- With 4 photons transmitting 4 fibers, many possible experiments could be imagined
- Classical signals can co-propagate, counter-propagate, etc.
- Each could have different classical wavelengths
- Choice of fiber lengths in each arm will change how Raman impacts fidelity
Notes: In conclusion, we have shown that teleportation systems can coexist with high data rate high power classical signals. Due to the noise engineering, we saw little degradation of power up to 10’s of mW C-band power. We note that the fidelities could be improved via the same improvements in arbitrary teleportation systems.
We further note that since our system has 2 photon pair sources, changing Alice’s state to an entangled state would result in entanglement swapping, which due to the low noise levels it is reasonable to conclude we could have noise robust entanglement swapping.

## Slide 13
Key Parameters to Investigate
CPCC
- Choice of quantum-classical wavelengths
  -Fermi setup is restricted to ~1536 nm quantum signals
  - some wavelengths are more noise-optimized (C-band/O-band)
  - but all are worth studying (ex. C-band/C-band)
  Note: Noise in C-band will be unavoidably much higher than using O-band quantum signals
- How does performance scale as a function of fiber lengths and power?
-Raman will increase, quantum rates will decrease
- How does increased noise impact the optimal pair generation rates to achieve highest fidelity?
  -In dark fiber, optimal fidelities will occur at low pair generation rates due to multi-pair emission noise.
  -This is not generally true when background counts and transmission losses are increased due to reduced signal-to-noise
Notes: In conclusion, we have shown that teleportation systems can coexist with high data rate high power classical signals. Due to the noise engineering, we saw little degradation of power up to 10’s of mW C-band power. We note that the fidelities could be improved via the same improvements in arbitrary teleportation systems.
We further note that since our system has 2 photon pair sources, changing Alice’s state to an entangled state would result in entanglement swapping, which due to the low noise levels it is reasonable to conclude we could have noise robust entanglement swapping.

## Slide 14
Plans for Initial Experimental Tests
CPCC
- Add in wavelength division multiplexers into the system to MUX and DEMUX classical signals (need to ensure low additional loss)
- Start with continuous wave laser for classical source, eventually move to demonstrate “real” data (Capabilities can be extrapolated from tolerable power levels in CW case to guide design)
- Start by adding spools into different arms of the swapping setup one by one
- Two good experiments to run in the lab:
~2 km spool to emulate Fermi deployed fiber
~60 km to emulate Fermi-Argonne link
- Optimized or non-optimized wavelengths? Could impact MUX/DEMUX design
Notes: In conclusion, we have shown that teleportation systems can coexist with high data rate high power classical signals. Due to the noise engineering, we saw little degradation of power up to 10’s of mW C-band power. We note that the fidelities could be improved via the same improvements in arbitrary teleportation systems.
We further note that since our system has 2 photon pair sources, changing Alice’s state to an entangled state would result in entanglement swapping, which due to the low noise levels it is reasonable to conclude we could have noise robust entanglement swapping.