## Slide 1
Dave Capista
Main Injector Internal Readiness Review
10 January2024
Safety Assessment Document Updates for DOE O 420.2D
SAD Section III Chapter 07 – Main Injector

## Slide 2: Outline
Main Injector Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 3: Outline
Main Injector Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 4: Main Injector Overview
3319 meters in circumference
Both recycler (RR) and Main Injector (MI) are in this enclosure
RR is an 8 Gev machine
MI is an 8-120 Gev machine
One injection line from MI8 to both MI and RR
Three transfer lines from RR
  RR to MI line
  P1 line to Muon
  Abort line
Three extraction lines from MI
  P1 line to Switchyard
  NuMI extraction line
  Abort line

## Slide 5: Main Injector Overview
MI is the bottom machine. Magnets are electrical
RR is the top machine. Magnets are permanent made from magnetized ferrite.
Vacuum beam pipe in both machines is stainless steel 316L, 65 mils (~1/16”) wall Vacuum is around 5E-8 torr to prevent scattering of the beam
Beam Loss Monitors are located at every quadrupole location (red magnet)

## Slide 6: Main Injector Overview
Injection and extraction lines can create complicated work areas
  Requires more engineering and technical time to plan and execute
  Involves multiple groups to complete the task
    LOTO
    Safety

## Slide 7: Outline
Main Injector Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 8: Hazard Inventory for Main Injector
Accelerator specific hazards are purple
Hazards not discussed today are evaluated via the common Risk Matrix tables
  Covered in SAD Section I, Chapter 4
Hazards evaluated via risk assessment methodology per DOE-HDBK-1163-2020
  Likelihood (L):
    Anticipated (A), Unlikely (U), Extremely Unlikely (EU), Beyond Extremely Unlikely (BEU)
  Consequence (C):
    High (H), Moderate (M), Low (L), Negligible (N)
  Risk (R):
    I , II, III, IV (descending order of concern)

## Slide 9: Outline
Main Injector
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 10: Non-Accelerator Specific Hazards - Radiological
Residual Activation
  High intensity beam delivery can produce activated materials inside the Main Injector enclosure due to beam loss
  The residual dose rate found in the Main Injector from initial entry surveys is historically less than 5 mrem/hr, exceptions include:
    The injection and extraction areas
    The collimation areas
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Locked Gates: P – Key Control Program P – Radiological Work Permit P – Postings P – Training P – Beam Loss Monitoring M – Machine Protection System M – Local Component Shielding M – Run Conditions | L: BEU C: N R: IV

## Slide 11: Non-Accelerator Specific Hazards - Radiological
Radioactive Water (RAW) system
  The Main Injector Abort is cooled with water which becomes activated.
  The system is self contained and heat exchanged with the MI LCW system
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Locked Gates P – Key Control Program P – Radiological Work Permit P – Postings: P – Training: M – Volume Monitoring M – Engineered Containment | L: BEU C: N R: IV

## Slide 12: Non-Accelerator Specific Hazards - Radiological
Air Activation
  Air activation can occur at any area in the accelerator where high beam losses are present.
  These areas are typically limited to the collimation and abort areas.
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Air Monitoring M – Run Conditions P– Beam loss Monitoring M – Machine Protection System M – Engineered Air Flow | L: EU C: N R: IV

## Slide 13: Non-Accelerator Specific Hazards - Radiological
Soil Interactions
  Radionuclides are produced which may contaminate ground water
  Can occur in areas of high chronic losses
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Beam Loss Monitoring M – Machine Protection System M – Engineered Beam Dump M – Beamline Design M – Run Conditions | L: U C: N R: IV

## Slide 14: Non-Accelerator Specific Hazards - Radiological
Radioactive Waste
  Radioactive waste produced during Main Injector operations will be managed within the established Radiological Protection Program (RPP) as prescribed in the Fermilab Radiological Control Manual (FRCM)
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Locked Gates P – Key Control Program P – Postings M – Run Conditions M – Distance to Stored Material M – Material survey and release process | L:BEU C: N R: IV

## Slide 15: Non-Accelerator Specific Hazards - Radiological
Contamination, 7Be
  Contamination is found in the Main Injector enclosure in areas where beam loss has occurred, such as the collimation region.
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Locked Gates P – Key Control Program M – Radiological Work Permit M – Training | L: EU C: L R: IV

## Slide 16: Outline
Main Injector Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 17: Accelerator Specific Hazards - Radiological
Prompt Ionizing Radiation – Beam Loss
  Ionizing radiation due to beam loss in the Main Injector enclosure
  Analyzed maximum credible incident (MCI) to determine credited controls
  Hazard applies to onsite facility workers, onsite co-located workers

## Slide 18: Outline
Main Injector Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 19: Maximum Credible Incident (MCI) – Radiological
The MCI is defined as an event that is expected to occur over the lifetime of the accelerator
The MCI focuses on exposure to an onsite worker, an onsite coworker and the maximally exposed off-site individual (MOI)
Incident bounds all postulated accident scenarios for the Fermilab Main Injector
The Main Injector is located beyond the public access gate and contains no areas where the public is invited
Fermilab uses Credited Controls that flow down to the Accelerator Safety Envelope (ASE) to mitigate the consequences of an MCI to the following conditions:
  Less than 5 rem in one hour in any area accessible by facility workers or co-located workers
  Less than 500 mrem in one hour in all Laboratory areas to which the public is assumed to be excluded
  Less than 100 mrem in one hour at Fermilab’s site boundary and/or in any areas onsite in which the public is authorized (which includes Batavia Road, Prairie Path, parking lots open to the public, and general access areas including Wilson Hall, Ramsey Auditorium)

## Slide 20: Maximum Credible Incident (MCI) – Radiological
The MCI for the Fermilab Main Injector enclosure is a beam with an intensity of 2.83E17 protons per hour at an energy of 120 GeV persistently incident on a beamline component
Assuming no shielding or other controls are present this incident would result in a dose to any individual of approximately 5.23E7 rem (52 Mrem)
MCI intensity is the theoretical maximum the machine could produce and is a product of the following parameters:
  7E12 per Booster batch and 12 Booster batches to fill the Main Injector
    Booster intensity limitation
  1.067s repetition rate
    Hardware limit of the Main Injector power supplies
  Recycler and Main Injector transmission efficiency of 100%
  All beam stability limitations, machine integrity limitations, and machine protection systems are ignored
    Will be covered in Defense in Depth

## Slide 21: Outline
Main Injector Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Shielding Assessment Discussion
Summary of Defense in Depth Controls

## Slide 22: Credited Controls – Passive
Movable Shielding
  Concrete block wall separating the Main Injector enclosure are present in the P1 and decommissioned A1 line, between MI and F-sector. There are also shielding blocks at the MI30 area shielding the MI31 service building.
Penetration Shielding
  The MI enclosure has utility and RF penetrations throughout the service buildings that are filled with either sand, poly beads, and/or covered with poly blocks
  Sight risers used for survey and alignment of the accelerator are filled with steel plugs and poly beads

## Slide 23: Credited Controls – Passive
Permanent Shielding
  Topographical surveys of the Main Injector enclosure and berm conclude that there is a minimum of 21.6 Equivalent Feet of Dirt (e.f.d.) shielding between the interior surface of the enclosure walls and the surface of the berm
  Efficacy of passive shielding evaluated at MCI intensity at the location determined that a minimum of 20.7 e.f.d. is required to limit the dose received to an individual standing on top of the berm at the maximum dose point to 500 mrem in an hour.
Credited Control: 20.7 e.f.d. shielding between the interior surface of the enclosure walls and the surface of the berm

## Slide 24: Credited Controls – Active Engineering
Credited Control: Radiation Safety Interlock System (RSIS)
  Inhibits beam by controlled redundant critical devices
  Enforces the search and secure process
  Interlocked doors are present at all access points into the Main Injector enclosure
  The ES&H Radiation Physics Engineering Dept. (RPE) ensures that all requirements for hardware and system testing are completed semi-annually with a four-month grace period
  RPE also verifies the inventory of interlock keys and updates procedures for maintenance and testing of interlock systems
  All RSIS are designed, installed and configuration managed in conformance with the requirements of the Fermilab Radiological Control Manual (FRCM)

## Slide 25: Credited Controls - Administrative
Credited Control: Operation Authorization Document
  Machine Beam Permit
  Machine Run Condition
  Beam will not be transported through Recycler or Main Injector without approval of these documents
Credited Control: Staffing
  Ensures operations within bounding conditions specified in Operation Authorization Document
  The following staffing shall be in place during applicable beam operation:
    At least one member of the AD Operations Department who has achieved the rank of Operator II or higher shall be on duty and on site.
    At least one member of the AD Operations Department shall be present in the Main Control Room (MCR).
    Note: these requirements could be satisfied by a single person
Credited Control: Accelerator Operating Parameters
  The MCI intensity of 2.83E17 protons/hr shall not be exceeded

## Slide 26: Outline
Main Injector Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 27: Defense in Depth Controls
Permanent Shielding
  0.9 e.f.d. excess shielding is present on the MI berm
Training
  All personnel engaged in the commissioning, operation, and emergency management of the MI/RR shall have at a minimum, Fermilab’s Radiological Worker. Furthermore, personnel approved for access into the MI/RR interlocked enclosure shall have Fermilab’s Controlled Access training.
Procedures
  FESHM 2100 requires all departmental procedure to be reviewed, re-approved and re-taught every twelve months
Radiation Detectors
  Located in various service buildings where tunnel beam loss could expose a worker to a higher dose than an administrated limit

## Slide 28: Defense in Depth Controls
Machine Protection Controls
  Provides deep defense in depth
    significantly reduces the probability of an MCI
  Passive control
    Destruction of the accelerator components from high intensity beam
      Beam pipe is 0.065” stainless steel and will melt when exposed to 1MW particle beam. The vacuum will breach. The accelerator will be let up to atmosphere stopping the incident.
        Has occurred twice with a single lost pulse
        Has occurred twice in the abort area from repeated low intensity operation
    Is difficult to predict.

## Slide 29: Defense in Depth Controls
Machine Protection Controls
  Active Engineered controls
    Centered around the Beam Permit System
      Fail safe designed active link around the accelerator containing some 200 possible inputs
      Inputs are required to be active high
      When an input to this permit system transitions to a low state, the accelerator will abort the beam and inhibit further beam pulses until the fault is cleared and the system is reset
    Alarms and Limits
      Displayed in the MCR for operators. Some alarms require acknowledgement
    Orbit control and monitoring
      Semi-automated tuning to keep the beam at desired positions. Some critical beam positions are connected to the permit system
      Reduces beam loss, tunnel activation, and aids ALARA
    Low Conductivity Water (LCW) activation monitoring
      Protected by chipmunks at the enclosure stairwells
    Accelerator Time-Line generator
      Programmed timing for accelerator operations. Modules require approval prior to use

## Slide 30: Defense in Depth Controls
Machine Protection Controls:
  Active Engineered controls
    Beam Switch Sum Box
      Allows or prevents beam from the Linac based on requests from the TLG, Status of beam switches, and status of the beam permit system from all machines involved in the operation.
    Beam transfer Permit system
      Allows or inhibits beam transfers to accelerators. Beam present in an upstream machine will be sent to the Abort absorber
    Vacuum Interlock System
      Requires vacuum in the accelerator to be adequate to contain the beam. Will close vacuum valves and trip the permit system if the vacuum is poor.
    Power Supply Permits and Regulation
      Requires critical power supplies to be on with some monitored for regulation. Will trip the permit system if not at the desired configuration

## Slide 31: Defense in Depth Controls
Machine Protection Controls:
  Active Engineered controls
    Beam Loss Monitor System
      Provides information to operator's tor control of beam losses, aids in ALARA
      Used in conjunction with AI for pattern recognition to locate the source of a tuning problem or accelerator drift
      Allows for the prediction of tunnel activation for WPC
      Connected to the Beam Permit System
      Monitors integrated beam loss through a cycle and if above limit, will drop the beam permit after extraction
      Monitors instantaneous loss and if over the limit, will drop the beam permit immediately
      Limits the accident to a single pulse as opposed to the MCI of 3374 pulses
MCR Display of BLM around the Main Injector.

## Slide 32
Thank you for your attention

## Slide 33: Outline
Linac Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls
Backup Slide(s)