## Slide 1: Muon Collider Experiments Overview of detector requirements and limitations R. Lipton, Fermilab
Why contemplate a Muon Collider?
Because of the reduced bremsstrahlung muon rings can be made compact
  Lower cost
  Lower power consumption- 230 (MuC) vs 570 (CLIC) MW for 3 TeV
    20% increase for 6 TeV
  Fits on existing sites
Different cost scaling and lower power consumption mean that one can contemplate collider rings to 6 TeV
A Muon Collider is uniquely capable of producing Higgs bosons in the s channel with beam energy resolution comparable to it’s width

## Slide 2: A Vision
Possible staging:
Project X proton source
Stored Muon Neutrino factory
Higgs factory
High energy muon collider
Physics at each step
Requires a sustained effort

## Slide 3: The Standard Model Higgs
The SM Higgs:
  All properties are determined for a given mass.
  Any deviations signal new physics.
Theoretical questions:
  Couplings and width SM?
  Scalar self-coupling SM?
  Any additional scalars? EW doublets, triplets or singlets? (e.g. SUSY requires two Higgs doublets)
  Any invisible decay modes?
M(H) = 126 GeV
G(H) = 4.21 MeV
Branching Fractions
bb = 0.584 W+W- = 0.229
tt = 6.02 x10-2 Z0Z0 = 2.82 x 10-2
cc = 2.57 x10-2 gg = 6.81 x 10-2
ss = 2.57 x10-2 gg = 2.26 x 10-3
m+m- = 2.09 x 10-4 Z0g = 1.58 x 10-3

## Slide 4: Questions
Central Question:
Can we do precision physics in the high background environment of the Muon Collider?
Subsidiary questions
What detectors are needed?
What compromises must be made and what is the physics impact?
What new technologies must be developed?
Identify and study sensitivity to specific processes in the Muon Collider environment

## Slide 5: HE Collider Physics Environment
Narrow beam energy spread
  Precision scan
  Kinematic constraints
2 Detectors
DTbunch ~ 10 ms
  Lots of time for readout
  Most backgrounds don’t pile up
Multi-TeV lepton collider cross sections dominated by boson fusion
Beamstrahlung in any e+e- collider
E/E  2
(Han)
Ronald Lipton 8/11/2011
5

## Slide 6
Higgs Factory Environment
An S-channel Higgs factory is possible:
Coupling: (mm/me)2 = ~40,000
G(H)~4.2 MeV
DE(beam) ~ 3 – 5 MeV possible
Beam energy resolution could be comparable to the Higgs width
  Direct measurement of width
  Precise mass measurement
~300 meter circumference
  DTbunch ~ 500 ns
1000 turns (~0.8 ms)/store
Polarization, (g-2)/2 provide precise beam energy measurement
Raja, Tollestrup
PHYSICAL REVIEW D 58 013005
10-6
10-5
124.99
125.01

## Slide 7: Higgs Factory Rates
Overall rates
Luminosity estimates are in the 1031-1032 range
If we fold a 4.2 MeV Breit- Wigner with a 2.5 MeV Gaussian beam we get a on-peak cross section of ~46 pb
This gives us between 3,000 (5 MeV, 1031) and 46,000 (2.5 MeV, 1032) Higgs/year
The physics we can do depends strongly on machine parameters
Cross section
At scan point

## Slide 8: Higgs Factory vs High Energy Collider Requirements
The unique contributions of a MuC Higgs Factory include precise, model-independent measurements of width and mass. This requires:
Excellent machine energy resolution and stability
g-2 based measurement of energy
Z/g* background rejection (W/W* signal probably best)
A high energy machine would be used to measure new states (supersymmetric …). The requirements are similar to CLIC, MuC has lower beamstrahlung – more precise fits.
Precise, low mass tracking (mm→Zh)
Vertex Flavor tagging
Calorimetry capable of separating W/Z signals

## Slide 9: For Detectors - It’s All About the Background
Experiments at the Muon Collider will endure very harsh background environments. The first order of business in evaluating physics capabilities is to understand and simulate the machine backgrounds.
Muon beam decays:
  For 62.5-GeV muon beam of 2x1012, 5x106 dec/m per bunch crossing
  For 0.75-TeV muon beam of 2x1012, 4.28x105 dec/m per bunch crossing, or 1.28x1010 dec/m/s for 2 beams; 0.5 kW/m.
Full MARS simulation of 1.5 TeV machine backgrounds available
Higgs factory background work underway

## Slide 10: Detector Simulation
Work based on ILCROOT/LCSIM simulations
Both full and fast simulation available
  Mars backgrounds incorporated into full simulation
  A variety of detector options can be explored
Background only studies
  Full event simulation
    Study how cuts affect backgrounds
    Study parameterization of backgrounds
    Build background library
  Background characteristics
    Time and energy distributions

## Slide 11: Detector Models based on ILC concepts (SiD, ILD, 4Th)
LCSIM Detector Model
Full Simulation

## Slide 12: MARS 1.5 TeV Machine Detector Interface Model
W
Q = 10o 6 < z < 600 cm x:z = 1:17
BCH2
Q1

## Slide 13: Overall Background – 1.5 TeV
Non-ionizing background ~ 0.1 x LHC
But crossing interval 10ms/25 ns 400 x
Detectors must be rad hard
Dominated by neutrons – smaller radial dependence

## Slide 14: Much of the Background is Soft
And Out of Time
(Striganov)
g
m-
m+
e+/-
h0
h+-
g
m-
m+
e+/-
h0
h+-

## Slide 15: Attacking the Background
It is clear that timing and energy discrimination will be crucial in limiting the background in a Muon Collider
We have concentrated on understanding the time resolution required and how it may affect the detector mass and resolution for physics objects
The R&D is synergistic with CLIC, which requires ns level resolutions, LHC which is looking at fast timing for background reduction, and intensity frontier experiments, which may require 100’s of ps resolutions

## Slide 16: Track Timing Information
Tracking can benefit from precise timing, low occupancy in a pixelated silicon detector.
(Terentiev)

## Slide 17
Background Path length in silicon detector vs de/dx
Detector thickness
Angled tracks
MIP
Background Inside a silicon detector:
dE/dX
Path in detector

## Slide 18
Neutrons
electrons
Compton
High energy
conversions
soft
conversions
positrons
Time of energy deposit with respect to TOF from IP

## Slide 19: Effects of Cuts on Tracker Background
Timing is the most important
  Reduces backgrounds by 3 orders of magnitude
De/dx also is also important
  We need pulse height information anyway since our timing accuracy will depend on signal/noise and time walk corrections
Radius | DT Cut | DT & rphi & dedx
20 | 0.0012 | 0.0009
46.2 | 0.0008 | 0.0006
71.7 | 0.0011 | 0.0007
97.3 | 0.0006 | 0.0004
122.9 | 0.0009 | 0.0006
Background Hit rejection
de/dx
Background, no time cut
Tracker Layer 4
Background, 1ns time cut

## Slide 20: Timing In a Tracker
There is already an example of a fast timing IC design at CERN for CMS upgrades
Intent is to use fast timing to reject “loopers”
65 nm process
  Pixel ~ 1mm x 100 m x 200 m thick
  Peaking time: 6 ns
  220 e- ENC for 260 fF input capacitance
  Consumption for nominal bias: 65 uA
Jitter for 0.6fC Vth and 2.5fC signal; ~50 ps rms
Jitter for 1 fC signal; ~100 ps rms.
Time resolution defined by time walk (~3 ns)  without correction the resolution will be ~500 ps RMS
Time walk for signals 1 to 10 fC (0.6 fC threshold); <3 ns

## Slide 21: Vertex Detector
ILC inner radius ~1.5 cm set by beamstrahlung
MuC Inner radius ~5 cm set by EM background from cone
Preserve IP resolution by scaling by router/rinner
MuC vertex
ILC vertex
ILC Charged particle
Density vs radius
(Mazzacane)

## Slide 22: Tracking Strategy
Tracker segmentation very similar to CMS Phase 2 tracker (1mm x 100 m x 200 m)
Lots of space for time stamping circuitry
  Read out all hits within a ~10ns window
  Time stamp each hit to ~0.5 ns
  Pulse height to allow offline energy cuts and time walk corrections
Offline include time stamp in fit to allow for low momentum tracks, protons and kaons …
Need to demonstrate that this works in full simulation with MARS backgrounds.

## Slide 23: Time Development of Hadron Showers
(F. Simon CALICE)
The problem of hadron calorimetry at CLIC and a Muon Collider is interesting…
Hadron showers take time to develop – nuclear processes can take more than the ns time scale we would like for mC
How is resolution affected by integration time for various schemes?
  Dual readout
  PFA
  Pixelated
Depends on absorber material
Depends on sensor material

## Slide 24: Two approaches
Pixelated digital calorimeter with 2ns gate [R Raja 2012 JINST 7 P04010]
Dual readout calorimetry with fast timing
Software compensation
Based on nuclear int. vertices
Hadron shower time development

## Slide 25: Compensation by vertex counting (Raja)
Counting vertices in a highly pixelated calorimeter could compensate for missing energy due to nuclear breakup
Geant generator-based results

## Slide 26: Resolution of a pixelated calorimeter with vertex counting compensation

## Slide 27: Summary of Detector Requirements
Much of the HE collider physics is similar to e+e- (ILC, CLIC), low mass tracking, good calorimetery w/z discrimination
But with the additional challenges of:
  Radiation hardness
  Nanosecond (or better) time resolution
Requirements are relaxed for Higgs Factory if we aim primarily at measuring the width
  Use bb pairs (higher background)
  W*W has almost no physics background

## Slide 28: Conclusions
The Muon Collider is a “poster child” for a technically ambitious project with high risks and rewards.
The central themes are fast and radiation-hard
Low mass tracking and vertexing with ns resolution
  Cooling, power delivery, and support are central issues in making a low mass tracker
Fast, high resolution calorimetry
  Pixelated? Digital?
  PFA?
  Dual readout?
We need to understand the detector possibilities and tradeoffs to access the physics reach of a Muon Coliider.