## Slide 1
Evan Niner
Internal Readiness Review 1C
23 January 2024
Safety Assessment Document Updates for DOE O 420.2D
SAD Section IV Chapter 09 – Neutrino Switchyard 120 Experimental Areas

## Slide 2: Outline
Neutrino Switchyard 120 Experimental Area Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 3: Outline
Neutrino Switchyard 120 Experimental Areas Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 4: Neutrino Switchyard 120 Experimental Areas Overview
NM4 beam enclosure and service building
  120 GeV proton beam from Neutrino beamline (III-14)
  4.2 second slow spill extracted once every 55 seconds from Main Injector (same extraction as to Meson Experimental Area)
Currently occupied by E1039 SpinQuest experiment
  Many systems repurposed from previous SeaQuest experiment last operated in 2017
  Introduction of cryogenics platform and solid ammonia target
  Ready to begin beam operations following ARR

## Slide 5: Neutrino Switchyard 120 Experimental Areas Overview
The Neutrino Switchyard 120 Experimental Areas are managed by the Particle Physics Directorate (PPD). The SpinQuest experiment has an assigned Experiment Liaison Officer (ELO) to manage the NM4 facility and provide assistance and oversight to the experiment including coordination of lab resources. The ELO coordinates with the beamline physicist assigned from the External Beams Delivery Department in the Accelerator Directorate (AD) who maintains any AD owned systems, instrumentation, beamlines, and controls that are present in the experimental space.
Radiation safety has been carefully considered in the design of the Fermilab Neutrino Switchyard 120 Experimental Areas. All radiation hazards relating to beam operations safety are the responsibility of the Accelerator Directorate. The Accelerator Directorate, whose facilities includes all beamlines, their shielding, radiation, interlocks, beam surveys, monitors and impact of radiation on the environment, is addressed in SAD Section III Chapter 14 on the Neutrino Area.

## Slide 6: Neutrino Switchyard 120 Experimental Areas Overview
SpinQuest Spectrometer
  Repurposed from SeaQuest, lower level (below ground) of NM4 enclosure
  Beam going left to right
  FMag is a closed aperture solid iron magnet to focus muons downstream and absorb beam protons which do not interact with the target
  KMag is a large open aperture magnet to measure muon momenta

## Slide 7: Neutrino Switchyard 120 Experimental Areas Overview
Cryogenics platform
  New cryogenics plant installed on second (ground) level of NM4 enclosure to capture gaseous helium and reliquify
  The red shielding blocks are surrounding FMag and existing from SeaQuest. The grey shielding blocks are new to SpinQuest

## Slide 8: Neutrino Switchyard 120 Experimental Areas Overview
Target cave systems
  Cryostat cooled with liquid helium and insulated with liquid nitrogen and high vacuum
  Superconducting magnet, 1K evaporation fridge, NMR and microwave system, and solid-state polarized ammonia target
  Due to shielding target cave accessed via ladder from upstream NM3 enclosure
  Also shown are external liquid nitrogen dewar and gaseous helium tanks connected to cryo platform
  Guard rails installed in target cave not shown in this illustration

## Slide 9: Neutrino Switchyard 120 Experimental Areas Overview
SpinQuest experiment status
  *40 Engineering notes related to cryogenic systems reviewed and approved
    Cryogenics plant is operational and producing liquid helium
  *61 ORCs for all each of the detector subsystems reviewed and approved
    Experiment subsystems are operational and being commissioned without beam
    Final full-system beam ORC in process this week
  *42 standard operating procedures for cryogenics plant, experiment systems, ammonia reviewed and approved
    10 grams of ammonia currently onsite for handling practice and no-beam commissioning activities (more on next slide)
*See backup slides for lists

## Slide 10: Neutrino Switchyard 120 Experimental Areas Overview - Ammonia
Ammonia handling
  SpinQuest makes use of beads of polarized solid ammonia as target material
  Beads are loaded into target insert stick in NM4 hall
  Target insert then transported to NM3 target cave and lowered into cryostat
  All work done keeping ammonia submersed in liquid nitrogen
    Ammonia will sublimate above -77C
    remove it from liquid nitrogen for less then 20 seconds at a time
  At most 28.9 grams of ammonia in the target insert during operations
  Ammonia target loses is polarization properties after some exposure to beam resulting in the need to change targets ~weekly when running beam
  Exhausted targets stored and ultimately shipped back to University of Virginia for additional studies

## Slide 11: Neutrino Switchyard 120 Experimental Areas Overview - Ammonia
SpinQuest has been working with ESH team of SMEs in a weekly meeting led by Barb Hill for nearly a year to create, review and approve procedures for handling the ammonia and other aspects of operations
Several months of practice now filling the target insert and loading the insert into the cave using plastic (HDPE) beads
  Ammonia handles differently and the plastic beads cannot be used for all commissioning or physics measurements
Procedures for working with the ammonia filling the target insert and loading the insert in the cave have been approved in addition to shipping material to Fermilab and storing 10 grams of material in NM4. FSO provided final review.
  10 grams of material shipped to FNAL 12/13/23
  Training courses for SpinQuest target team
    SpinQuest Ammonia Target Handling [FN000761/RR/01]
    SpinQuest Ammonia Target Handling On the Job Training [FN000762/OJ/01]
  SpinQuest target team has been practicing the first step in the procedure handling ammonia in the back of NM4 prior to filling the target insert or loading the insert into the cryostat.
    Oversight from ESH and Industrial Hygiene for initial practice and air sampling
    Daily training log recording who is performing each task and lessons learned to adjust procedures
SpinQuest is taking this very slowly one step at a time

## Slide 12: Neutrino Switchyard 120 Experimental Areas Overview – Ammonia next steps
Remaining ARR work:
  Finalize procedure for a longer term storage solution for larger quantities of ammonia both before and after irradiation
    Explosion proof shed outside NM4
  Finalize plan with Radiation Safety and Hazard Control on shipping plans after beam exposure
    Reviewing activation calculations and shipping logistics, using RP form #47 for irradiated shipments
  Modify procedure to load target insert in/out of cryostat to include RCT coverage in beam conditions
Next commissioning steps
  First polarization of plastic (HDPE) beads on 1/21/24
  After another week or so of ammonia handling practice the 10 gram sample on hand will move into the target cryostat for initial commissioning (operating super conducting magnet, mircrowave, NMR systems for polarization studies) without beam, scaling up to 28.9 grams
Continue to work with ESH to adjust and improve procedures as SpinQuest learns from experience

## Slide 13: Outline
Neutrino Switchyard 120 Experimental Areas Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 14: Hazard Inventory for Neutrino Switchyard 120 Experimental Areas
Accelerator specific hazards are purple
Hazards not discussed today are evaluated via the common Risk Matrix tables
  Covered in SAD Section I, Chapter 4
Hazards evaluated via risk assessment methodology per DOE-HDBK-1163-2020
  Likelihood (L):
    Anticipated (A), Unlikely (U), Extremely Unlikely (EU), Beyond Extremely Unlikely (BEU)
  Consequence (C):
    High (H), Moderate (M), Low (L), Negligible (N)
  Risk (R):
    I , II, III, IV (descending order of concern)

## Slide 15: Outline
Neutrino Switchyard 120 Experimental Areas Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 16: Non-Accelerator Specific Hazards - Radiological
Residual Activation
  SpinQuest target station and front face of absorber magnet will activate
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – General and/or job specific RWP P – Use of LSM P – Radiological training P – Keyed entry M – Signage and decay time requirements | L: BEU C: M R: IV

## Slide 17: Non-Accelerator Specific Hazards - Radiological
RAW
  RAW water system in service of FMag
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: L R: III | P – Interlocked doors P – Key control P – Radiological training M – Design of water system | L: BEU C: N R: IV

## Slide 18: Non-Accelerator Specific Hazards - Radiological
Air Activation
  Air activation from scattered beam off target
  In SeaQuest operations 120 minute cool-off
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Interlock system preventing access to beam enclosure while beam is present. P – Air monitoring system P – Beam loss monitoring system P – Cool-off time M – Ventilation system design M – Run conditions | L: BEU C: L R: IV

## Slide 19: Non-Accelerator Specific Hazards - Radiological
Radioactive Waste
  Radioactive waste produced during Main Injector operations will be managed within the established Radiological Protection Program (RPP) as prescribed in the Fermilab Radiological Control Manual (FRCM)
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: L R: III | P – Radiological worker training P – Locked doors P - Key control program M – Any item in a beam enclosure during beam-on conditions is removed and surveyed by radiological workers and classified appropriately M – Any item identified for disposal is surveyed and processed by Radiological Control organization personnel in accordance with FRCM chapter 4 | L: BEU C: N R: IV

## Slide 20: Non-Accelerator Specific Hazards - Radiological
Contamination
  Contamination possible in the SpinQuest target cave area with beam going through air gap
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Locked gates P – Key control program P – Radiological training M – RCT coverage and/or job specific RWP M – Monitoring via contamination wipes | L:EU C: L R: IV

## Slide 21: Non-Accelerator Specific Hazards – Toxic Materials
Ammonia
  At most 28.9 grams of solid ammonia used as target material presents a toxicity hazard should its temperature rise above its melting point of -77°C
  An active ventilation system in NM3 target cave comprising a 1,800 CFM curtain fan blowing air into the target cave and a 5,000 SCFM explosion proof, ducted fan draws any ammonia away from the target cave and dilutes the gas in the NM3 enclosure
  Automatic activation of the ventilation system, warning lights and sounding of an audio alarm, occurs should either of two sensors located in the target cave detect ammonia concentrations above 25 ppm
  FIRUS alarm
  Key control to ensure only trained personnel present during a target changeout
  Ventilation system locked ON during target changeouts
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: M R: II | P – Standard Operating Procedures for handling P – Training M – PPE (dermal) M – Engineering control (room ventilation) | L: EU C: N R: IV

## Slide 22: Non-Accelerator Specific Hazards – Magnetic Fields
Fringe Fields
  KMag, FMag, target system magnet
  In supervised access power supplies are config controlled off for KMag and FMag
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
Exposure to fringe fields beyond allowable limits (worker with ferromagnetic or electronic medical device(s)) L: A C: H R: I Exposure to fringe fields beyond allowable limits (worker without ferromagnetic or electronic medical device(s)) L: A C: L R: III Exposure to flying metallic objects L: A C: M R: II | P- Industrial hygiene conducts field surveys to establish safe field boundaries for workers. P- Access control points and individual components of concern (e.g., experiment permanent magnet) have postings to notify workers of magnetic hazard. P – Facility specific hazard awareness training alerting to fringe fields P- Industrial hygiene conducts field surveys to establish safe field boundaries for workers. P- Access control points and individual components of concern (e.g., experiment permanent magnet) have postings to notify workers of magnetic hazard. P – Facility specific hazard awareness training alerting to fringe fields P- Brass tools are used to prevent flying metallic objects from occurring, thereby preventing worker injury as prescribed by relevant magnet SOP P-Work Control procedure/SOP (ferromagnetic object control) requires that all ferromagnetic objects are removed prior to entry into a fringe field area (30G administrative limit). P-Work Control procedure/SOP requires worker training while in areas possessing fringe fields (300 G administrative limit). | L: BEU C: H R: III L: BEU C: L R: IV L: BEU C: M R: IV

## Slide 23: Outline
Neutrino Switchyard 120 Experimental Areas Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 24: Accelerator Specific Hazards - Radiological
Prompt Ionizing Radiation – Beam Loss
  Ionizing radiation due to beam loss in the Neutrino Switchyard 120 Experimental Area spaces
  Analyzed maximum credible incident (MCI) to determine credited controls
  Hazard applies to onsite facility workers, onsite co-located workers
  Credited Controls are needed

## Slide 25: Accelerator Specific Hazards - ODH
Cryogenics
  NM4 cryogenics plant takes in liquid nitrogen and gaseous helium from external sources to produce liquid helium
  Liquid nitrogen from external dewar and liquid helium circulated from cryoplant into NM3 target cave cryostat for ammonia cooling and superconducting magnet operations
  NM3 target cave air ventilation system described with ammonia hazard. NM4 around cryo platform area has two 20,000 CFM fans for air mixing
  Both spaces are engineered ODH 0 areas
  Oxygen sensors and alarms present to trigger ventilation system in both the NM3 target cave and NM4 independently
  Credited Controls Required

## Slide 26: Outline
Neutrino Switchyard 120 Experimental Areas Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 27: Maximum Credible Incident (MCI) – Radiological
Although the experiments are installed in the Neutrino beamline areas, the experiments themselves do not affect the Maximum Credible Incident (MCI) as presented in Section III Chapter 14 for the Neutrino Area beamlines. The MCI for the experimental area is covered by the MCI analysis for the beamlines which pass through the experimental enclosures. The Neutrino area experiments do not require any additional credited controls.
New experiments for the Neutrino Switchyard 120 Experimental Areas are proposed through a Technical Scope of Work (TSW). If an experiment introduces new hazards or requires changes to beamline configuration or operations the USI screening process would evaluate any necessary changes to shielding assessments, the SAD chapter, or ASE for III-14 or IV-09.

## Slide 28: Outline
Neutrino Switchyard 120 Experimental Areas Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 29: Credited Controls – Radiological
All radiological credited controls are described in the Neutrino Area SAD chapter III-14 for the entire beamline including the experimental area.

## Slide 30: Credited Controls – Active Engineering
ODH Safety System
NM4 (Cryo platform)
  During personnel access into NM4, the following components of the Oxygen Deficiency Hazard (ODH) Safety System shall be in place, with no known loss of safety function, during personnel access into applicable areas:
    Two (2) area/fixed oxygen monitors (one high, one low)
    One (1) horn and one (1) strobe.
NM3 (Target Cave)
  During personnel access into NM3, the following components of the Oxygen Deficiency Hazard (ODH) Safety System shall be in place, with no known loss of safety function, during personnel access into applicable areas:
    Two (2) area/fixed oxygen monitors (one high, one low)
    One (1) horn and one (1) strobe.

## Slide 31: Outline
Neutrino Switchyard 120 Experimental Area Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 32: Defense in Depth Controls
Training
  Radiological worker and controlled access training
  Ammonia specific training
Administrative
  TSW and ORC process to review and approve experiment operations
Standard Operating Procedures
  Ammonia handling
  Cryo plant operations

## Slide 33: Summary
Neutrino Switchyard 120 Experimental Areas Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls

## Slide 34
Thank you for your attention

## Slide 35: Outline
Neutrino Switchyard 120 Experimental Areas Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Summary of Defense in Depth Controls
Backup Slide(s)

## Slide 36: SpinQuest Engineering Notes
EN03917 | (FNAL) LN2 outdoor dewar
EN04120-B | (FNAL) LN2 supply and vent lines Rev-B
EN04121 | (FNAL) QT-QT cool down line
EN04140 | (FNAL) gHe supply/return buffer tank to liquefaction plant
EN04630 | (FNAL) LCW cooling water system for cryo-plant & roots.
EN04678 | (QT) LHe dewar A, (250 liter)
EN04679 | (QT) LHe dewar B, (250 liter)
EN04748 | (QT) He purifier catalina cylinders (DOT cylinders)
EN04749 | (FNAL) Pneumatic air supply (supports QT system)
EN04752 | (FNAL) Pneumatic system receiver tank pressure vessel note
EN04753-A | (FNAL) gHe outdoor buffer tank (RD-1047) Rev-A
EN04755-A | (FNAL) gHe outdoor buffer tank (RD-1048) Rev-A
EN04772 | (QT) He recovery compressor
EN04773-A | (QT) He purifier dewar, Rev-A
EN04777 | (QT) LHe transfer line
EN04787 | (UVa) Target LN2 volume
EN04847-A | (FNAL) NM3 & Target Cave ODH Analysis Rev-A
EN04867 | (QT) Helium Liquefier, Low pressure gas
EN04894 | (FNAL) Beam pipe vacuum windows
EN04911-A | (QT) Purifier manifold, Rev-A
EN04935 | (QT) Dewar Pressure control line
EN05027 | (FNAL) NM4 ODH Analysis
EN05273-A | (UVa) Magnet Helium volume, Rev-A
EN05275 | (FNAL)Target Cave ODH system controls
EN05332 | (UVa) Target magnet gHe return line (Quench Line)
ED0016616 | (FNAL) Target cave ammonia spill mitigation
EN06273 | (UVa) Target Phase Separator vessel
EN06375 | (UVa) UVa Refrigerator Piping
EN07072 | (FNAL) E1039 NM4 ODH controls
EN07073 | (FNAL) E1039 NM4 ODH Calculations
EN07152 | (FNAL) Helium safety vent line
EN07172 | (UVa) Target fridge vessel
EN07252 | (UVa) Helium "U" tube
EN07455 | (UVa) Liquid Nitrogen delivery to target cryostat (in target cave)
EN07475 | (UVa) N2 vent pipe in target cave
EN09055 | (UVa) Cryofab portable dewar stinger & xfer line
EN09748 | (FNAL) Ammonia spill in NM4 (calculations)
EN10247 | (UVa) short gHe transfer line
ED0028948-B | (FNAL) Target insert jib crane and pulley, Rev B
EN11467 | (FNAL) Microwave water cooling system
EN06573 | KMAG LCW regulator
EN08675 | NS2 regulators in deionization loop
ED0013882 | (QT) Liquefaction System "What If" (V&I list)
ED0013883 | (QT/FNAL) Overall QT engineering document (from QT notes)
ED0030446 | NS2 cooling tower sprayers

## Slide 37: SpinQuest ORCs – Target/cryogenic systems
1834 | E1039 Microwave Test Stand
1837 | E1039 Target Lifter System
1837.01 | E1039 Target Lifter Addendum (re-installation)
1847 | E1039 Roots Vacuum
1847.03 | E1039 addendum to ORC-1847 for gHe recovery piping
1853 | E1039 Magnet Power Supply Rack
1854 | E1039 NMR system part 1 (custom electronics)
1857 | E1039 Liquefaction Electrical System
1857.01 | E1039 Liquefaction Electrical System
1865 | E1039 Target Lifter Control System
1866 | E1039 Target Lifter ADC System
1867 | E1039 AC power dist for slow controls rack
1877 | E1039 Target lifter monitor
1888 | E1039 NMR system part 2 (commercial components)
1888.01 | E1039 NMR addendum
1895 | E1039 Slow controls rack for the SpinQuest experiment
1933 | E1039 NMR rack quiet AC power
1934 | E1039 Microwave motor controlling system (exp. Hall)
1938 | E1039 Helium Liquefaction plant
1941 | E1039 ODH & Hazardous Gas Controls
1954 | Spinquest (E1039) Fridge valve controlling system
1968 | E1039 Microwave test setup at counting hall
1969 | E1039 Microwave setup in Hall
1969.01 | E1039 Microwave setup in Hall (reinstall)
1970 | E1039 Annealing system at Hall (slow controls rack)
1970.01 | E1039 Annealing system (Roots gate valve control box)
1982 | E1039 Magnet Power supply rack update
1982.01 | E1039 Helium level addendum to ORC-1982
1983 | E1039 Update Roots vacuum
1984 | E1039 VME based NMR system (LANL)
1984.01 | E1039 VME based NMR system Addendum (LANL)
2002 | E1039 LN2 delivery and gN2 vent piping
2008 | E1039 Liquid Helium transfer and cooldown piping
2046 | E1039 NM4 ODH Controls
2049 | E1039 Target Magnet (electronics)
2050 | E1039 Target Fridge (electronics)
2053 | E1039 Target cave Helium, nitrogen piping
2056 | Target Magnet (cooldown cryogenics/mechanical)
2056.01 | Target magnet (Fridge addendum)
2071 | Target Magnet Powerup
2137 | E1039 Target Gate Valve bypass valve control box
2162 | Polarized target insert (electronics & microwave)
2167 | 2nd Microwave control box (for test stand)
2171 | Heat Tape for target cryostat
2186 | NMR Test Stand
2199 | Outdoor gHe tank pressure/temp sensors & readout
2201 | Magnet gHe flow controller bypass control electronics
2209 | Temperature sensors for cryo-compressor water system
2213 | UVa NMR 3 channel box (test stand)

## Slide 38: SpinQuest ORCs - Spectrometer
1521 | Dark Photon Hodoscope
1522 | Proportional Tube Test Stand
1529 | Tiawan TDC (& test stand)
1530 | Chamber electronics
1550 | Hodoscopes
1574 | Chambers (St 3)
1594 | Trigger Supervisor
1628 | Chambers (St0, St 2)
1673 | Dark Photon Hodoscope
1673.01 | ACPower for DP Hodoscope Readout
2074 | Proportional Tubes
2089 | KMAG/FMAG Operation

## Slide 39: Procedures – Part 1
Procedure | Docdb ID
Cryogenics on the cryoplatform | 
QT Purifier LN2 fill | 10337
Warm Purifier LN2 fill | 10528
QT Liquefier Dewar level cleaning and Dewar cleaning | 10401
Dewar evacuation | 10178
UVA-QT Purifier Helium Space Cleaning Procedure | 10404
UVA-QT Purifier LN2 Space Cleaning Procedure | 10407
Helium boiloff capture procedure | 10282
LHe transfer using commercial LHe Dewar in the cave | 9670
Stinging/Unstinging QT transfer line to/from QT Dewars | 10624
Observation of a LHe jet through QT transfer line | 10395
Liquid helium transfer between QT dewars A and B | 10543
Liquid helium transfer between commercial dewar and QT dewars A/B | 10546
Liquid helium transfer from commercial dewar to target magnet w/ UVa xfer line | 10547
Liquid helium transfer between QT dewars A and B w/ UVa xfer line | 10550
Liquid helium transfer from commercial dewar to QT dewars A/B w/ UVa xfer line | 10553
QT System Non-Cryogenics | 
QT system startup and shutdown | 10364
HR3 Compressor Oil, Oil filter replacement | 10320
In-cave Cryogenics | 
Magnet LHe fill | 9670
Magnet shield LN2 fill | 10337
Fridge LHe fill | 10375
Magnet cooldown | 9651
LOTO procedure for fast magnet cooldown | 10571
Magnet operations | 10062
Magnet fill from commercial LHe Dewar | 10056

## Slide 40: Procedures – Part 2
Procedure | Docdb ID
Procedures related to gases | 
Pumping and purging (generic) | 10184
Leak checking (generic) | 10188
Outside gHe tank refill | 10198
Manually vented He Gas Storage Tank to the Atmosphere | 10285
Load gHe bottle into the system | 10525
Cleaning outside gHe tank using the UVA-QT purifier | 10523
Turning ON/OFF procedures | 
UVA-NMR system shutdown,startup,tuning, data-taking | 10367
Target Slow Control System turn on/off | 10369
Annealing System turning on/off | 10372
Microwave system powering up, Operation, and shutting down | 10387
Target lifter system powering up and shutting down procedure | 10381
HDPE Target Material Handling Related (Include Cryogenics) | 
Handling Target material CH2/CD2 (HDPE) | 10411
Filling the portable handheld dewar | 10358
Target material dewar filling from the portable handheld dewar | 10427
Target insert loading/unloading procedure (magnet cryostat) | 10355
Target material shipping procedure | 10498
NH3/ND3 Target Material Handling (Include Cryogenics) | 
Handling Target material NH3/ND3 | 10360
SpinQuest Target Pre-Irradiation Target Material storage 10g | 10696

## Slide 41: ODH Layout – NM3 Target Cave

## Slide 42: ODH Layout – NM4