## Slide 1
Michael K. Olander
Switchyard Accelerator Readiness Review
19-21 March 2024
Safety Assessment Document Updates for DOE O 420.2D
SAD Section III Chapter 13 – Meson

## Slide 2: Outline
Meson Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Pre-start Action Items

## Slide 3: Outline
Meson Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Pre-start Action Items

## Slide 4: Meson Overview
One extraction line from Switchyard
  120 GeV
  Referred to as “Meson Primary” (MPrimary)
Two transfer lines
  Energy can vary
  Meson Test (MTest)
  Meson Center (MCenter)
MTest and MCenter can be independently dumped in the Meson Target Train (MTT), allowing independent access to the experimental halls

## Slide 5: Meson Overview
Beam is split in Switchyard, but follows a common beam pipe into M01
In M01, beam is directed to MTest, MCenter, or the Meson Target Train
M01 through MTT is MPrimary
There are primary targets along MTest, allowing for a variety of secondary energies.
There is a single primary target in MC6
There is no target in the Meson Target Train – the name is historic
MTest
MCenter
Meson Target Train
MPrimary

## Slide 6: Outline
Meson Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Pre-start Action Items

## Slide 7: Hazard Inventory for Meson
Accelerator specific hazards are purple
Hazards not discussed today are evaluated via the common Risk Matrix tables
  Covered in SAD Section I, Chapter 4
Hazards evaluated via risk assessment methodology per DOE-HDBK-1163-2020
  Likelihood (L):
    Anticipated (A), Unlikely (U), Extremely Unlikely (EU), Beyond Extremely Unlikely (BEU)
  Consequence (C):
    High (H), Moderate (M), Low (L), Negligible (N)
  Risk (R):
    I , II, III, IV (descending order of concern)
Radiological |  | Toxic Materials | 
☒ | Prompt Ionizing Radiation | ☒ | Lead Shielding
☒ | Residual Activation | ☒ | Beryllium
☒ | Groundwater Activation | ☐ | Fluorinert & Its Byproducts
☒ | Surface Water Activation | ☐ | Liquid Scintillator Oil
☒ | Radioactive Water (RAW) Systems | ☐ | Pseudocumene
☒ | Air Activation | ☐ | Ammonia
☐ | Closed Loop Air Cooling | ☐ | Nanoparticle Exposures
☒ | Soil Interactions | Flammables and Combustibles | 
☒ | Radioactive Waste | ☒ | Combustible Materials (e.g., cables, wood cribbing, etc.)
☒ | Contamination | ☐ | Flammable Materials (e.g., flammable gas, cleaning materials, etc.)
☒ | Beryllium-7 | Electrical Energy | 
☒ | Radioactive Sources | ☒ | Stored Energy Exposure
☐ | Nuclear Material | ☒ | High Voltage Exposure
☐ | Radiation Generating Devices (RGDs) | ☒ | Low Voltage, High Current Exposure
☐ | Non-Ionizing Radiation Hazards | Kinetic Energy | 
Thermal Energy |  | ☒ | Power Tools
☐ | Magnet Bakeouts | ☒ | Pumps and Motors
☒ | Hot Work | ☒ | Motion Tables
☒ | Cryogenics | ☐ | Mobile Shielding
Potential Energy |  | Magnetic Fields | 
☒ | Crane Operations | ☒ | Fringe Fields
☒ | Compressed Gasses | Other Hazards | 
☒ | Vacuum/Pressure Vessels/Piping | ☒ | Confined Spaces
☒ | Vacuum Pumps | ☒ | Noise
☐ | Material Handling | ☐ | Silica
Access & Egress |  | ☒ | Ergonomics
☒ | Life Safety Egress | ☐ | Asbestos

## Slide 8: Outline
Meson Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls

## Slide 9: Non-Accelerator Specific Hazards

## Slide 10: Non-Accelerator Specific Hazards
The public is not invited into the Meson Area.

## Slide 11: Non-Accelerator Specific Hazards - Radiological
Residual Activation
  High intensity beam delivery can produce activated materials inside the Switchyard enclosures due to beam loss
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Radiological Work Permit P – Postings P – Training M – Run Conditions M – Local Component Shielding | L: BEU C: L R: IV

## Slide 12: Non-Accelerator Specific Hazards - Radiological
Radioactive Water System
  Applies to the Meson Target Train
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Postings P – Radiological Work Permit P – Training M – Run Conditions | L: BEU C: M R: IV

## Slide 13: Non-Accelerator Specific Hazards - Radiological
Air Activation
  Air activation can occur at any area where high beam losses are present.
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: N R: IV | P - Measured air release documented in 2003 Shielding Assessment for the Switchyard 120 Project indicated 0 Ci per year under similar beam condition. M – Engineered Air Flow M – Run Conditions | L: U C: N R: IV

## Slide 14: Non-Accelerator Specific Hazards - Radiological
Soil Interactions
  Radionuclides are produced which may contaminate ground water
  Can occur in areas of high chronic losses when the beam passes through a berm pipe
  Can occur around the Meson Target Train Dump
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Radiological Work Permit required for excavation M – Engineered Beam Dump M – Beamline Design M – Run Conditions | L: U C: N R: IV

## Slide 15: Non-Accelerator Specific Hazards - Radiological
Radioactive Waste
  Radioactive waste produced during Switchyard operations will be managed within the established Radiological Protection Program (RPP) as prescribed in the Fermilab Radiological Control Manual (FRCM)
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Locked Gates P – Key Control Program P – Postings M – Run Conditions M – Distance to Stored Material M – Material survey and release process | L:BEU C: N R: IV

## Slide 16: Non-Accelerator Specific Hazards - Radiological
Contamination
  Contamination is found in the Switchyard enclosures in areas where beam passes through an air gap, such as vacuum isolation at a septum.
  Hazard applies to onsite facility workers and onsite co-located workers
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Radiation Survey P – Posting M – Radiological Work Permit M – Training | L: EU C: L R: IV

## Slide 17: Non-Accelerator Specific Hazards - Other
Confined Space
  The Meson Area has several areas within the enclosures that are considered Confined Spaces due to a single point of egress.
    These areas are below grade.
  Hazard applies to onsite facility workers and onsite co-located workers.
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P: Confined Space training informs workers of hazard and process for working in the confined space. P: Work practice procedure requires use of an attendant, outside of the enclosure. P: “Permit Required Access” and “Reclassification” require ES&H approval on every access. M: Mechanical ventilation active, when required. | L: BEU C: M R: IV

## Slide 18: Outline
Meson Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Pre-start Action Items

## Slide 19: Accelerator Specific Hazards
Radiological – Prompt Ionizing Radiation
Ionizing radiation due to beam loss in the Meson enclosures
Analyzed maximum credible incident (MCI) to determine credited controls
Hazard applies to onsite facility workers, onsite co-located workers
Credited Controls are needed
Cryogenics – Oxygen Deficiency Hazards (ODH)
Cryogens are not used operationally in Meson
Cryogenic transfer lines pass through the Meson enclosures
Meson enclosures M02, M03, M04, and M05 are classified as ODH-1 areas
Credited Controls are needed

## Slide 20: Outline
Meson Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Pre-start Action Items

## Slide 21: Maximum Credible Incident (MCI) – Radiological
The MCI focuses on exposure to an onsite worker, an onsite coworker and the maximally exposed off-site individual (MOI).
Fermilab uses Credited Controls that flow down to the Accelerator Safety Envelope (ASE) to mitigate the consequences of an MCI to the following conditions:

## Slide 22: Maximum Credible Incident (MCI) – Radiological
120 GeV protons: 4.2E13 protons per cycle at 55 second cycle time, delivered from P3 line in Switchyard
The MTest and MCenter beamlines also transport secondary beam, that is, beam produced by the interaction of the 120 GeV protons with a target
  The configuration of the secondary line is controlled by a “mode controller”, which is a credited control
  Each secondary beamline is considered separately
  Each secondary beam assumes 120 GeV protons, 4.2E13 protons per cycle, and 55 second cycle time
  Each secondary beam is assumed to be in the mode which results in the greatest radiological impact

## Slide 23: Maximum Credible Incident (MCI) – Radiological
For the Meson Area primary beam the MCI is 2.8E15 protons per hour:
The most we can get from Switchyard
55 second cycle time
120 GeV protons
For MTest secondary beam, results in:
2.8E10 particles per hour
55 second cycle time
30 GeV particles
For MCenter secondary beam, results in:
1.3E12 particles per hour
55 second cycle time
90 GeV particles

## Slide 24: Outline
Meson Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Pre-start Action Items

## Slide 25: Credited Controls – Passive
Permanent Shielding
The required shielding will vary depending on whether the beam strikes a magnet, long pipe, or buried pipe. Where the permanent shielding is less than the required shielding, active engineered controls will be used.
Movable Shielding
The Meson Area has moveable shielding placed in the tunnel vehicle access entrances at M01, M02, M03, and M04, at the M04 and M05 crossovers, and along the sides and in between the MC7 and MC8 enclosures. The MC6 and MT6 enclosures are assembled from large concrete movable shielding blocks. These movable shield blocks are either posted to prohibit moving of these blocks without ESH approval or are additionally chained and locked with a Radiation Safety lock and an applicable padlock, where deemed necessary.
Penetration Shielding
The enclosures have utility penetrations throughout the service buildings and are accounted for in the Safety Assessment Document

## Slide 26: Credited Controls – Passive
Permanent Shielding:
  Meson Primary – 15.3 e.f.d. credited.
  Meson Center – 12.8 e.f.d. credited.

## Slide 27: Credited Controls – Passive
Permanent Shielding:
  Meson Test:
Longitudinal Location [ft] | Credited Shielding [e.f.d.]
4340 – 4605 | 14.5
4605 – 4710 | 14.5
4710 – 4716 | 14.5
4716 – 4889 | 14.5
4889 – 4989 | 14.5
4989 – 4995 | 9.9
4995 – 5043 | 15.0
5043 – 5164 | 11.6
5164 – 5590 | 3.0
5590 – 5618 | 3.0
Transverse Location [Station] | Credited Shielding [e.f.d.]
ME2 4375’ | 14.5
MC2 4480’ | 14.5
MC2 4540’ | 14.5
MC2 4550’ | 14.5
MC3 4775’ | 14.5
MC3 4973’ | 14.5
MC3 4985’ | 9.9
ME3 5003’ | 15.0
ME3 5005’ | 15.0
MC3 5025’ | 15.0
MC3 5065’ | 11.6
MC4 5297’ | 3.0
MC5 5520’ | 3.0

## Slide 28: Credited Controls – Passive
The existing radiation fencing surrounding the Meson Area berm is credited.
The existing radiation fencing north of the MC6 enclosure, spanning between the Meson Polarized and Meson West beamlines, is also credited.

## Slide 29: Credited Controls – Active Engineering
Credited Control: Radiation Safety Interlock System (RSIS)
  Inhibits beam by controlled redundant critical devices
  Enforces the search and secure process
  Interlocked doors are present at all access points into the Switchyard enclosures
  Includes interlocked radiation detectors which protect individuals by disabling beam should prompt radiation from operations cause exposure to exceed specific dose rates
  Includes interlocked mode chassis which ensures the beam line is correctly configured to transport secondary particles
  The ES&H Radiation Physics Engineering Dept. (RPE) ensures that all requirements for hardware and system testing are completed semi-annually with a four-month grace period
  RPE also verifies the inventory of interlock keys and updates procedures for maintenance and testing of interlock systems
  All RSIS are designed, installed and configuration managed in conformance with the requirements of the Fermilab Radiological Control Manual (FRCM)

## Slide 30: Credited Controls – Active Engineering
MTest Primary Logic Chassis ensures the beamline is configured for a particular mode of operation.

## Slide 31: Credited Controls – Active Engineering
MCenter Critical Device Controller includes a current window input, which prevents beam energy greater than 90GeV from being transmitted downstream.

## Slide 32: Credited Controls – Active Engineering
Interlocked Radiation Detectors
Detector Type | Location | Credited Control Limit (mrem/hour)
Chipmunk | MT3 Cryo Penetration | 95
Chipmunk | MDB MC6 US | 19.7
Chipmunk | MDB MC6 Mid | 28.2
Chipmunk | MDB MC6 DS | 28.2
Chipmunk | MC6 Catwalk | 4870
Chipmunk | MC7 Air Gap | 485

## Slide 33: Credited Controls – Active Engineering
ODH Safety System
During personnel access into Meson (M02, M03, M04, M05), the following components of the Oxygen Deficiency Hazard (ODH) Safety System shall be in place, with no known loss of safety function, during personnel access into applicable areas:
One (1) area/fixed oxygen monitor of four (4) available,
One (1) horn and one (1) strobe for each enclosure.

## Slide 34: Credited Controls - Administrative
Credited Control: Operation Authorization Document
  Meson Primary
    Meson Primary Beam Permit
    Meson Run Condition
    Beam will not be transported through Meson Primary without approval of these documents
  Meson Test
    Meson Test Beam Permit
    Meson Test Run Condition
    Beam will not be transported through Meson Test without approval of these documents
  Meson Center
    Meson Center Beam Permit
    Meson Center Run Condition
    Beam will not be transported through Meson Center without approval of these documents

## Slide 35: Credited Controls - Administrative
Credited Control: Staffing
  To ensure accelerator operations are disabled and initiate an immediate response in the event of a determined ASE violation.
  The following staffing shall be in place during applicable beam operation:
    At least one member of the AD Operations Department who has achieved the rank of Operator II or higher shall be on duty and on site.
    At least one member of the AD Operations Department shall be present in the Main Control Room (MCR).
    Note: these requirements could be satisfied by a single person
Credited Control: Accelerator Operating Parameters
  Primary proton beam delivery shall not exceed 2.75E15 protons per hour at 120 GeV

## Slide 36: Outline
Meson Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls
Pre-start Action Items

## Slide 37: Pre-start Action Items
A new Chipmunk is required for the MC7 enclosure, on the ceiling, between the upstream scraper and the tertiary target to protect against the MCI.
(Circle on drawing)

## Slide 38
Thank you for your attention

## Slide 39: Outline
Meson Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls