## Slide 1
Accelerator Readiness Review
19-21 March 2024
Safety Assessment Document Updates for DOE O 420.2D
SAD Section III Chapter 9 – P1 and P2 Beamlines

## Slide 2: Outline
P1 and P2 Beamlines Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls

## Slide 3: Outline
P1 and P2 Beamlines Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls

## Slide 4: P1 and P2 Beamlines Overview
The P1 and P2 Beamlines transport
  8 GeV beam from the Recycler to the Muon Campus (M1)
  120 GeV beam from the Main Injector to Switchyard (P3)
Recycler and MI beam merge into the P1 line occurs in the Main Injector segment

## Slide 5: Outline
P1 and P2 Beamlines Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls

## Slide 6: Hazard Inventory for P1 and P2 Beamlines
Accelerator specific hazards are purple
Hazards not discussed today are evaluated via the common Risk Matrix tables
  Covered in SAD Section I, Chapter 4
Hazards evaluated via risk assessment methodology per DOE-HDBK-1163-2020
  Likelihood (L):
    Anticipated (A), Unlikely (U), Extremely Unlikely (EU), Beyond Extremely Unlikely (BEU)
  Consequence (C):
    High (H), Moderate (M), Low (L), Negligible (N)
  Risk (R):
    I, II, III, IV (descending order of concern)
Radiological |  | Toxic Materials | 
☒ | Prompt Ionizing Radiation | ☒ | Lead
☒ | Residual Activation | ☐ | Beryllium
☒ | Groundwater Activation | ☐ | Fluorinert & Its Byproducts
☒ | Surface Water Activation | ☐ | Liquid Scintillator Oil
☐ | Radioactive Water (RAW) Systems | ☐ | Pseudocumene
☒ | Air Activation | ☐ | Ammonia
☐ | Closed Loop Air Cooling | ☐ | Nanoparticle Exposures
☒ | Soil Interactions | Flammables and Combustibles | 
☒ | Radioactive Waste | ☒ | Combustible Materials (e.g., cables, wood cribbing, etc.)
☒ | Contamination | ☒ | Flammable Materials (e.g., flammable gas, cleaning materials, etc.)
☒ | Beryllium-7 | Electrical Energy | 
☒ | Radioactive Sources | ☒ | Stored Energy Exposure
☐ | Nuclear Material | ☒ | High Voltage Exposure
☐ | Radiation Generating Devices (RGDs) | ☒ | Low Voltage, High Current Exposure
☐ | Non-Ionizing Radiation Hazards | Kinetic Energy | 
Thermal Energy |  | ☒ | Power Tools
☐ | Bakeouts | ☒ | Pumps and Motors
☒ | Hot Work | ☐ | Motion Tables
☐ | Cryogenics | ☐ | Mobile Shielding
Potential Energy |  | Magnetic Fields | 
☒ | Crane Operations | ☒ | Fringe Fields
☒ | Compressed Gasses | Other Hazards | 
☒ | Vacuum/Pressure Vessels/piping | ☒ | Confined Spaces
☒ | Vacuum Pumps | ☒ | Noise
☒ | Material Handling | ☒ | Silica
Access & Egress |  | ☒ | Ergonomics
☒ | Life Safety Egress | ☐ | Asbestos

## Slide 7: Risk Table summary

## Slide 8: Outline
P1 and P2 Beamlines Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls

## Slide 9: Non-Accelerator Specific Hazards - Radiological
Residual Activation
  High intensity beam delivery can produce activated materials inside the P1 and P2 Beamlines enclosures due to beam loss
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Radiological Work Permit P – Postings P – Training M – Run Conditions M – Local Component Shielding | L: BEU C: L R: IV

## Slide 10: Non-Accelerator Specific Hazards - Radiological
Air Activation
  Air activation can occur at any area where high beam losses are present.
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | M – Run Conditions M – Engineered Air Flow | L: A C: L R: III

## Slide 11: Non-Accelerator Specific Hazards - Radiological
Soil Interactions
  Scattered beam has the potential to activate soil at low levels calculated in the shielding assessment.
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: N R: IV | P – RWP for excavation M – Beamline Design M – Run Conditions | L: U C: N R: IV
Notes: Radiation sensing equipment is used to keep risk of soil interactions limited to the area of the inactive target station.

## Slide 12: Non-Accelerator Specific Hazards - Radiological
Radioactive Waste
  Radioactive waste produced during P1 and P2 Beamline operations will be managed within the established Radiological Protection Program (RPP) as prescribed in the Fermilab Radiological Control Manual (FRCM)
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Locked Gates P – Key Control Program P – Postings M – Run Conditions M – Distance to Stored Material M – Material survey and release process | L: BEU C: N R: IV

## Slide 13: Non-Accelerator Specific Hazards - Radiological
Contamination
  Contamination can be created when beam or beam loss strike dust or debris on or near the accelerator.
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Radiation Survey P – Posting M – Radiological Work Permit M – Training | L: EU C: L R: IV

## Slide 14: Non-Accelerator Specific Hazards - Radiological
Radioactive sources
  Radioactive Sources may be used in shutdown and maintenance activities
Baseline Qualitative Risk (without controls) | Controls Preventive (P)/Mitigative (M) | Residual Qualitative Risk (with controls)
L: A C: H R: I | P – Training P – Posting M – Storage Requirements M – “In-Use” Requirements | L: EU C: L R: IV

## Slide 15: Outline
P1 and P2 Beamlines Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls

## Slide 16: Accelerator Specific Hazards - Radiological
Prompt Ionizing Radiation
  Ionizing radiation due to beam loss in the P1 and P2 Beamlines
  Analyzed maximum credible incident (MCI) to determine credited controls

## Slide 17: Outline
P1 and P2 Beamlines Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls

## Slide 18: Maximum Credible Incident (MCI) – Radiological
8 GeV beam
  The maximum-credible beam at 8 GeV would result from a large orbit distortion in the Recycler that could be caused by one or more correction elements being energized incorrectly. If the orbit was distorted such that the first turn of beam injected into the Recycler was steered into the extraction channel of the Lambertson at MI-52, all the beam getting to the Recycler could be sent to the P1 and P2 Beamlines.
  3.78 E17 protons/h = 7 E12 protons/batch * 15 Hz
120 GeV beam
  Maximum number of batches for SY120 at Booster MCI intensity, limited to 55s cycle time using Repetition Rate Limiter
  2.75 E15 protons/h = 6 batches/cycle * 7 E12 protons/batch / 55 s
The 8 GeV MCI drives the shielding and radiation detector requirements

## Slide 19: Maximum Credible Incident (MCI) – Radiological

## Slide 20: Outline
P1 and P2 Beamlines Overview
Hazard Inventory
Non-Accelerator Specific Hazards
Accelerator Specific Hazards
Maximum Credible Incident (MCI) Discussion
Summary of Credited Controls

## Slide 21: Credited Controls – Passive Engineering
Permanent Shielding
  17.9 e.f.d. in all locations except in the 520-701 region (MI 8400-8475) where the loss is on a buried thick pipe, which requires 20.3 e.f.d.
Penetration Shielding
  F13 10” diameter cryo penetration must be filled with at least 16.8 feet of sand
  F13 6” diameter cryo penetration must be filled with at least 14.7 feet of sand
  F15 48” diameter cryo penetration must be filled to the top of the berm with sand
  No other penetrations are required to be filled
Obvious and Operating Barriers to Ensure Only Authorized Access
  To permit entry to only authorized individuals into the area where the General Site Basis applies surrounding the P1 and P2 Beamlines segment of the Fermilab Main Accelerator, Obvious and Operating Barriers shall be established at the following locations to permit only authorized access:
    Wilson Hall West, Wilson Hall East, Site 5

## Slide 22: Credited Controls – Active Engineering
Credited Control: Radiation Safety Interlock System (RSIS)
  Inhibits beam by controlled redundant critical devices
  Enforces the search and secure process
  Interlocked doors are present at all access points into the Switchyard enclosures
  Includes interlocked radiation detectors which protect individuals by disabling beam should prompt radiation from operations cause exposure to exceed specific dose rates
  Includes an interlocked repetition rate limiter which protect individuals by disabling beam if a magnet is energized longer than allowed in a fixed amount of time.
  The ES&H Radiation Physics Engineering Dept. (RPE) ensures that all requirements for hardware and system testing are completed semi-annually with a four-month grace period
  RPE also verifies the inventory of interlock keys and updates procedures for maintenance and testing of interlock systems
  All RSIS are designed, installed and configuration managed in conformance with the requirements of the Fermilab Radiological Control Manual (FRCM)

## Slide 23: Credited Controls – Active Engineering
Detector Type | Location | Credited Control Limit
Chipmunk | F15 Air Handler | 440 mrem/hour
Interlocked Radiation detectors
  The P1 and P2 Beamlines do not have enough shielding for the MCI at the F15 Air Handler location, so interlocked radiation detectors are required
  The credited control limits for these interlocked radiation detectors are sufficient to protect against the MCI
  We operate at levels below the MCI intensity.
  Limit levels are set by the Radiation Physics Operations Department (RPO) to satisfy occupancy requirements per 10 CFR Part 835
  For 120-GeV beam, an interlocked repetition rate limiter prevents more than one MI extraction per 55s by disabling beam if a magnet is energized longer than allowed in a fixed amount of time

## Slide 24: Repetition Rate Limiter

## Slide 25: Credited Controls - Administrative
Credited Control: Operation Authorization Document
  Machine Beam Permit
  Machine Run Condition
  Beam will not be transported through the P1 and P2 Beamlines without approval of these documents
Credited Control: Staffing
  To ensure accelerator operations are disabled and initiate an immediate response in the event of a determined ASE violation
  The following staffing shall be in place during applicable beam operation:
    At least one member of the AD Operations Department who has achieved the rank of Operator II or higher shall be on duty and on site.
    At least one member of the AD Operations Department shall be present in the Main Control Room (MCR).
    Note: these requirements could be satisfied by a single person
Credited Control: Accelerator Operating Parameters
  Beam shall not exceed 3.78 E17 protons per hour at 8 GeV beam energy
  Beam shall not exceed 2.75 E15 protons per hour at 120 GeV beam energy

## Slide 26
Questions?