## Slide 1: JLab ERL Test Bed Opportunities for HEP Technology Development and Physics Experiments
George R. Neil
Associate Director, Jefferson Laboratory
February 2013
Snowmass Workshop
Chicago IL

## Slide 2: Existing JLab High Intensity ERL
Typical operation:
E = 130 MeV
135 pC pulses @ 75 MHz
The first high current ERL
provides a high intensity,
cost-effective platform
for HEP-related studies
Highlighted activities:
Search for Dark Matter
Cooling Ring Studies
Fixed Target Options

## Slide 3: JLab FEL Accelerator Capabilities
 | Near Term Capability | Full Capability | Internal Target (Near Term)
 | external target | external target | internal target
E (MeV) | 80-320 | 80-610 | 80-165
Pmax (kW) | 100 | 300 | 1650
I (mA) | 0.31-1.25 | 0.5/3.75 | 10
fbunch (MHz) | 750/75 | 750/75 | 750/75
Qbunch (pC) | 1.67-0.4/16.7-4 | 5-0.67/50-6.7 | 13.5/135
etransverse (mm-mrad) | ~1/~3 | ~2/~5 | ~3/~10
elongitudinal (keV-psec) | ~5/~15 | ~10/~25 | ~15/~50
Polarization | No | Up to 600 mA | No
 | 750 MHz drive laser; single F100 | 12 GeV RF drive; three F100s | 12 GeV RF drive; three F100s

## Slide 4
Workshop to Explore Physics Opportunities with Intense, Polarized Electron Beams up to 300 MeV
March 14th -16th at MIT
http://web.mit.edu/lns/PEB_Workshop/
Plenary Session
Overview talk: dark photon physics Maxim Pospelov
Overview talk: parity violation physics Yury Kolomensky Overview talk: precision nucleon structure Carl Carlson
Overview talk: nuclear astrophysics Achim Schwenk JLab FEL Accelerator Complex David Douglas
Mainz/MESA Kurt Aulenbacher
BNL ERL development Ilan Ben-­‐Zvi
Polarized e-­‐source development Matt Poelker
Precision electron polarimetry Eugene Chudakov
Report on JLab‐MIT test in July 2012 Chris Tschalär
Parallel Sessions on dark photons, parity violation, precision nucleon structure, experiments with nuclei, and technology

## Slide 5
Workshop to Explore Physics Opportunities with Intense, Polarized Electron Beams up to 300 MeV
March 14th -16th, MIT, Cambridge, MA
http://web.mit.edu/lns/PEB_Workshop/
Qweak report and Technology Application at Lower Energies Mark Pitt
Calculation of γZ box graph Wally Melnitchouk
Comparison of γZ Structure Function Models Benjamin Rislow
Future weak charge measurements including Moeller design Kent Paschke
Charge Symmetry breaking effects Gerald Miller
The P2@MESA experiment at Mainz Dominik Becker
Back angle measurements using P2 Sebastian Baunack
Particle physics motivation Bill Marciano
Nuclear physics aspects Bill Donnelly
Mainz/MAMI Harald Merkel
HPS at JLab Stepan Stepanyan
APEX at JLab Philip Schuster
DarkLight Experiment Ray Cowan
DarkLight beam background measurements Jim Boyce
Dark photon search at MESA Matthias Molitor
The TREK/E36 Experiment at J-­‐PARC Michael Kohl
Relat. Dark Matter Sarah Andreas
Invisible Decays Yonatan Kahn
Measurement of the charge radius of the proton Mehdi Meziane
MUSE@PSI: muon vs. electron Ron Gilman
MAMI initial state radiation expt Miha Mihovilovic
Polarizabilities expt Rory Miskimen

## Slide 6
Workshop to Explore Physics Opportunities with Intense, Polarized Electron Beams up to 300 MeV
Polarizabilities theory nucleon Vladimir Pascalutsa)
Polarizabilities theory few body Harald Griesshammer
Overview talk on lattice QCD Will Detmold
Nuclear structure corrections to Lamb shift in muonic deuterium Mikhail Gorshteyn
Tests of chiral symmetry: theory Barry Holstein
Tests of chiral symmetry: experiment Aron Bernstein
160(γ,α)12C and 160(e,e’α)12C to access 12C(α,γ)16O Genya Tsentalovich
12C(α,γ)16O accessed using electrons and internal targets Narbe Kalantarians
160(γ,α)12C to access 12C(α,γ)16O Claudio Ugalde
Ideas for polarized electron scattering at the S-­‐DALINAC Joachim Enders
AT motivation and theory Andrei Afanasev
Potential AT measurements at Mainz David Balaguer Rios
AT and PREX, PREX-­‐II, CREX report Mark Dalton
Neutron skins and neutron stars Jorge Piekarewicz
Potential Rn and AT measurements at Mainz Concettina Sfienti
Test of nonlocality in quantum mechanics Jacek Ciborowski
Clean measurements of the nucleon axial-­‐vector
and magnetic free neutron form factors Alexandre Deur
High brightness Beam Diagnostics Ralph Fiorito)
Polarimeters at MAMI and MESA: Past and future Valery Tyukin
The polarimeter chain at MESA Kurt Aulenbacher
Polarimetry -­‐ Scaling with energy David Gaskell
Hydro Moeller development at Mainz Patricia Aguar-­‐Bartholomae
High Power Cryotargets and Modeling Silviu Covrig
Status of the MESA Injector Robert Heine
Report on Workshop on TPCs at high rate experiments

## Slide 7
LIPPS Search for Dark Matter
Courtesy J. Boyce
Light from the JLAB FEL was used to search for Dark Matter
Notes: 7

## Slide 8
LIPPS Search for Dark Matter - Results
Courtesy J. Boyce
JLAB search successfully excluded significant mixing regions in a modest 40 hour experimental run
Notes: 8

## Slide 9
Run Procedure:
Pump out system.
Close Shutter S2
Open Shutter S1
Send Laser (Green, or Red, or FEL) into chamber for time TL
Close Shutter 1.
Open Shutter 2 after TD
Open camera shutter.
Close camera shutter after Dt time.
Store camera image.
Repeat steps 2 – 9 for series of delay times TD.
Repeat steps for series of decreasing ND values and TD values.
LTB
PUMP
CCD
Dipole
Shutter S1
Shutter S2
ND 10
S1
open
TR
DT
S1
closed
S2
closed
S2
open
S2
closed
TR = image readout
(~6 seconds)
DT = image exposure
The chamber is exposed to laser light when S1 is open: TL
The afterglow is recorded when S2 is opened at a time TD after S1 is closed.
TL
TD
Proposed FEL Chameleon Search – set-up as follow-on to LIPPS
Window
Window
Courtesy J. Boyce

## Slide 10
DarkLight Feasibility Test
Courtesy R. Milner (MIT)
DarkLight Collaboration
Notes: 10

## Slide 11
DarkLight Feasibility Test
Goal
Simulate high-power ERL operation with an internal gas-jet target controlling power deposition from beam loss and impedance/wake effects from both beam core and halo components through a 10 cm long small aperture (6, 4, or 2 mm diameter)
i.e., put > 400 kW through a coffee stirrer!
Target
Chamber
Tube block
Stepper motor
Designed and constructed by MIT-Bates R&E Center in collaboration with JLab FEL staff
DarkLight Collaboration
Notes: 11

## Slide 12
Darklight Experiment
E-beam
Chamber
Viewer1 inserted
Viewer2
replaced
3F7 Quad
3F6 Quad
Also radiation detectors for background determination
DarkLight Collaboration
Notes: 12

## Slide 13: Cube and Diagnostics
DarkLight Collaboration

## Slide 14: Achievements
  Established low beam loss in transmission of CW high power sub-100 micron beam at 100 MeV by independently controlling betatron match of primary beam and halo.
  Measured beam interception as low as 3.2 PPM in 2 mm aperture while running 450 kW of beam power (100 MeV, 60 pC, 75 MHz) significantly exceeding DarkLight requirements
  Measured background radiation to establish anticipated ratio of signal to background levels and detector shielding requirements
  Performed 8 hour stability run delivering 120 C though 2 mm aperture
  Performed halo imaging and profile measurements using new camera with 105 dynamic range.
DarkLight Collaboration

## Slide 15
DarkLight Collaboration
Experiment under detailed planning
Modest experiment cost ($5M) and operating cost compared to typical HEP studies

## Slide 16: DarkLight transverse beam diagnostics
Area: 1 mm x 1 mm;
Best Gaussian: fit σx=50 μm; σy=52μm
50 cm upstream
50 cm downstream
center
10 μm diffraction limit on resolution
Separate measurement showed ability to image halo at 5 x 10-4 level
DarkLight Collaboration

## Slide 17
Four sorts of the unwanted beam (beam halo)
Fraction of the phase space distribution that is far away from the core (due to the beam dynamics)
Low charge due to not well attenuated Cathode Laser (ERLs) – but real bunches that have proper timing for acceleration
Due to the Cathode Laser but not properly timed (scattered and reflected light)
Field emission: Gun (can be DC or RF), Accelerator itself (can be accelerated in both directions)
High Dynamic Range Diagnostic Development is Essential
Evtushenko

## Slide 18: Combining algorithm; LDR image
Combining algorithm operates on lines of the images
The integration time is sufficient for normalization of two images
Averaging works as usual to improve SNR and DR (need stable beam)
Becomes non trivial to display LDR images
P. Evtushenko
funding by DOE BES under Young Investigator Program

## Slide 19: Measurements vs. Modeling at the level ~103
Measured in JLab FEL injector,
local intensity difference of the
core and “halo” is about 300.
(500 would measure as well)
10-bit frame grabber & a CCD
with 57 dB dynamic range
PARMELA simulations of the same setup with 3E5 particles:
X and Y phase spaces, beam profile and its projection show
the halo around the core of about 3E-3.
Even in idealized system (simulation) non-linear beam
dynamics can lead to formation of halo.
Evtushenko

## Slide 20: Linear vs. Log scale
The two pictures here show exactly the same data (beam profile - (x,y)) but in linear and log scale
Next step is to use such measurements for beam characterization, emittance and Twiss parameters measurements (add x’ and y’)
Ultimately we want to do tomographic measurements; for now just quad scan
For non-Gaussian beam RMS beam width is a tricky thing! It depends on how much of tails of the distribution function f(x) is taken in to account.
Evtushenko

## Slide 21: Quadrupole scan raw data
Level of interest (LOI)
more tails included
less tails included
Evtushenko

## Slide 22: Emittance and Twiss parameters
beta function(s)
alpha function(s)
RMS emittance
more tails included
less tails included
Evtushenko

## Slide 23: ERL Circulator Electron Cooler applications to high energy proton rings
ion bunch
electron bunch
circulator ring
Cooling section
solenoid
Fast kicker
Fast kicker
SRF Linac
dump
injector
e-bunches circulates 10 -100 times  reduction of current from an ERL by a same factor
Design Choices
Energy Recovery Linac (ERL)
Compact circulator ring
to meet design challenges
Large RF power (up to 81 MW)
Long gun lifetime (average current 1.5 A)
Required technologies
High bunch charge magnetized gun
High current ERL (55 MeV, 15 to 150 mA)
Ultra fast kicker
energy recovery
30 m
Solenoid (20 m)
SRF
injector
dumper
Optimization
eliminating a long return path
could double the cooling rate
Proposal: A technology demonstration
using JLab FEL facility
Edward Nissen’s
Notes: 23

## Slide 24
Extraction transport configured to exit at west end of building
    Delivers beam to open area
    Provides appropriate beam/lattice properties for tuning/control
Fixed Target Dedicated
Facility Configuration
2-pass,
up to 600 MeV
no energy recovery