## Slide 1: The CSU Advanced Beam laboratory (ABL)
Sandra Biedron

## Slide 2: ABL: Two Primary Focus Area
Accelerator Science and Technology
  Leads: Sandra Biedron and Stephen Milton
Lasers
  Jorge Rocca, Menoni, Mario Marconi
Main Concept
  Merge Accelerator Technologies with Laser Technologies to create new technologies with performance capabilities not possible with only one.

## Slide 3: The Advanced Beam Laboratory
CSU Board of Governors approved construction and expenditure of the money needed to build of the new building.
CSU President has chosen to move forward with the construction and has developed a funding plan.

## Slide 4: ABL Timeline
Accelerated Delivery
  Made possible by an existing construction contract to build what is called Engineering II.
  We are using the same Architect and General Contractor
Timeline (Abbreviated)
  12 November 2012 – Fence off construction yard
  19 November 2012 – Begin site preparation work
  February 2013 – Walls go up
  31 July 2013 – Building ready for move in

## Slide 5: ABL: Current Status
Footings and Slab Complete
Iron work going up

## Slide 6: ABL Basic Layout and Initial Capabilities
Laser Lab 1
Laser Lab 2
Accelerator Lab
Drive Laser Laboratory
Accelerator Control Room
100-150 Terawatt Ti:Sapphire laser system. Wavelength: 0.8 micrometers, Energy before compression: 13 Joules. Repetition rate: up to 5 Hz. Plans to scale to 0.5 Petawatt
1 J, 5 picosecond, 100 Hz repetition rate diode-pumped laser (100 W average power)
Wavelength: 1.03 micrometers. Highest repetition rate diode-pumped chirped-pulse-amplification laser in the world. Can be scaled in repetition rate and pulse energy, future parameters depend on funding.
6 MeV Photocathode Driven Electron Linac
L- Band (1.3 GHz)
Two Klystrons Available (One needed for PC Gun)
15 us pulse durations at 10 Hz
Up to 81.25 MHz pulse rates available

## Slide 7
High energy femtosecond Ti:Sapphire laser (> 100 TW, up to 5 Hz repetition rate)
Profs. Jorge Rocca, Carmen Menoni

## Slide 8
Energy Pre-compression= 13 J
Std div. = 1.5 %
High repetition rate Titanium-Sapphire laser

## Slide 9
Unique high power diode-pumped solid state lasers pump table-top soft x-ray lasers at 100 Hz repetition rate
Laser Diode Drivers
Soft X-Ray Plasma Amplifier
Solid State Ultrashort Pulse High Power Laser
Ag+19
13.9 nm laser
e
B. Reagan et al., Optics Letters, 37, 3624, ( 2012)

## Slide 10: Compact high power diode-pumped CPA laser generates 1 J , 5 ps, pulses at 100 Hz repetition rate
B. Reagan et al., Optics Letters, 37, 3624, ( 2012)
1 J, 5 ps, 100 Hz

## Slide 11
Laser Pumped SXRL λ= 8.8– 32.6 nm
Discharge Pumped SXRL λ=46.9 nm
100 nm lines
82 nm holes
Chemical spectroscopies
Microscopy
Microscopy
Nanomachining
Interferometry
Compact plasma-based soft x-ray lasers for application (J.J. Rocca, C.S Menoni. M. Marconi)
Plasma diagnostics
58 nm pillars
Nanopatterning
High pulse energy (µJ-mJ)
High monochromaticity (λ/Δλ < 10-4)
High peak spectral brightness

## Slide 12
Gain-saturated table-top SXRLs cover 8.8 nm - 47 nm wavelength region
Pr
Saturated
Seeded

D. Alessi et al. Phys. Rev X, 1, 021023, (2011)

## Slide 13: CSU Accelerator Laboratory
Donated by the Univ. of Twente
Donated by the Boeing Corp.

## Slide 14: Linac Performance Parameters
Linac Characteristics | 
Energy | 6 MeV
Number of Cells | 5 ½
RF Frequency | 1.3 GHz
Shunt Impedance | 50 MW/m
Q-Value | 18,000
Axial Electric Field | 
Cell no. 1 | 26 MV/m
Cell No. 2 | 14.4 MV/m
Cell No. 3 – 6 | 10.6 MV/m
Solenoid Field Strength | 1,200 G

## Slide 15: System Performance Parameters
Major System Parameters | 
Linac | 
Frequency | 1.3 GHz
Repetition Rate | 10 Hz
Mircopulse Rep. Rate | 81.25 MHz (max.)
Klystron | 
Type | TH 2022C (Thales)
Power | 20 MW
Modulator | 
Type | PFN
Pulse Duration | 15 msec
Undulator | 
Type | Hybrid: NdFeB
K | 1 (at 8 mm gap)
Period | 25 mm
Periods | 50

## Slide 16: Cathode Preparation Chamber
A Variety of Cathodes Can be Used
  Cathode preparation chamber
  Used in the past
    CeK2Sb, K3Sb, and Copper
    The choice is dependent on what the experiment demanded

## Slide 17: ABL Initial Capabilities/Explorations
Laser Laboratories: Initial and Historical Functions
  Soft x-ray lasers (driven by the optical lasers in previous slide) Wavelength range: 8.8 nm to 47 nm. Picosecond pulse duration. Pulse energy = 2-10 microjoule. Average power: up to 0.15 mW (world highest average power table top soft x-ray lasers)
  Side Note:
    These soft x-ray lasers are made possible by the generation of very uniform, high density plasmas.
  Ancillary Capabilities of Group
    Laser design and fabrication
    High power optics development and production
    Nano patterning

## Slide 18: ABL Initial Capabilities/Explorations
Accelerator Laboratories: Initial and Historical Functions
  Compact, High-power THz FEL
    Tunable between 200-800 microns
    About 1 MW peak power from 900 MW available peak beam power (6 MeV, 150 A peak current)
    Average: a few mW (81.25 MHz rep rate, 15 microsecond macropulse,25-ps micropulse)
  Specialized beam diagnostics
    Electro Optical Sampling System
    System intended for tests at JLab FEL
    If JLab not ready then we will test it at CSU
  Laser/Plasma/e- Beam Interaction Studies
    Continuation of an experiment started at University of Twente

## Slide 19: A Smattering of Current Projects
Soft X-ray compact laser development
High-Power THz FEL
Neural Network Control of Accelerators
X-band Technologies
High Power Optics Development
Nanopatterning
High Density Plasma Theory, Simulation, and Production
Electro-Optical Sampling Diagnostic for High-Power Beams
Photocathode studies
Laser/Plasma/e- Beam interactions
Compact source design and development
Study of LSC/CSR and the Microbunching Instability
Medical Applications of Accelerator System
Two-Beam Systems
FEL Harmonic Control
Blue indicates areas potentially relevant to HEP programs

## Slide 20: Other Intriguing Areas We Are Beginning to Pursue
Capillary Discharge
Electron Density Profile
Near Field
Far Field
The potential to use this technology for high-gradients is tremendous and CSU IS the world leader in this.

## Slide 21: Summary
The CSU Advanced Beam Laboratory
  The Coupling of
    Accelerator Expertise and Existing Accelerator System
      6 MeV photocathode linac system with state-of-the-art drive laser
    Laser/Plasma Expertise and Existing Laser, Plasma and Ancillary Systems/Areas
      Unique state-of-the-art laser systems
      Plasma Sources
      EUV/Soft x-ray Microscopy/Spectroscopy expertise
      Multilayer Optics expertise
Will be used for
  Basic beam (Laser, particle and combined beam) research and development
Purpose-Built Building
  Ready for move in 31 July 2012