## Slide 1: APEX – early background studies
Eric Church
APEX mtg
7-March-2024

## Slide 2: Motivation
We’d like to broaden physics scope – and do Low Energy Physics -- in a module 3
  ala APEX
    The expanded light coverage might offer this possibility
  But backgrounds need to be understood and controlled
    here we consider two particular bkgds
      Cavern gammas (from just one long wall, for now)
        From 238U/232Th chains in rock
      FRP vertical supports for Arapucas (from just the long walls, for now)
        These sit on the inside in the fiducial volume
    Yet to consider, say,
      Exterior neutrons and the Arapucas themselves, etc …

## Slide 3: Supernovae, solar ns
Supernovae burst detection is in the DUNE physics charge
solar ns are part of a new hoped-for program at lower energy for all modules and give a broad low-energy spectrum of events to show our capabilities, or lack thereof.
Thus, as a start, I generate 8B solar Marley events in our new APEX standalone geometry
Thanks, Franciole for the geometry!
    github.com:fcmarinho/module3_standalone_sim.git
  I have iterated to add an outer cryostat
  I take the DetectorConstruction.* files giving latest geometry as of a couple wks ago, and drop them into my sndwrm simulation
    sndwrm – simulation of a neutrino detector with radiopure materials)
    github.com:echurch/sndwrm/tree/liquid_deception

## Slide 4: 8B as a metric

## Slide 5: Primary 8B e-s
Anybody who understands
all these primary Marley e-s please explain
to me.
This is the max (first in stack) e- primary KE.

## Slide 6: Standalone simulation
For now I will just count Arapuca hits
  Impose pde=0.03
There’s no signal formation, just hits
  So, no noise yet whose signals could conceivably be counted as hits
No charge drift, no charge hits
No reconstruction
However, the upside is no photon lookup library is used in this work.
  All photons are tracked by G4
  It’s easy to change the geometry and re-run

## Slide 7: Typical external rock g events
green are optical photons
Looking down from above
Looking from the side

## Slide 8: Initial g spectra
From the rock
gs which produce photons that hit Arapucas

## Slide 9: x (horiz) optical photon origin
This is wrong/incomplete!
In fact, most photons that hit arapucas, come
from large abs(x) -- behind the Arapucas!
Discovered as putting this talk together this morning!
Big implication to count rate!

## Slide 10: x (horiz) optical photon origin
This one is correct! So, there may be a bug – and I am counting backside Arapuca hits, which is wrong and can be avoided and which I thought I had avoided.
OTH, some of these photons may be hitting Arapucas on other side and properly being counted.
Stay tuned.

## Slide 11: vertical bar events
x,z point of origin of optical photons
rhs zoomed
further zoomed

## Slide 12: FRP vertical bars
Fiber Reinforced Poly
I find a SCDMS assay in radiopurity.org of
  CFRP
    This is not what BNL is proposing to use, but for now
      Use: .8, 2.93, 8.21 mBq/kg: U, Th, K
      I suspect this is too low
  For now use the same Eg spectrum as for cavern gs, lhs pg 8
    And scale according to the sum
      11.9 mBq/kg

## Slide 13: Npe
Impose a 3% pde
From slide 5 and 208Th line this looks like about 3 MeV

## Slide 14: NhitArapucas

## Slide 15: Subsequent work
I would like to add neutrons
  Will produce capture gammas in LAr at ~6 MeV
  The cavern neutron rate will be 3-4 orders of magnitude reduced if we can put in water shielding outside the cryostat
    Or use borated foam in cryostat walls, e.g.
    This will also benefit the cavern gamma rate I showed today
  Cold cryostat wall neutrons can not be shielded.
Clearly, the gs shown here need better statistics
    Since the rate is very high the falling edge needs to be understood all the way down where it crosses into signal
    These rates would also be reduced by water shielding outside
  Are the CRPs in and do they have correct reflectivity?

## Slide 16: Eventually: Eres
Getting the Energy resolution in our standalone simulation(s) will take work
We need to add event-by-event the charge and light signals
Unlike in LArSoft there is not readily an e- drift model and wire/CRP signal simulation
  Nor the Nq and Npe reconstructions
Happy to discuss how we can get there.
  Or when it’s time to go back to LArSoft for these studies
    Or whatever the new framework is!