## Slide 1
Katsuya Yonehara
TSD Topical Meeting
3/21/2024
Advancing Targetry R&D for
The US Muon Collider

## Slide 2: Begin of the story: Why Muon Collider?

## Slide 3: Discovery of Higgs boson!
Higgs boson was discovered in 2012 at CERN
  LHC is 14 TeV COM p-p collider
Event plot shows
Bottom histogram plots show the event rate of

## Slide 4: What we know and what we don’t know about H?
The Standard Model predicts the existing of Higgs boson which provides a mass to elementary particles with the Higgs mechanism
Higgs boson has been investigated
  Observed Higgs character is similar as the SM prediction
  Higgs mass is measured
Still several questions
  How top quark () has heavier mass than Higgs?
  What is the origin of neutrino mass?
Need more Higgs to investigate its property
Higgs for theorists

## Slide 5: Muon Collider has potential to the Higgs factory
: can be Higgs, or new discovery particle
  Muons are coated with vector bosons, which are suddenly stripped by collisions, and creates multiple Higgs (Vector boson fusion): This is the analogy of synchrotron light emission from electrons

## Slide 6: Muon Collider has potential to the Higgs factory
collision event is typically clean by comparing a hadronic collision event
High Luminosity LHC (HL-LHC) will provide
X-section of is

## Slide 7: Muon Collider is energy efficient
Efficiency becomes better at higher COM energy in case of muon collider
(Very) preliminary cost estimation for various collider projects

## Slide 8: Muon Collider at Fermilab Site
Layout shows a 10 TeV COM muon collider inside Fermilab campus
Totally three RCS rings needed
Two RCS rings is in one tunnel

## Slide 9: Challenge of muon acceleration
Muon is tertiary particle
  Dominant phase space of muons,
Muon has a finite lifetime, ms
  Need rapid acceleration to reach TeV scale
Pions have a large angular momentum, , thus muons
  Need to reduce their phase spaces by, for producing desired collider luminosity,
  Need muon emittance cooling

## Slide 10: Layout of muon accelerator complex for colliders
Targetry (cover in this talk)
MAP baseline design (based on simulation study)
Proton driver: 1014-1015 protons within 1-3 ns bunch length
Front end: p/m capture section (m/p efficiency 10-15 % for each sign)
MW-Class Target: Interface between proton driver and Front-end
The US physics community had Muon Accelerator Program (MAP) in 2010-2016

## Slide 11: Characteristics of Proton beam parameter at intense beam facility
 | Neutron spallation source (ESS, SNS, CSNS) | Accelerator Neutrino beam (T2K, CNGS, NuMI, SBN, LBNF) | Muon collider (MAP, IMCC design)
Proton beam energy | Low (1-3 GeV) | Wide range (8-400 GeV) | Medium (5-20 GeV)
Proton beam bunch length | Short (105-700 ns) | Long (4.2-10.5 ms) | Extremely short (1-3 ns)
Proton beam intensity per bunch | Medium (1e13-1.5e14) | Medium (4.8e13-3.2e14) | High (1e14-1e15)
Repetition rate | High (14-60 Hz) | Low (0.4-2 Hz) | Medium (5-15 Hz)
Target material | Liq. Hg, W, Liq. Li etc | graphite | ?
Is there any target capable of withstanding such an exceptionally high thermal shock?

## Slide 12: Thermal shock is a key parameter for survivability of High-Power Target
Neutrino HPT R&D Materials Exploratory Map (Graphite)
Boundary represents operational threshold for thermal shock on graphite targets

## Slide 13: Past Muon Collider Target Study

## Slide 14: Demonstrate liquid (Hg) target
1 cm
Layout of MERcury Intense Target (MERIT)
Proof-of-principle demonstration of a free Hg jet target for a 4-MW proton beam, contained in a 15-T solenoid
MERIT was carried out in 2007 by using CERN nTOF11 beam line
  14 & 24 GeV protons up to 16 bunches/pulse, up to 3.5e12 protons/bunch with beam angle 67 mrad w.r.t. magnet
  360 beam pulses in total
3/21/24
Target R&D for Muon Collider, Yonehara

## Slide 15: Jet splash in Magnet and Secondary yield measurement
0 Tesla
2 Tesla
4 Tesla
6 Tesla
10 Tesla
Plot shows side view of Hg jet profile with proton beam impact in a solenoidal field (simulation)
Plots show the observed integrated signal in pCVD detectors (position of detectors are shown a magenta cross mark below)

## Slide 16: Summary of MERIT
Jet surface instability is significantly reduced at higher magnetic field strength
Jet disruption length is less than length of beam overlap with the jet
There is no jet disruption for pulses of less than 1 Tp (or higher in higher magnetic field)
Bunches more than 5 ms apart act separately in causing disruption
While visible disruption begins 50 ms after a proton pulse, secondary particle production is the same for pulses that follow at several times this value
A liquid (or granular) target is an attractive method for intense muon sources
  Are there any alternative materials besides mercury?

## Slide 17: Granular Tungsten
Potential candidate for High Power Target
  Mitigate thermal stress & Maintain fresh material
  No cavitation issue & no beam window (C-ADS scheme)
  Comprehensive studies led by STFC, CERN, and C-ADS
Powder lifted by beam
due to electrostatic or electromagnetic force
W-25
W-45
W-90
W-150
1 mm
Neutron source proposed by C-ADS
Layout of granular W beam test at HiRadMat
Han-Jie Cai et al.
Nucl. Eng. Tech. 54 (2022) 2650
C. Caretta et al.
Phys. Rev. AB 21, 033401 (2018)
T. Davenne et al.
Phys. Rev. AB 21, 073002 (2018)

## Slide 18: Strategic plan for Future MuC Target R&D

## Slide 19: International Muon Collider Collaboration (IMCC)
CERN has head(?) started the feasibility study of muon collider since 2021
  They will evaluate the collider design by 2026
  They will decide either FCC-ee, CLIC or muon collider
  If muon collider is selected, the demonstrator will start constructing around 2028
They need a target for the demonstrator
Layout of demonstrator facility
Possible location of demonstrator facility

## Slide 20: (Rough) Timeline of the US MuC activity
P5 suggests to develop the feasibility of MuC in the next 5-7 years
  They encourage to design the demonstrator
  The demo target will be designed for low power beam, if the technology is extendable to multi-MW
So far, we have no resource for MuC
  No money in FY24
  Expect some support in FY25, but we do not know…
What I propose
  Form the MuC target R&D working group
  Simulation study
  Performance test

## Slide 21: DOE suggests to make a roadmap for HPT R&D
HPT R&D is aligned with timeline of HEP Accelerators
HEP HPT R&D Workshop
April 11-12 2023
NOTE:
Each project set a specific target parameter, thus
each target has a specific challenge and specific R&D.
Current HPT R&D plan works on a generic item.
We should identify a specific issue on MC.

## Slide 22
R a D I A T E Collaboration
Radiation Damage In Accelerator Target Environments
RaDIATE collaboration created in 2012, with Fermilab as the leading institution. The collaboration has grown up to 20 institutions over the years.
First MoU was signed with 5 institutions 10 years ago!
Objective:
Harness existing expertise in nuclear materials and accelerator targets
Generate new and useful materials data for application within the accelerator and fission/fusion communities
Activities include:
Analysis of materials taken from existing beamline as well as new irradiations of candidate target materials at low and high energy beam facilities
In-beam thermal shock experiments
Contact:
Frederique Pellemoine, fpellemo@fnal.gov
Web: radiate.fnal.gov
Join RaDIATE
Notes: To address these material challenges, the HPT community formed the RaDIATE collaboration in 2012, with Fermilab as the leading institution. The goal was to bring experts from the accelerator and fission/fusion communities together to generate new data for accelerator materials. The collaboration has grown up to 14 institutions over the years.

## Slide 23: Specific subject on the MC Target R&D
Utilize High Performance Computing Facility
  Build AI to enhance target performance
    Look into the MC target system from multiple view-point
  Develop simulation to study sub-pico second evolution of defect
    Apply ML to learn discrepancy Models from Experimental Data
    Develop pico-sec radiation damage sensor (LDRD)
Collaborate with UW Madison and SNS to enhance computing radiation material science

## Slide 24: LDRD: Fast non-contact radiation damage sensor
Observe time evolved reflectivity of material using probe light
  Reflectivity represents a material structure
Proposed test stand
Predicted reflectivity change
(typical metal)

## Slide 25: Types of simulations: Time vs. system size
Density functional theory (DFT): Defect formation energies, band gap, etc.
  Apply this technique to design HEA
Molecular dynamics (MD): Radiation damage such as void formation, evolution of system with respect to temperature, etc.
Macroscopic phenomena
Microscopic phenomena
Goel, Saurav, et al. Materials Today Chemistry 18 (2020): 100356
Arora, Gaurav, et al." Materialia 15 (2021): 100974
DFT is capable to simulate defect annihilation, clustering and mobility in sub-pico-sec time step
Notes: David senor PNNL
Give example of formation energy of defect.

## Slide 26: Pion yield measurement at Fermilab
Study beam interactions in beam intercepting devices
Because the EMPHATIC spectrometer is compact, it realizes
  Large angular acceptance
    Small dead space
  Fine position detection
    Precise angular distribution measurement
Pico sec fast counter
  Precise energy measurement
US-Japan collaboration
  FY25 budget requested
EMPHATIC spectrometer

## Slide 27: Enhance MuC target performance
Manage mechanical stress within specified tolerances
Maximize pion yield with preferred energy band
  Find most effective configuration of low Z (to reduce edep and pion recapture) and high Z materials (to increase and localize pion yield)
  Determine optimal dimensions to satisfy engineering tolerance as well as pion yield
Capture pions & muons
  Ideally capture both signs  Solenoid or FODO cell magnet
  Transport them into the downstream channel
  Remove primary proton beam from muons
  Manipulate phase space of pions and muons if needed
Develop AI technology to enhance target performance

## Slide 28: Propose MuC High Power Targetry R&D

## Slide 29: Plan
Forming MC Targetry R&D working group
  Scientist + Target engineer + AI scientist
  Join RaDIATE collaboration
    Utilize their expertise and facility to develop the MC target technology (next slide shows the current world RaDIATE map)
Gain resources
  FY25 LDRD approved to make an ultra-high-speed non-contact radiation damage sensor for future HPT system
  FY25 US-Japan collaboration requested
  Anticipate more resources from the GARD HPT
    Budget for utilizing Beam Irradiation Facility & PIE Facility
Longer term
  Add more collaborators
  Beam irradiation tests