## Slide 1: ROI study for data reduction and improving low energy sensitivity
Matthew Man,
Nikolina Ilic,
Danaisis Vargas
March , 2024

## Slide 2: Motivation
Trigger threshold is limited by data volume, 30 PB/year for DUNE
ROI reduces data volume by removing “empty” channels from trigger records (zero suppression)
Goal to increase sensitivity to low energy events ( <10 Mev ) by permitting a lower threshold
ROI to be implemented in DAQ data filter

## Slide 3
Slide from Josh Klein

## Slide 4: ROI details
ROI is threshold based. When a channel goes above an ADC peak threshold, ROI is applied
Neighboring channels stored, width of 10 wires on each side
  Recommended by Wirecell experts as the effective induction range for a point charge
ROI time granularity is width of the frame, 6000 ticks ~= 100 μs
Outside the ROI is zero suppressed
Tunable parameters are the peak threshold, and neighboring channel width

## Slide 5: Simulations
2DROIAna package in duneana fork here:
  https://github.com/matthew-man-457/duneana/tree/mman/2D_ROI
Simulation workflow (dune10kt_1x2x6):
  MARLEY gen using solar boron 8 flux + latest decay0 backgrounds
  Standard G4
  Detsim uses notpcsigproc (outputs rawdigits)
  ROIAna
Uses:
larsoft_v09_82_02d01
dune10kt_v6_refactored_1x2x6.gdml
dunefd_hd_backgrounds_1x2x6_v3_5

## Slide 6: ROIAna
In the analysis the ROI is applied on RawDigits, which are simulated raw waveforms
In the Data Filter we would run on Trigger Records (not yet implemented/tested)
Applies ROI on RawDigits and calculates various performance metrics:
  Energy fraction captured within ROI
  Charge fraction captured within ROI
  Data reduction rate estimate (as fraction of channels within ROI)
  Sensitivity to signal
Definitions:
  sim::IDE.energy – amount of energy released by ionization (from G4 simulation)
  sim::IDE.numElectrons – amount of electrons reaching the readout channel after drifting

## Slide 7: ROIAna output
n=10000 events
Threshold is 100 ADC counts
Proportion of ionization energy deposited captured within ROI
%

## Slide 8: ROIAna output
n=10000 events
Threshold is 100 ADC counts
Proportion of electrons reaching the within ROI
%

## Slide 9: ROIAna output
n=10000 events
Threshold is 100 ADC counts
Proportion of channels with ROI
With this threshold on average ~80% fewer channels stored

## Slide 10: ROIAna output
n=10000 events
Threshold is 100 ADC counts
Sensitivity of ROI to Marley signal, as given by fraction of energy of Marley events within ROI
With this threshold on average 42% of energy from signal events is contained within ROI

## Slide 11: Discussion
From DAQ side this is another knob to tune data rate sent offline
From LowE side this tunes sensitivity and statistics of <10 MeV events, eg. Solar neutrinos
  Reality is a balance of the two
Input from low energy and DAQ groups on setting the ROI threshold
Should check reconstruction performance on ROI-applied data, that deconvolution doesn’t introduce aliasing
Can Readout keep up with a rate corresponding to a lower threshold?
Working on sensitivity study of ROI on solar B8 and background rejection
  Would be interesting to break down each metric by their source

## Slide 12: Backup slides

## Slide 13: Solar B8 spectrum
We expect a solar neutrino event rate of ~100 per day in a 40kt LArTPC
So our sample of 10000 events represents 100 days

## Slide 14: Decay0 backgrounds
Slide from Sergio Manthey

## Slide 15: OLD version of ROI
Implemented in Wirecell
The width ROI in time was too tight, it introduced artifacts upon deconvolution, which were too troublesome to work around

## Slide 16: Example event