## Slide 1: 9 O’Clock Meeting
Nathan Ruffatti
MCR Crew Chief
Monday, April 1st, 2024

## Slide 2: Since Friday…
  Friday:
  KRF5 tune-up study, MIRF15 tie-in
  8 GeV collimators partially put in, 8 GeV BPM issues
  GMPS trip on vacuum activity
  Saturday:
  FAST Laser Room HVAC trip, Contractors replaced Condensate pump
  B:IPINJ1 bad ‘A’ cable, was unplugged from PS
  R:KPS4D thyratron delay fire trips, Pete raised filament and reservoir voltages
  F4 SB power loss, Tripped main breaker for upper circuits. DE recovered

## Slide 3: Since Friday…
  Sunday:
  MI abort vacuum alarms high, took a couple steps up since Saturday
  MIRF14 HV deck interlock faults, station bypassed
  I:LD5FP, MI damper forward power, dropped to zero
  Monday:
  R:QT306 tripped on ground fault indication, replaced with spare. Regulator breaker had also tripped.