## Slide 1
DUNE Timing System
Introduction
DUNE Timing System interim PRR for
DUNE-variant AFC
19/April/24

## Slide 2
Overview
System Requirements
Implementation
  Redundant paths
  uTCA based
  Components in system
System Design
  Role of AFC in system
  How many AFCs
19/Apr/2024
2
Notes: 2

## Slide 3
System Requirements
Described in EDMS 2389053 .
Key requirements:
  Alignment of clock/timestamp between endpoints in a single cavern better than 5ns (RMS).
    Relaxed w.r.t. v1 of requirements. Can be satisfied by measuring to single bit-time.
  Global alignment with respect to TAI/UTC better 1us
  Detection of failed endpoint in O(1s)
  High uptime ( > 99.9% ) – DUNE is a neutrino observatory as well as detecting beam neutrinos.
  High reliability – when the system delivers a time, the time must be accurate.
We will aim to show that the DUNE-variant AFC is part of a system that will meet these requirements
19/Apr/2024
3
Notes: 3

## Slide 4
Implementation
19/Apr/2024
4
Notes: 4

## Slide 5
Implementation
Redundancy
  GPS receiver at each of: Ross, Yates.
19/Apr/2024
5
Notes: 5

## Slide 6
Implementation
Redundancy
  Two uTCA crates.
    One active
    One standby
  Outputs combined optically
19/Apr/2024
6
Notes: 6

## Slide 7
Implementation
uTCA based
  Hot swap PSU
  Hot swap fans
  Hot swap AMC (AFC) boards
  Voltage, Current, Temp, Fan monitoring
19/Apr/2024
7
Notes: 7

## Slide 8
Implementation - AFC
uTCA AMC FMC carrier boards host interface to detector.
AFC chosen (simple, low cost, open hardware)
Crate can host up to 12 boards
19/Apr/2024
8
Notes: 8

## Slide 9
Implementation
Transmit/Receive between timing master and endpoints over optical fibre.
  1000Base-BX SFPS – both directions on same fibre.
Passive Optical Splitting used to:
  Drive multiple timing endpoints from one timing fibre
  Allow redundancy: 2:1 combiner/splitter between active and stand-by crates.
19/Apr/2024
9
Notes: 9

## Slide 10
Components – GPS Interface Board
Above ground. Link to GPS.
Prototype under test
Pre-production version Q2/24
Covered by PRR Q3/24
19/Apr/2024
10
Covered by full PRR
Notes: 10

## Slide 11
Components – MicroTCA Interface Board
Receives timing from GIB
In MCH1 slot of uTCA crate
Second prototype under test
Pre-production version Q2/24
Covered by PRR Q3/24
19/Apr/2024
11
Covered by full PRR
Notes: 11

## Slide 12
Components – FIB
Houses optical interfaces to detector
Hosted by AFC
Double width FMC format
Prototype under test
Pre-production version undergoing checks before manufacture
Covered by PRR Q3/24
19/Apr/2024
12
Covered by full PRR
Notes: 12

## Slide 13
Components – AFC
Hosts FIB
Standard format AMC
Open Hardware
Hot swappable
Needs minor modification for DUNE use.
Covered by this iPRR
19/Apr/2024
13
Photo: https://ohwr.org/project/afc/wikis/home
Subject of this interim
PRR
Notes: 13

## Slide 14
Role of AFC
Routes clock and timing data from/to MIB to/from FIB
At heart of AFC – a low-jitter clock cross-bar
  250MHz clock from MIB (four times bit-rate) transmitted over dedicated point-to-point uTCA backplane differential lines (TCLKA)
19/Apr/2024
14
Notes: 14

## Slide 15
Role of AFC
FPGA on AFC receives timing data from MIB via cross-bar.
  Carried from MIB to AFC on dedicated point-to-point FCLK lines.
  Timing ``master’’ in each crate in MIB FPGA handles polling on endpoints attached to FIBs
19/Apr/2024
15
Notes: 15

## Slide 16
Role of AFC
FPGA on AFC receives data from 8 SFPs on FIB and multiplexes onto single point-to-point TCLKB line to MIB
19/Apr/2024
16
Notes: 16

## Slide 17
AFC Modification
Standard AFC routes FCLK to FPGA Gigabit transceiver reference clock input
Signal not accessible to logic inside FPGA
Modify design to route FCLK to clock cross-bar
19/Apr/2024
17
Notes: 17

## Slide 18
AFC Modification
Need for modification to standard AFC drives the need for this interim PRR
  Move FCLK on AFC from Gigabit transceiver reference clock to clock cross-bar
  Have tested by patching standard AFC v4 boards.
Modification minor, but want to produce pre-prototype boards with modification and test before production
 Long lead time
 iPRR
(More detail of schedule in following talk)
19/Apr/2024
18
Notes: 18

## Slide 19
AFC Numbers
System will need:
  Twenty AFC/FIB for Horizontal Drift Cavern
    Ten in each crate
  Ten AFC/FIB for Vertical Drift Cavern
    Five in each crate
  Will provide spare timing connections at cryostat for tests and flexibility
  See introduction to EDMS 3069484 for details of fibre/board numbers
(See next talk for spares policy, pre-production boards and boards for permanent test/development set-up,)
19/Apr/2024
19
Notes: 19

## Slide 20
Changes as a result of FDR
Has the consortium responded appropriately to the relevant recommendations from past design reviews and are they closed?
Timing System FDR recommendations still open, (Review-022 paraphrased):
  Rec 12, 13 “A full system test should be performed before PRR and production.” Will be done at NP04/02 before PRR in Q3/24
  Rec 7 “Tests should include a full range of endpoints.”
    Will be done at NP04/02 before PRR in Q3/24.
    Existing data shows timing master / endpoint combination factorizes. ( No bad master/endpoint combinations)
     Since all endpoints tested with prototype hardware don’t need to wait for tests with AFC at ProtoDUNE
  Rec 5 “Tests should include hot swap functionality.”
    As a result of review decided to change to “warm swap”.
    Will be tested at NP04/02 before PRR in Q3/24.
    Swapping between sources handled by GIB/MIB combination  Don’t need to wait for warm-swap tests including AFC.
19/Apr/2024
20
Notes: 20

## Slide 21
Changes as a result of FDR
Has the consortium responded appropriately to the relevant recommendations from past design reviews and are they closed?
DAQ FDR recommendations still open (Review-081 paraphrased):
  Rec 1 “Designs of all DTS boards to be finalized and used in a full system test”.
    Pre-production boards will be used at NP04/02 before PRR in Q3/24
    Full chain (with standard AFC patched to specification of DUNE-variant AFC ) tested in lab. More details in next talk.
  Rec 12 “A complete system test should be done at ProtoDUNE-II”. Will be done at NP04/02 before PRR in Q3/24
  Rec 13 “An electrical safety review of boards must be carried out”
    An interim electrical safety review of the AFC has been done (EDMS 3057177). Will be completed when pre-production AFCs are available, before PRR in Q3/24. More details in next talk
    A safety review of the uTCA system has been completed (in conjunction with VD TDE)
    A safety review of the pre-production GIB , MIB , FIB will be done when boards are available, before PRR in Q3/24
19/Apr/2024
21
Notes: 21

## Slide 22
Changes as a result of FDR
Are there any further relevant reviewer comments and recommendations based on design changes
We have received no comments relevant to AFC
(MIB, FIB will be reviewed later in 2024)
19/Apr/2024
22
Notes: 22

## Slide 23
Summary
The AFC is an Open Hardware board that is relatively low cost and tested in other projects.
A minor modification to clocking circuitry is needed for use with DUNE Timing System
  Tested by modifying standard AFC v4 (removing some capacitors / resistors and adding external “twin-ax” cable) – results in following talk.
  Prefer to modify design rather than patching standard board for production boards. (Details on schedule in following talk)
We have undertaken a “full chain” test to demonstrate that AFC meets requirements (see following talk)
Number of boards that will be ordered gives room for flexibility and permanent debug/development system during the life of DUNE.
19/Apr/2024
23
Notes: 23

## Slide 24: BACKUP

## Slide 25
DTS for ND
DTS has sufficient performance for use at ND
  Need O(100ps) alignment
  Will need addition to AFC firmware
    Measuring phase of returning data to O(10ps)
3/Mar2024
25
Notes: 25