## Slide 1: MQXFA18 Coil Reception Electrical QC Measurements Coils 154, 160, 161, 243, 244, 246
MQXFA18 Coil Selection Review
Bob Memmo, Pardeep Chahal, Dan Cheng
May 21, 2024
LBNL

## Slide 2: Overview
New Coils reported on will be
  154, 160, 243, 246
  Coils 161 and 244 are spares
LBNL EQC Acceptance Data
  Summarized in following slides
  Now includes acceptance values reviewed by V. Marinozzi

## Slide 3: Coil Data
All coils are Series coils, with limited voltage taps
 |  |  | 243 | 244 | 160 | 161 | 154 | 246 | 
See DocDB #956 / SU-1010-1903 |  |  |  |  |  |  |  |  | 
RLQ |  |  |  |  |  |  |  |  | Acceptance Range
 | R | (mΩ) | 604 | 604 | 598 | 601 | 605 | 609 | 590-625
 | Ls (mH) | 20 Hz | 10.021 | 10.014 | 9.933 | 9.973 | 10.01 | 10.075 | 9.9-10.3
 |  | 100 Hz | 6.423 | 6.419 | 6.403 | 6.407 | 6.409 | 6.394 | 6.2-6.6
 |  | 1 kHz | 5.813 | 5.815 | 5.797 | 5.793 | 5.803 | 5.785 | 5.5-6
 | Q | 20 Hz | 1.289 | 1.289 | 1.3 | 1.294 | 1.288 | 1.274 | 1.2-1.4
 |  | 100 Hz | 5.53 | 5.508 | 5.539 | 5.506 | 5.483 | 5.44 | 5.2-5.8
 |  | 1 kHz | 8.354 | 8.542 | 8.475 | 8.414 | 8.523 | 8.5 | 5.8-10.7
QH R (Ω) |  |  |  |  |  |  |  |  | 
 | NT | A01 | N/A | N/A | N/A | N/A | N/A |  | 
 | T | A02 | N/A | N/A | N/A | N/A | N/A |  | 
 | T-P | B01 | 2.1 | 2.1 | 2.1 | 2.1 | 2 | 2.2 | 1.4-2.7
 | NT-P | B02 | 2.1 | 2 | 2 | 2.1 | 2.2 | 2.3 | 1.4-2.7
 | T-M | B03 | 2.1 | 2.4 | 2 | 2 | 2.1 | 2.3 | 1.4-2.7
 | NT-M | B04 | 2.1 | 2.3 | 1.9 | 2.1 | 2.2 | 2.3 | 1.4-2.7
VT R (mΩ) Individual coils |  |  |  |  |  |  |  |  | 
@1 Amp |  | A1 | 0.00020 | 0.00007 | 0.00011 | 0.00016 | 0.00007 | 0.00009 | 
 |  | A2 | 0.00025 | 0.00013 | 0.00016 | 0.00021 | 0.00013 | 0.00014 | 
 |  | A3 |  |  |  |  |  |  | 
 |  | A4 |  |  |  |  |  |  | 
 |  | A5 |  |  |  |  |  |  | 
 |  | A6 |  |  |  |  |  |  | 
 |  | A7 |  |  |  |  |  |  | 
 |  | A8 |  |  |  |  |  |  | 
 |  | B8 |  |  |  |  |  |  | 
 |  | B7 |  |  |  |  |  |  | 
 |  | B6 |  |  |  |  |  |  | 
 |  | B5 |  |  |  |  |  |  | 
 |  | B4 |  |  |  |  |  |  | 
 |  | B3 |  |  |  |  |  |  | 
 |  | B2 | 0.60415 | 0.60390 | 0.59770 | 0.60070 | 0.60480 | 0.60930 | 
 |  | B1 | 0.60430 | 0.60410 | 0.59790 | 0.60090 | 0.60520 | 0.60960 | 
HIPOT |  |  | OK | OK | OK | OK | OK |  | 
IMPULSE |  |  | OK | OK | OK | OK | OK |  | 

## Slide 4: Hipot and Impulse tests
Hipot tests passed for all coils
  See Coil EQC data workbook on Indico Page
Impulse tests at 2000V shown below

## Slide 5: Summary
Coil acceptance EQC tests are complete
  All measurements passed
  No other issues observed

## Slide 6: Appendix