## Slide 1: Tooth strip to board step measurements
Nelson, Dar
13-may-2024

## Slide 2: outline
Production procedures update
Status to step measurements
Production status and schedule projection

## Slide 3: Procedures update
The US (W&M) group had been using a version of the UK’s geometry board assembly procedures based on last summer
  We make a version of that procedure updated for local conditions
    Different tooth strip trimming – we do ours on a fixture on a CNC mill
    Different epoxy application method
    All other aspects meant to be the same
They have made a number proc’s updates in the UK over the last year
  We knew of some by not other of these
    Cleaning was done the same, for example
    Measurements of step between board and strip was developed in parallel
    Using a Dremel brush to remove excess epoxy was new to us
Had a couple productive sessions reviewing the UK proc’s in detail
  Led by Brian and Justin with QA office participating
  When we get revised UK proc note will insert the US specific areas
  Then we will again be working on a common procedure

## Slide 4: Step between board and tooth strip
Specification of +/- 200 um (0.2mm) between top surface of the board and the top of the tooth strip
Two measurement techniques
  A machinist’s dial indicator – for production (right)
    Currently https://www.mcmaster.com/20715A81/ with a 4mm tip
    Moving to the UK’s tip indicator with 1mm tip https://www.zoro.co.uk/shop/measuring-and-test-equipment/dial-test-indicators-lever-type/dial-test-indicator-513-424-10t/p/ZT1025781P
    Moving from a lab bench to an optical table for production measurements
  A precision profilometer – for testing precision of method
    https://www.bruker.com/en/products-and-solutions/test-and-measurement/stylus-profilometers/dektakxt.html
    10s of nm precision, available for (shared) use in W&M’s core labs
    Cross calibration in progress

## Slide 5: Preliminary tests of 6 boards
Dial indicator in a work bench
All 36 measurements were within the 200um
All but one point with the strip above the board

## Slide 6
Profilometer in action

## Slide 7
8760040 | Board is higher (microns)
1 | 112
2 | 129
3 | 117
4 | 47
5 | 104
Assembled board foot step
1
1
2
3
4
5

## Slide 8
8760038 | Board is higher (microns)
1 | 82
2 | 103
3 | 83
4 | 32
5 | 83
6 | 130
7 | 55
8 | 60
Assembled board foot step
1
1
2
3
4
5
6
7
8

## Slide 9
8760038 | Board is higher (microns)
1 | 137
2 | 180
3 | 176
4 | 167
5 | 123
6 | 125
7 | 124
8 | 132
Assembled board foot step
1
1
2
3
4
5
6
7
8

## Slide 10
8760038 | Board is higher (microns)
1 | 85
2 | 57
3 | 35
4 | 62
5 | 46
6 | 114
Assembled board foot step
1
1
2
3
4
5
6

## Slide 11
200 tolerance line
Profilometer data
All are “board taller than strip” in this sample

## Slide 12: Observations
We see larger variations in step away from the center of the board
  UK’s plan for adding 4 extra clamps near the corners is a good idea
  When the updated drawings are ready, we will update the fixtures accordingly

## Slide 13: Precision?
Initial cross check (1 board, 6 points) shows 20-30um RMS on the comparison of the two devices
More correlated data on the way
  This will be w/ new dial indicator + smaller ball + optical table
  Will work through the current inventory to test and develop statistics
Note time-motion test on these measurement add about 25% to the effort to produce a board

## Slide 14
Notes on status

## Slide 15: Status
On a work stop
  Pending plans, review, and (possible) site visit to W&M to address issues seen in delivered boards
Recent issues
  Main - older boards (before ~ Sept 2023) have adhesions problems at least in part due epoxy loading near the ends of the ends of the strips
    Do not plan to use these boards unless there is an approved remediation method; not pursuing at this point
  Epoxy on tooth strips and surface of some recent boards
    New UK proc with Dremel tool will fix the issues on the strips
Actions
  Adding new QC checks at the end of production accordingly
  Sent video of our assembly process for comment from the UK
  Got useful feedback
  After we have added the W&M-specific steps in the proc’s to reshoot for feedback

## Slide 16
After reauthorization to start production, we could produce an APA’s work each two weeks
  Worked with Brian on a set of deliverable documentation
  It is important to get the reject boards (their IDs too) from UC to track their status and make sure we understand the origin on these issues
  Plan needs approval
  Hope for this in early June

## Slide 17: Production status/schedule
Have delivered acceptable boards for
  APA 1 all layers
  APA 2 x, v layers
Currently we only have received U long side boards for 2.7 APAs
  Some of those were in the bad-board era
  Last delivery in January
  Do not have enough currently to complete APA 2 u layer
  These boards are the critical path – other board types assembled do no advance our completion date

## Slide 18
Backup slides

## Slide 19
8760038 | Board is higher (microns)
1 | 101
2 | 105
3 | 90
4 | 54
5 | 57
6 | 83
7 | 128
Assembled board foot step
1
1
2
3
4
5
6
7

## Slide 20
8760054 | Board is higher (microns)
1 | 40
2 | 40
3 | 84
4 | 68
5 | 102
6 | 48
Assembled board foot step
1
1
2
3
4
5
6

## Slide 21
8760054 | Board is higher (microns)
1 | 30
2 | 58
3 | 109
4 | 41
5 | 56
6 | 35
Assembled board foot step
1
1
2
3
4
5
6

## Slide 22
8760057 | Board is higher (microns)
1 | 144
2 | 58
3 | 142
4 | 230
5 | 77
6 | 182
Assembled board foot step
1
1
2
3
4
5
6

## Slide 23
8760038 | Board is higher (microns)
1 | 114
2 | 103
3 | 72
4 | 42
5 | 140
6 | 105
7 | 135
Assembled board foot step
1
1
2
3
4
5
6
7

## Slide 24
8760057 | Board is higher (microns)
1 | 104
2 | 112
3 | 31
4 | 98
5 | 70
6 | 174
7 | 175
8 | 90
Assembled board foot step
1
2
3
4
5
6
7
8

## Slide 25
8760040 | Board is higher (microns)
1 | 201
2 | 82
3 | 195
4 | 153
5 | 60
6 | 141
Assembled board foot step
1
1
2
3
4
5
6