## Slide 1: Oscura in 10 Minutes
On behalf of the Oscura Collaboration
Edgar Marrufo
New Perspectives 2024

## Slide 2
SIFS bench spectrograph
Dark Matter Evidence
  Evidence for the existence of dark matter from Astronomy/Cosmology
  Astrophysical Probes
  Rotation curves, cluster collisions, gravitational lensing
  Cosmological Probes
  CMB anisotropies
  Structure formation
Planck Collaboration 2008

## Slide 3
SOAR Telescope
SIFS bench spectrograph
1
1
1
1
eV-scale Bosons and Sub-GeV DM:
Absorption and Inelastic scattering as interaction mechanisms (feeble interactions)
DM Kinetic Energy
Imparted Momentum in Scattering
Imparted Energy and Momentum in Absorption
Direct Dark Matter Detection

## Slide 4
Sub-GeV DM needs other detection channels
[JHEP 05 (2016) 046]
DM direct detection with CCDs
DM-nucleus scattering
mχ ~ GeV → energy transfer is a few keV
DM-electron scattering
mχ ~ MeV-GeV
→ energy transfer is a few eV
DM absorption
Bosonic DM at the eV scale
→ energy transfer equals mχ

## Slide 5
Skipper CCD qualities for direct detection:
  Energy threshold of Si bandgap(~1.1 eV)
  Low dark current (e-/pix/day)
  Sub-electron (~0.1e-) readout noise
  Low Threshold enables low-mass searches:
Skipper-CCDs for direct DM search
  Electron scattering of 1-1000 MeV DM
  Absorption of 1-1000 eV DM

## Slide 6
World best limits for sub-GeV DM candidates with this technology
Skipper-CCDs for direct DM search
Ongoing program
Experiment | Mass [kg] | #CCDs | Radiation bkgd [dru] | Instrumental bkgd [e-/pix/day] | Commissioning
SENSEI @ MINOS | ~0.002 | 1 | 3400 | 1.6 x 10-4 | late-2019
DAMIC @ SNOLAB | ~0.02 | 2 | ~10 (exp*) | ~3 x 10-4 (exp*) | late-2021
DAMIC-M LBC | ~0.02 | 2 | 10 | 3 x 10-3 | late-2021
SENSEI-100 | ~0.1 | 50 | 10 (goal) |  | mid-2022
DAMIC-M | ~1 | 200 | 0.1 (goal) |  | ~2023
OSCURA | ~10 | 20,000 | 0.01 (goal) | 1 x 10-6 (goal) | ~2028
Oscura builds on existing efforts
* expected from DAMIC with standard CCDs [PRL 123, 181802/PRL 125, 241803]
The challenges are to increase mass (from 10s to 10,000s CCDs) and to reduce the backgrounds (2 orders of magnitude)
Major R&D

## Slide 7
Oscura: 10-kg skipper-CCD experiment
3 m
LN2 pressure vessel @ 450 psi
Multi-Chip Module
(16 skipper-CCDs)
Super Module
(16 MCMs)
[arXiv:2202.10518]
Detector payload in 6 columnar slices (96 SMs)

## Slide 8
Sensors reach sub-electron noise and meet almost all constraints to reach desired instrumental background
Spurious charge is under study and new approaches are being implemented
Installed underground setup at MINOS (MOSKITA) to measure the ultimate DC
Oscura: Sensors performance
No events with >1e-
No events with 3e- or more

## Slide 9
Copy of SENSEI-100 vessel with 10 prototype ceramic MCMs and the discrete readout electronics
Largest ever built instrument with skipper-CCDs controlled by 1 LTA → Demonstrates electronics solution
Oscura: Massive testing setup with 10 MCMs (160 sensors)
~90% of the sensors working without a preselection! This is a BIG deal!*
*LSST, the largest “astronomical camera” has 189 CCDs!
[JINST 18 P01040]
Setup is being used to develop analysis software and could be used for early science

## Slide 10
With the current sensors performance, we have zero background events with 4e- or more (4e curve)
Oscura: Projected sensitivities for 30 kg-year
DM-electron scattering mediated by a heavy (left) or light (right) mediator

## Slide 11
Oscura: Timeline and goals per period
Operation
2021
2022
2023
Sensor preproduction
Operation of SM in LN2
Project Execution Plan
Evaluation of new sensors
Demonstration of MCM readout
Decision on cold-end electronics
SM full backgrounds simulation
Full DAQ
Shield at Snolab
R&D
Design
Construction
Sensor packaging facility
Integration test (10%)
Sensors, cryostat and electronics at SNOLAB for assembly
2024
2025
2026
2027
2028
2029
* Technically driven Oscura timeline
- Achieved

## Slide 12
Oscura is the next step in skipper-CCD DM searches (10 kg)
It will provide unprecedented sensitivity to sub-GeV DM interacting with electrons
R&D work has been successfully completed and main risks have been addressed
Oscura is moving into design phase, with plan to begin construction in FY25 and operations at SNOLAB in FY29
With a partial load, Oscura can do early science producing very competitive results
Stay tuned!
Take-home messages

## Slide 13: THANK YOU!