## Slide 1
PXIE Overview: Goals, Scope, and Organization
Sergei Nagaitsev
Project X Machine Advisory Committee
March 18-19, 2013

## Slide 2: Project X R&D program
Goal is to be prepared for a construction start in Q1FY18
  Most likely, Stage 1
Goal of the R&D Program is to mitigate risk: technical/cost/schedule
      The unique capabilities of Project X depend entirely on the front end, in particular the wideband chopper.
Technical Risks
  Front End
    CW ion source through SSR1
  H- injection system
    Booster in Stage 1, 2; Recycler in Stage 3
  High Intensity Recycler/Main Injector operations
  High Power targets
Cost Risks
  Superconducting rf
    Cavities, cryomodules, rf sources – CW to long-pulse
PXIE

## Slide 3: Front-End R&D Program (as proposed in Oct 2011)
We are building an integrated systems test of the first ~30 MeV of Project X.
  Validate the concept for the Project X front end, thereby minimizing the primary technical risk element within the Reference Design.
  Demonstrate wideband chopper; low-b acceleration
  Operate at full design parameters
Integrated systems test goals:
  1 mA average current with 80% chopping of beam delivered from RFQ
  Efficient acceleration with minimal emittance dilution through ~30 MeV
Collaboration between Fermilab, ANL, LBNL, SLAC, SNS, India
Beam through b=0.1 , 0.2 CM at ~30 MeV with nearly final parameters (1 mA cw, 5 mA peak, arbitrary bunch chopping)

## Slide 4: Bunch structure
The concept of Project X relies heavily on a bunch-by-bunch chopper in the MEBT and transverse rf splitters at high energy
  Some elements of this system are beyond present state of the art

## Slide 5: Project X (Stage 1)
1 GeV
1 msec
1 mA
0.91 mA
0.09 mA
f0/2
RFQ beam Current: 3.64 mA
Average Linac beam current: 1 mA
Transverse RF splitter at 1 GeV
Bunch pattern created in the MEBT

## Slide 6: Project X (Stage 2)
1 GeV
3 GeV
0.5msec
2 mA
1 mA
1 mA
0.25 mA
0.5 mA
0.25 mA
f0/4
f0/8
RFQ Beam Current: 5.0 mA

## Slide 7: PXIE vs Project X
PXIE goal – 1 mA average current
Project X (Stage 1) – 1 mA
Project X (Stage 2,3) – 2 mA
Project X (upgrade capability) – 5 mA
Ion source: 0 – 15 mA (DC)
RFQ design: 1 – 10 mA, 5 mA (nominal)

## Slide 8: Project X Injector Experiment: PXIE
CW H- source delivering 5 mA at 30 keV
LEBT with beam pre-chopping
CW RFQ operating at 162.5 MHz and delivering 5 mA at 2.1 MeV
MEBT with integrated wide-band chopper and beam absorbers capable of generating arbitrary bunch patterns at 162.5 MHz, and disposing of 4 mA average beam current
Low beta superconducting cryomodules: 1 mA to ~25 MeV
Beam dump capable of accommodating 2 mA at 25 MeV (50 kW) for extended periods.
Associated beam diagnostics, utilities and shielding
RFQ
MEBT
HWR
SSR1
LEBT
~ 40 m long
HEBT

## Slide 10: PXIE Goals
Validate the Project X concept and eliminate technical risks
  CW RFQ
  Bunch-by-bunch chopper (2 kickers and absorber)
  MEBT vacuum level and MEBT/HWR interface
  High-current beam acceleration in HWR and SSR1
    Complications can be due to beam loss of RFQ tails in SC linac
  Extinction for the removed bunches better than
    10-4 – specified by the PXIE FRS and determined by multi-experiment operation
    <10-9 – as desired by m-to-e experiment (no formal specification)
Obtain experience in design and operation of SC proton linac
  SSR1 cryomodule will be designed and built by Fermilab

## Slide 11: Major PXIE Features
“Adiabatic optics” – small beta-function variation
  Mitigation of space charge
LEBT
  LEBT chopper
    Supports machine tuning in pulsed mode: Dt ~ 0.5 – 10 ms, frep=60 Hz
RFQ
  162.5 MHz RFQ
    freq. low enough for bunch-by-bunch chopping, T  6.2 ns, bandwidth of ~ 1 GHz
MEBT
  “Two-kickers chopping” makes chopping possible with present technology
  21 kW beam dump for chopped-out beam
  Differential pumping to minimize H2 leakage to the SC cryomodules and RFQ

## Slide 12: Major PXIE Features (continue)
SC cryomodules operating at 2 K
  Solenoidal focusing
  Warm gap between cryomodules
  Fast vacuum valves at both sides of the cryomodules
RF separation at the top energy for beam extinction studies, f=1.5*162.5 MHz
  Can help in measurements of bunch length and longitudinal tails
Instrumentation (not a complete list)
  Toroids, BPMs, wire scanners, laser wires, scrapers
Spectrometer at the end of the machine
50 KW beam dump
  can support operation up to 2 mA beam current

## Slide 13: PXIE location

## Slide 14: PXIE stages
Stage 1:
  Ion source, LEBT, prototype chopper
  RFQ at full power
  Full MEBT with prototype kickers, (possibly) prototype absorber, temp. dump, bunchers, diagnostics
  Cryo system
  SSR1 CM – cold and rf powered, no beam
Stage 2:
  HWR CM – cold and rf powered, no beam
Stage 3:
  Full diagnostics line, final MEBT kickers, final 50 kW beam dump, 1-mA CW beam delivered to the dump.

## Slide 15: PXIE time line
Stage 1 complete – early FY17 (~Nov 2016)
  Beam delivered to the end of MEBT with nearly final parameters (2.1 MeV, 1 mA CW, 80% arbitrary chopping)
Stage 2 complete – Aug 2017
Stage 3 complete – Aug 2018

## Slide 16
16
PXIE Summary Schedule

## Slide 17: PXIE Organization

## Slide 18: India contributions
MEBT/HEBT Quadrupoles, Dipoles
SSR1 Solid State Amplifiers
BPM Electronics
Associated Design, Spec, Procurement Labor

## Slide 19: Ion Source
The Linac beam starts from an H- ion source operating at a constant current, set for a given bunching scenario:
  The minimum ion source current is 1 mA
  The nominal ion source beam current used in Linac design is 5 mA
  The ion source is capable of 15 mA, RFQ and MEBT are designed to 10 mA
Regardless of the ion source current, the average linac beam current is 1 mA
  this is achieved by a LEBT and MEBT choppers

## Slide 20: PXIE LEBT
No BEND in PXIE design

## Slide 21: RFQ
Ion type: H-
Beam current: 5 mA (nominal); 1 – 10 mA
Transverse emittance (norm, rms): < 0.25 mm-mrad
Longitudinal emittance (rms): 0.8 – 1.0 keV-nsec
Input energy: 30 keV
Output energy (kinetic): 2.1 MeV
Duty factor: 100% (CW)
Frequency: 162.5 MHz
Length: ~4.4 m

## Slide 22: Beam in LEBT and RFQ
Input = Gaussian Beam, Envelopes (3-sigma)
LEBT
RFQ
Neutralized
un-neutralized
Details in F.Ostiguy presentation, Nov.29,2012
DC beam

## Slide 23: PXIE Optics from RFQ to beam dump
RFQ
Beam Dump (50 kW)
HWR
SSR1
Diagnostics & Dump
MEBT
Kicker polarity in chopper is set for passing beam
8 x (S-C)
4 x (C-S-C)
SC

## Slide 24: MEBT schematic
Matching from RFQ to MEBT
Measure parameters of the beam coming out of RFQ
Chopping system
Differential pumping/ scraping
Measure parameters of the beam coming into SRF linac
Sections with bunching cavities
Beam energy 2.1 MeV
Input current 1-10 mA
Output current 1 mA
Max bunch
Frequency 162.5 MHz
Bunch-by-bunch selection
Specifications and scheme are stable since Jan 2012

## Slide 25: MEBT
#2-Kicker
#4-Kicker
#3-Wire scanner, fast Faraday cup, RF
#5-Absorber, OTR
#6–Diff. pumping, scrapper,
wire scanner,
Slow valve, Toroid
#0-
Scrapper, RF
#1-Emitttance, laser, Wire scanner, scrapper
#7-Scrapper, RF, Slow valve, Extinction monitor
#8 –
Fast valve, DCCT, Toroid, Laser wire, wire scrapper,
Scrapper ?
Chopped beam
Passing beam

## Slide 26: HWR cryomodule (βG=0.11)
8 cavities, 8 SC solenoids (x,y correctors) and 8 BPMs
Beam energy: 2.1 -- 11 MeV
The first upstream element is a SC solenoid to mitigate vacuum transition
CM Length (flange-to-flange) ~ 5.9 m
P.Ostroumov, Collaboration meeting LBNL,April 10-12,2012,

## Slide 27: SSR1 Cryomodule (βG=0.22)
8 cavities, 4 SC solenoids (x,y correctors) and 4 BPMs
Beam energy: 11 – 25 MeV
CM Length (flange-to-flange) ~ 5.2 m

## Slide 28: HEBT
Beam current monitor
Emit.diagn. Box: slit, LW/WS

## Slide 29: Summary
No change in PXIE design for > 1 year
Organization is in place and functioning
Developed RLS and adjusted the schedule to align with projected budgets
Published the PXIE design handbook