## Slide 1: Machine Protection Systems (MPS)
Arden Warner, and Jim Steimel
Project X Machine Advisory Committee
March 18-19, 2013

## Slide 2: MPS Scope
MPS goals and scope:
  Protect the accelerator from beam induced damage
    Safely switch off or reduce beam intensity in case of failures
    Monitor/control beam intensity
    Fail Safe design where possible
    Provide highest machine availability possible
  Provide overview of machine status
    Subsystems status (ok/not-ok)
    Manage and display alarms
    Performance/fault analysis (i.e. data logging etc.)
    Determine the operational readiness of the machine

## Slide 3: Simplified MPS overview
MPS system will be developed based upon existing, proven systems:
ASTA
SNS

## Slide 4: Operational Modes and Beam Modes
  Operational Mode: :
  Defines the beam path through the accelerator
  A valid beam path through the machine is usually defined by a unique set of critical components (dipole magnets, kickers, beam stops, etc.).
  The MPS monitors the setting of these components to mask alarms that are outside the chosen beam path.
Beam Mode:
  Defines range of beam intensity and duty cycle
  Beam modes define the full range of possible operational beam chopping/intensity scenarios including cycles without beam (no beam) to the MPS.
  Alarm thresholds may be changed or alarms masked for different beam modes to allow for diagnostic operations.

## Slide 5: Sub-System List
vacuum
RF
BLMs
Toroids
BPMs
magnets
Movable devices
LCW
pneumatics
cryogenics
Quench
LLRF
MPS needs to integrate with several subsystems with different times scales of interest:
  BPMs
  BLMs (µsec)
  RF interlocks etc (nsec)
  LLRF (nsec)
  Movable diagnostics (Scrapers, OTR,YAG..) (slow)
  Pneumatics (air, water, gas) dumps
  Toroids (nsec)
  Magnets (msec)
  Timing
  LCW
  Vacuum (msec)
  Beam dumps and kickers
  Rad Safety
All monitored by MPS

## Slide 6: MPS Sphere of Influence
Machine Protection System
Control System Status & Alarms
Beam Instrumentation Data Acquisition
Beam Stop Devices
Device & Component Status (PLC)
Damage Threshold of Beamline Components
Loss Monitors
Limits on Beam Position and Intensity
Fast or Slow Trip Devices
Threshold for Low Duty (Pulsed) Operation
Data Logging
Status of Global Utilities
Operator Interface
- Core of MPS. Provides hooks to interrupt beam in less than 100us.
- Critical interface. MPS must have clear specification from all systems for reliable design.
- Strong influence. MPS designers will have strong expertise and influence over design issues.
Time Stamping

## Slide 7: Critical Interface Issues
Beam Stop Devices:
  Beam reaction time
  Fail safe operation
Beam Instrumentation Data Acquisition:
  Processing time
  Location of processing (within MPS system or BPM system)
  Level of processing (MPS receives status, analog, or raw signals)
  Beam position sensitivity
  Beam current accuracy
  Loss monitor sensitivity and response time

## Slide 8: Critical Interface Issues Cont’d
Device and Component Status:
  Fast vs. slow response devices
  Level of monitoring (MPS processes all monitors directly or receives summary status inputs)
Control System Alarms and Status:
  Communication with controls system (embedded processor)
  Packaging of information to operators
  Response to global system failures (water skid, cryo-plant, facility AC power, etc.)
  Time stamp for changes in status

## Slide 9: System Models
SNS has 1GeV H- SC linac with same average current specified by PXIE. They have a working MPS for their facility.
We have experience with MPS system design for SC linac at NML (electron linac).
Block diagram of SNS MPS system.
Block diagram of NML MPS system.

## Slide 10: Technical Concerns
CW Beam:
  Losses develop continuously; no large, peak beam intensities to trigger loss monitors.
  MPS must allow pulsed, diagnostic beam operation when CW losses inhibit normal operation.
MEBT Chopper:
  Kicks out individual bunches to reduce average current of beam from 5mA to 1mA. Diagnostics needed to insure SRF is not overloaded.
Low Energy SRF Transition:
  Most loss monitors are ineffective at low energies.
  Reduced penetration depth of beam energy impacting niobium.
  Need a way to detect losses before cavities quench.

## Slide 11: PXIE Study Plans
Warm section:
  Develop understanding of acceptable loss rates in
    LEBT
    RFQ
    MEBT
  Develop strategy to monitor chopped beam from the MEBT
Low energy cold section:
  Detection of beam loss in cryomodules
    Develop understanding of low energy beam loss mechanisms and their instruments
    Develop/select sensor technology to directly measure low energy beam loss
    Understand impact of dark current effects on MPS instruments

## Slide 12: Damage Potential and Timing
LEBT Kicker /primary actuator for beam
Require feedback and monitoring of intensity/losses
Chopper must be closely monitored
Devices upstream of MEBT chopper exposed to over 10KW of beam power in early stages of Project X development.
MPS Response time depends primarily on Kicker shut-off time (~100 ns), time of flight (~3µs) and FPGA processing time (1-2 nsec).
Front end beam line (up to 1 GeV) can be tuned with 100 µs beam pulses safely (only 100 Joules of energy at high end). Under this scenario a maximum MPS response time of 100 µs sufficient.
Full scale Project X introduces higher damage potentials. Using SNS as an example, the design goal would be to react in less than 25 µsec.

## Slide 13: MPS Progress to date
Work on cryomodule beam loss detection has begun
  CVD diamond loss monitors are being considered
    Some testing has taken place
    Testing results not yet available
    Early indication: the sensor technology is encouraging
Beam Toroid signal
Single particle detection of scattered electrons and secondary protons from dump

## Slide 14: Summary
MPS is an important piece of Project X design.
Have a close model for a working system at SNS (180MeV to 1GeV).
Have experience with MPS design at NML (electron accelerator).
Need to establish interfaces between MPS, instrumentation, and control systems.
Need to examine low energy issues (2.1MeV to 180MeV) and higher energy issues (1GeV to 8GeV).
PXIE will act as a platform for testing low energy MPS issues.