## Slide 1: Accelerator Facility Design: Safety and Radiation Shielding
Tony Leveling
Project X Machine Advisory Committee
March 18-19, 2013

## Slide 2: Outline
Shield Design Process
Generic radiation shield requirements
Shield design basis
Facility Radiological Goals
Facilities design
Shield Design Status
Challenges
  Non-technical
  Technical

## Slide 3: Shield Design Process
Shield Calculations
Shield Design
Safety Analysis
Radiological design goals
Generic Shielding Requirements
Facilities Design

## Slide 4: Generic Shield Requirements
Fermilab Radiological Controls Manual
  Design requirements source
Shielding Policy
  Fermilab Safety Assessment Document, Appendix B ESHQ DocDB Document 1067-v9
Machine Beam Loss Scenario Documents
  ESHQ DocDB Document 1935-v4
    Provides risk based guidance for shielding design

## Slide 5: Shield design basis
Normal losses
  Goal: generally, limit beam loss to <100 mW/m
  H- stripping
    Intra-beam stripping – dominant source
    Inelastic beam gas scattering
    Halo scraping at apertures
    Lorentz force (magnetic stripping)
    Blackbody photon interactions
  To be defined by region in the safety analysis

## Slide 6: Shield design basis
Intra-beam stripping is the dominant nominal beam loss at CW Linac

## Slide 7: Shield design basis
Accident Condition
  Nominally full beam power loss for 1 hour
    Impractical to apply this principal to megawatt machines
      Implies the use of passive shielding
      Could result in irreparable harm to the machine
    Suggests that active protection is a more sensible approach
  Some credit can be taken for machine protection and controls
    ESHQ DocDB Document 1935-v4
    A list of controls will need to be developed for Project X
  A credible accident condition needs to be developed
    e.g., full beam power loss for 2 seconds

## Slide 8: Shield design basis
Safety analysis will be required
  Preparation is by Project X staff
  Contains
    Normal beam loss conditions
    Credible accident condition
    Machine protection elements
    Active Radiation Safety System controls (if adopted)
SA requires review and approval of SRSO

## Slide 9: Facility Radiological Goals
Limit radiation effective dose to < 0.05 mrem/hr to all spaces
  service buildings, shielding berms, parking lots, control rooms, and associated areas
Limit average beam loss in all accelerator and beam line enclosures to < 1 Watt/m
  Minimize personnel radiation exposure due to maintenance activities
Limit radiation exposure to activated air both on site and at the site boundary
Limit ground water and surface water activation (including tritium) to levels well below regulatory standards
Prevent the activation of beam component surfaces to avoid the generation of removable radioactivity
  Simplify maintenance activities
Minimize the activation of accelerator components
  Provide indefinite component service life

## Slide 10: Facilities Design
Tunnel enclosure
  Size and shape of tunnel
  Position of machine components within enclosures
Support facility requirements
  Service buildings and proximity requirements
Other design features
  Penetrations
  Exit labyrinths
  Drop hatches
  Elevators

## Slide 11: Shield Design Status
Shield Calculations
Shield Design
Safety Analysis
Radiological design goals
Generic Shielding Requirements
Facilities Design
Have these
Don’t have these

## Slide 12: Shield Design Process
Chart: Shielding requirement as function of Beam Energy for various beam power losses to limit effective dose < 0.05 mrem/hr
| 8 | 3 | 1 | 0.9 | 0.8 | 0.70000000000000007 | 0.60000000000000009 | 0.5 | 0.4 | 0.30000000000000004 | 0.2 | 0.1 | 7.0000000000000021E-2 | 5.000000000000001E-2 | 2.0000000000000004E-2 | 1.0000000000000002E-2
1 W/m | 14.4853 | 14.9779 | 15.4339 | 15.4009 | 15.3419 | 15.1973 | 14.9118 | 14.4197 | 13.6296 | 12.3204 | 10.2247 | 6.9162 | 5.6075 | 4.6236 | 2.9369 | 2.2397
10 W/m | 17.4808 | 17.9912 | 18.4248 | 18.3858 | 18.2929 | 18.1108 | 17.7837 | 17.2238 | 16.2931 | 14.7743 | 12.3317 | 7.966 | 7.451 | 6.9122 | 5.7566 | 3.7655 | 2.9507
100 W/m | 20.4743 | 20.9845 | 21.4021 | 21.3525 | 21.2427 | 21.0323 | 20.6581 | 20.0208 | 18.9627 | 17.2336 | 14.4443 | 9.9992 | 8.2181 | 6.8848 | 4.5908 | 3.6645

## Slide 13: Challenges
Non-technical
  Develop a draft safety assessment for submittal to SRSO
    List of machine protection features to get credit
      e.g., machine protection system
    Develop basis for a credible accident condition
    Include consideration of active protection
  Obtain approval of the safety assessment
Technical
  A total loss monitor system (TLM) is a candidate system which could provide active protection
    Development work is ongoing
    Goal is for approval of a prototype system in February 2014
    If the system is not approved, determine an alternate active protection system

## Slide 14: Extra slides

## Slide 15: TLM response to 8 GeV proton beam loss