## Slide 1: A17 shim analysis
Paolo Ferracin
on behalf of the MQXF collaboration
AUP Meeting
LBNL, USA
June 12th, 2024

## Slide 2: Outline
A14b and A05 and A13 quench performance
Computation radial build-up in A14b and A05
Target loading shim size in A17

## Slide 3: Quench performance
After the test of A13, we focused on the analysis of the pre-load in A14b and A05
  At that time, they had the fewest training quenches up to the acceptance current, and both of them met requirements
A14b
A05
A13

## Slide 4: Outline
A14b and A05 and A13 quench performance
Computation radial build-up in A14b and A05
Target loading shim size in A17

## Slide 5: Room temperature pre-stress
The final coil and shell pre-load achieved at the end of the bladder and key operation is determined by the combination of
  the size of the load key shim
  the radial dimensions of the shimmed coil pack
    (under the assumption that collars, pads, masters, yoke, and shell have nominal dimensions).

## Slide 6: Size of the load key shim
A14b
A05
Loading shim size: 43 mils, 1.092 mm
Total key size: 13.84 mm
Loading shim size: 41 mils, 1.041 mm
Total key size: 13.79 mm
Interf shim : 22 mils, 0.483 mm
interf key size: 13.31 mm

## Slide 7: Size of the load key shim
A portion of the total key/shim is to create contact (contact key/shim), and a portion to produce the pre-load (interf. Key/shim)
A14b
A05
Loading shim size: 43 mils, 1.092 mm
Total key size: 13.84 mm
Loading shim size: 41 mils, 1.041 mm
Total key size: 13.79 mm
cont shim : 22 mils, 0.483 mm
cont key size: 13.31 mm

## Slide 8: Radial dimensions of the shimmed coil pack
The coil arc-length is usually undersized
With the mid-plane shim we bring the coil “almost” to the nominal dimensions
  In reality 1) shim has finite given thickness and 2) coil has size variations along the length (and shim is full length with constant thickness)
So, we can produce a radial deviation resulting from the final shimmed azimuthal deviation (average of the coils)
  r_ave = _arc-length_ave * 2/ 
 | Ave ss | LE min | RE min
 | mm | mm | mm
A14b | -0.007 | -0.129 | -0.107
A5 | -0.025 | -0.129 | -0.105
A14b
A05

## Slide 9: Radial dimensions of the shimmed coil pack
There is also a radial deviation due to OR+mid-plane fit of the coil dimensional measurement data
 | OR Ave ss | OR LE min | OR RE min
 | mm | mm | mm
A14b | -0.029 | -0.056 | -0.050
A5 | -0.025 | -0.050 | -0.050

## Slide 10: Radial build-up of the structure
“under the assumption that collars, pads, masters, yoke, and shell have nominal dimensions”
A14b
A05

## Slide 11: Summary
By adding up the interf. Shim and the coil radial size……
  We get an upper bound (A14b) and a lower bound (A05)
 | Ave ss | OR_Ave ss | Sum_ss | LE min | OR_LE_min | Sum_LE | RE min | OR_RE_min | Sum_RE | Key | Shim | Shim | Ave ss + ishim | LE + ishim | RE + ishim
 | mm | mm | mm | mm | mm | mm | mm | mm |  | mm | mils | mm | mm | mm | mm
A14b | -0.007 | -0.029 | -0.037 | -0.129 | -0.056 | -0.185 | -0.107 | -0.050 | -0.157 | 13.84 | 43 | 1.092 | 0.497 | 0.348 | 0.377
A5 | -0.025 | -0.025 | -0.050 | -0.129 | -0.050 | -0.179 | -0.105 | -0.050 | -0.155 | 13.79 | 41 | 1.041 | 0.433 | 0.303 | 0.327

## Slide 12: Outline
A14b and A05 and A13 quench performance
Computation radial build-up in A14b and A05
Target loading shim size in A17

## Slide 13: Summary and proposal
Proposed target
  Aiming at a shim of 43 mils, with the possibility of going to 42-44 mils depending on SG data
 | Ave ss | Key | Shim | Shim | Ave ss + shim
 | mm | mm | mils | mm | mm
A17 up | -0.004 | 13.84 | 43 | 1.092 | 1.088
A17 low | -0.004 | 13.77 | 40 | 1.016 | 1.012
 | LE | Key | Shim | Shim | LE + shim
 | mm | mm | mils | mm | mm
A17 up | -0.134 | 13.84 | 43 | 1.092 | 0.959
A17 low | -0.134 | 13.77 | 40 | 1.016 | 0.882
 | RE | Key | Shim | Shim | RE + shim
 | mm | mm | mils | mm | mm
A17 up | -0.125 | 13.87 | 44 | 1.118 | 0.992
A17 low | -0.125 | 13.82 | 42 | 1.067 | 0.941

## Slide 14: Key-shim size vs. bladder pressure

## Slide 15: Magnet assembly and loading Specifications (shells)
For the pre-load targets at the end of the pre-load:
  The target average measured stress on coils, shells and rods at the end of the loading (after at least 24 h) shall be
    Shell average azimuthal stress: +58 ±6 MPa
Channel | SC02TT | SC02RT | SC02BT | SC02LT | Average
Preload (end) | 64 | 65 | 47 | 66 | 61
Overnight (end) | 63 | 65 | 45 | 66 | 60
Channel | SC04TT | SC04RT | SC04BT | SC04LT | Average
Preload (end) | 65 | 50 | 69 | 66 | 63
Overnight (end) | 65 | 50 | 68 | 65 | 62
Channel | SC07TT | SC07RT | SC07BT | SC02LT | Average
Preload (end) | 61 | 67 | 71 | 66 | 66
Overnight (end) | 60 | 67 | 71 | 65 | 66

## Slide 16: Magnet assembly and loading Specifications (coils)
For the pre-load targets at the end of the pre-load:
  The target average measured stress on coils, shells and rods at the end of the loading (after at least 24 h) shall be
    Coil (winding pole) average azimuthal stress: -80 ±8 MPa
Channel | CQ1T | CQ2T | CQ3T | CQ4T | Average
Preload (end) | -92 | -73 | -98 | -79 | -86
Overnight (end) | -93 | -72 | -98 | -80 | -86

## Slide 17: Magnet assembly and loading Specifications (coils)
For the maximum stress reached during the pre-load operations:
  During the entire pre-load operation, the maximum compression measured on each coil shall never exceed -120 MPa
Peak stress on coils (MPa)
CQ1 | CQ2 | CQ3 | CQ4
-110 | -91 | -120 | -100
CQ1-700 | CQ2-700 | CQ3-700 | CQ4-700 | CQ1-1900 | CQ2-1900 | CQ3-1900 | CQ4-1900 | CQ1-3800 | CQ2-3800 | CQ3-3800 | CQ4-3800
-86 | -89 | -98 | -83 | -88 | -129 | -121 | -103 | -83 | -93 | -94 | -70
Electrical SGs
FBGs

## Slide 18: How does A17 compare to the other magnets?

## Slide 19: How does A17 compare to the other magnets?
Straight section
LE
RE

## Slide 20: Appendix

## Slide 21: Impregnated coil dimensional tolerances Arc length excess (ends)
At 260 and 300 mm (for the lead end) and at 4340 and 4380 mm (for the return end) the absolute value of the coil delta arc-length must not exceed 210 mm.
  The coil delta arc-length is the difference between the coil arc length at each location in the ends and the average coil arc-length in the straight section.

## Slide 22: Only few coils have the measurements in the 260-300 mm positions, but all in the 207 mm position

## Slide 23: Only few coils have the measurements in the right position
Except for 1 coil (A17_237), the 207 mm position is a relatively good representation of the minimum of 260-300 mm positions
All included, the average difference is -0.021 mm (260-300 mm slightly smaller than 207 mm