## Slide 1: Main Injector / Recycler at The Nine
A.P. Schreckenberger 2024-06-14

## Slide 2: Beam to NuMI – The Weekly Summary

## Slide 3: MI Downtime – The Weekly Summary

## Slide 4: RR Downtime – The Weekly Summary

## Slide 5: Can I Get A Mid-Week Montage!? – Recap
Look at MI8 collimator losses on Monday morning
Wren continued his abort line tuning studies
  Established decent tunes for 8 and 10 GeV
    Still working on 9 GeV
Phil looked at impact of 8 GeV vertical tune on beam at the NuMI baffle
  Long tails must come from different mechanism
Cris has returned to us! And is already doing RR studies parasitically under the $E0

## Slide 6: Can I Get A Mid-Week Montage!? – Recap
Modulator swap in RF Station 14
MI-52 Pond Pump flow [I:52PF01] dropped under lower limit
  Strainers were cleaned on May 7th and the pond was treated
    ISD cleaned strainer again on June 12
    Took pump out of alarm state
  Heat exchanger cleaning??
I:S118AR Sump A went to zero
  Ops bypassed A and enabled alarms on Sump B [I:S118BR]

## Slide 7: T.G.I.F.
Strange readouts observed coming from RF Station 19
  Was operating, but Mid-level RF signals drove feedback mechanisms in unexpected ways
    Group B RF sum (I:VSMAGB) was reading artificially low
  RF experts swapped a cable, which yielded resolution
Vacuum issues developed when R:BV341 and R:BV401 closed unexpectedly
  Cold, frigid solder... ...broken links and shuttered valves... ...healed by an iron
  AKA, the joint was resoldered
R:IP6101 toggling alarm

## Slide 8: T.G.I.F.
I:LD6FP (longitudinal damper forward power) alarm
  Phil and Mitch guided ops through condition
MI-30 LCW Pump #3 had low suction pressure trip WedN
  Reset attempts by ops did not recover pump
  Able to run through the night
  Jesse installed a new pressure transducer, but discharge pressure got railed at 400 psig
    Tom Z called in to calibrate transducer / evaluate
    Another transducer installed – led to supply side pressure alarm
    Work continuing today
RF Station 13 tripped on shunt regulator overcurrent Have a fantastic Friday!