## Slide 1
RAL Remote Handling Mock-Up Area
Angus Mackley
(STFC Rutherford Appleton Laboratory)
LBNF Target Exchange System Technical Design Review 24-25 June 2024

## Slide 2: Presenter Background
Angus Mackley
Graduate Mechanical Engineer
High Power Targets Group at STFC
Started in September 2023
Notes: Would be very quick

## Slide 3: Presentation Outline
Mock-Up Area Overview
Horn A Mock-Up
  Brief, Features in Detail & Current Progress
Dummy Target
  Brief & Current Concept
Questions
Notes: Also quick, but gives an overview

## Slide 4: Mock-Up Area Overview
Offline test area for development of target remote handling equipment
Replica of important interfaces and components

## Slide 5: Mock-Up Area Overview
Dummy Target
Horn A Mock-Up
Target Exchange System

## Slide 6: Horn A Mock-Up – Brief
Represents the internal geometry of Horn A.
  Test target insertion with the TXS.
  Nominal clearance varies between 5.1mm and 12.1mm.
Recreate the interface connections.
  Target supports (red plate), also helium line connectors and instrumentation connections.
React mechanical loads introduced from TXS.
Axis | Required Accuracy (±)
X | 0.1mm
Y | 0.1mm
Z | 2mm
Roll | Minimal effect on thin parts
Pitch | 5.789° ± 0.5
Yaw | No affect as axisymmetric
Beamline (z)

## Slide 7: Horn A Mock-Up – Features in Detail
XY stages for initial alignment
Fiducial Points for alignment
Connecting Interfaces
Optimised Frame – Parametric FEA Study

## Slide 8: XY Adjustment Stages
Series of cross-sectional “profile” plates – work like XY stages.
Have adjustment in X and Y from M5 fine pitch screws.
Allow easy adjustment to meet tight positional tolerance.
Include fiducial locations for ISIS laser tracker.

## Slide 9: Horn A Mock-Up – Current Progress

## Slide 10: Dummy Target - Brief
Replicate the geometry and mass of the LBNF target and remote connections.
  Representative form (straightness) as LBNF target weldment
  Representative mass and COG
Replica of key interfaces (flexibly, when required).
  Target support
  TXS
  Instrumentation connections
  Helium cooling inlet/outlet connections
Requirement | Acceptable Range
Deflection (gravity sag) | 0.5mm
Form Accuracy | 0.5mm
Mass | 123kg ± 5%
CoG (X, Y, Z) | Nominal ± 10%

## Slide 11: Dummy Target - Concept
3D printed casing for form.
Attaches to TXS and bracketry in same way.
Stiff concentric aluminium in core structure.
Barbell for flexible mass attachment.
Potential to attach laser tracker at downstream end.

## Slide 12: Dummy Target – Mass Configurations
1 | Target Weldment | = | Dummy Target Weldment
2 | Green Plate | = | Green Plate
3 | Ring Bracket | = | Ring Bracket
4 | Suitter Clamps + Bracing | = | Mass A
5 | Alu Bracket + Tub | = | Mass B, C
6 | Hylen Device | = | Mass D
1
2
3
4
5
6
1
2
3
4
5
6
Each part on the real assembly has a “dummy” counterpart.
  Individually replicates their mass and CoG.
Can be replaced as real components are manufactured.
*Potential solution

## Slide 13: Dummy Target – Mass Configurations
Full Dummy
Instrumentation Connections
Instrumentation & Suitter
Suitter Clamps & Bracketry
Clamps not added for visibility