## Slide 1: Muon Campus Shutdown Report
Jim Morgan
Friday 09:00 Shutdown Meeting
July 26, 2024

## Slide 2: Muon Campus status
Study – Alternative M5 optics
Study – M1-M3 Optics
Transitioned into shutdown mode the week of 7/15
  LOTO performed by PESD and Ops Friday and Monday morning
  PESD performed additional LOTO steps on circuits with circuit breaker issues
  Wednesday morning, final Muon Campus enclosure reverted to Supervised Access
  Delivery Ring, Extraction and M4 Enclosures re-cored for shutdown keys
  Kickers and cooling skids shut off for the summer
Feeder 24 (Muon Campus) power outage Wed. 7/17 for feeder maintenance
  Ops recovered various controls crates and communication nodes after outage
  Ops recovered vacuum system, but BV510 would not open (later closed valves)
  Various water skids needed to be restarted after outage
Many tunnel jobs still need engineering or planning details to be completed
High voltage turned off for PWC’s and IC’s
Numerous LCW leaks, but mostly small (Overall leak rate <20Gal/Day)
Prepared for M4 Final Focus LQ fiducial changes due to power lead covers
AP-0 A/C work resumed on Tuesday and continued through week
  Requires access to AP-0 water cage and rad fence area

## Slide 3: M4 Final Focus quadrupoles in lower level
Plexiglass power lead covers
Covered fiducials

## Slide 4: Delivery Ring extraction region
Delivery Ring
M4 Line
Q205
Extraction Lambertson
Special vacuum pipe
Rad hard 8Q24
Extraction C-Magnet

## Slide 5: Upcoming work
Main worklist items
  Install rad hard 8Q24 at Q205, send uninstalled 8Q24 to TD for rad hard water lines
  Q205 vacuum pipe replacement to simplify vacuum connection to ELAM
  Unroll ELAM (was rolled 24 mr to improve g-2 extraction trajectory)
  Several alignment tasks including D30 level run and M4 Final Focus
  ESS1 and ESS2 septum stand motion-control improvements
  ESS fluorinert piping installation from AP-30 to tunnel
  M4 Final Focus vacuum installation
  ELAM downstream horizontal motion at limit before reaching nominal position
  Need to check sizing of all power supply panel breakers, upgrade as necessary
  Install additional steel shielding above ECMAG
  Repair Kirk Key hardware on disconnects
  AP-0 Dump system will be drained and water lines blown out
  Hope to finish operational ESS2 and install it in tunnel late in shutdown
ESS2 (operational version in A0 Clean Room)
  ESS2 cathode final polishing underway at vendor, should be picked up today
  If cathode hasn’t been warped in polishing process, will be installed in tank
AP-0 A/C controls work continues
Jerry gone after Monday, I’ll be main Muon Campus contact person next week