## Slide 1: ND/TMS magnet assembly
M.Oriunno Aug 14, 2024

## Slide 2: Baseline Configuration
AISI 1006 steel
  60 x 40 mm plates
  40 x 15 mm plates
  100 x 40 mm gap for detectors
  6 x rectangular coils
  ±1 T B field in the active area between the coils
Sub-System | Metric tons
Steel | 711
External Coil x 4 | 26 (6.5 ea)
Internal Coil x 2 | 16 (8 ea)
Support Frame | 35
Detectors | 20
Racks and Cables | 5
Total = 813 tons

## Slide 3: Coil Requirements
Same as CDR:
  1T minimum in the active area
  Expected max current required, 30 kA.turn
  Max temperature rise from ohmic dissipation shall be < 60oC (FPA 70, National Electric Code)
Change from the CDR:
  Installation of coils pre-assembled and tested at the factory

## Slide 4: Coil Design – MINOS with cold plates
Cold plate
Cold plate
Cooling circuit
Plank Design a-la MINOS
Preliminary studies show that a single cold plate (top or bottom), single-pass 3 gpm, with 5/8” pipe, meets the requirement of < 60oC
Cross section envelope of the coil package 246 mm x 288 mm (263mm)
3.5 m
7.2 m

## Slide 5: Steel Design – Changes from the CDR
CDR, 820 tons
PDR, 711 tons. ~ 13% mass saving from CDR
2
1
4
3
The single layer is made of four plates, previously 3, with identical width, spaced horizontally by a 20mm gap (flatbed truck width < 3.5 m)
Shorter steel length beyond the coils, outside the fiducial volume
Low reluctance links to return the B-Field. 20% mass reduction
Space between the coils increased to 3.6 m to accommodate the cassette detectors for an increased active area

## Slide 6: Steel/coil integration parameters
5
5. The Notches in the iron plate from the CDR have been converted to Vertical Slots for the insertion of the pre-assembled coils
6. Coil package at 20 mm gap from the steel for installation clearance. Need to study the effect of the gap on the leakage field
6
6

## Slide 7: Support Frame – no changes from the CDR
The total mass of the support frame is 35 tons, A36 steel
The parts will be lowered in the cavern with 3-4lift
The assembly is welded and bolted underground
Commissioning with the PRISM motion system, before the assembly of TMS starts
PRIMS: Hilman rollers on steel rails

## Slide 8: Magnetic isolation from the frame
The magnet is magnetically isolated from the frame by a bed of 4’x8’, 1.5” thick Aluminum tiles, to minimize local field distortion

## Slide 9: Magnetic Forces
Despite the B-field analysis have been benchmarked on the results of CDR, we have still discrepancies on the magnetic forces for the steel plates and the coils
Directions and value of the magnetic forces are required to dimension the joints and interconnections
We believe that the B-flux return links mitigate substantially the problem, decreasing the magnitude of the attractive forces between the coil and steel and between the steel plates
The two end plates, will experience anyway large forces along the beam direction. The mitigation of this effect remains to be addressed. It is not complex either

## Slide 10: Forces induced by B-field (CDR)
CDR studies, by V.Guarino et al.
25kN
5kN

## Slide 11: Installation of the Lower Coils
Coils mass, 6.5 and 8 tons each
The bed on the top of the support frame is equipped with Alu brackets, retraining the coils
Each coil segment is supported by six brackets
8 tons
6.5 tons

## Slide 12: Steel Plate installation
The steel plate deck will be assembled sequentially, backward along the beam, i.e. 40mm plates first
A temporary support structure holds the first group of plates
Each plate is < 3 tons

## Slide 13: Clamps/Spacer
A clamp/spacer is bolted to magnetic gap layer
It holds each plate to the support frame, reacting the magnetic forces
It set the gap between the plate along the beam direction
The clearance between the steel and coil is 20mm
  required to accommodate the shape tolerances of the plate (±.125”)
  Considered sufficient to keep the steel clear form the coil, when using a fine pitch crane hook

## Slide 14: Spacer/clamp details
40mm
40mm
38mm
M16

## Slide 15: B-flux return links
B-flux return link
M16 bolt
The flux return links are installed individually, on each layer, while advancing through the assembly of the steel

## Slide 16: Spacer/clamps & Upper coils supports
As the plate's assembly proceeds, additional spacers and support brackets for the upper coil are installed
Temporary supports
Upper coils bracket

## Slide 17: Before installation of the upper coils
The temporary support holding the first plates is removed, after a yet undefined number of plates has been secured to support frame
The full stack of 60 + 40 plates is completed, and it is ready for the installation of the upper coils

## Slide 18: Upper coils installation
The Three pre-tested coils are lowered individually and attached to the support brackets
Fine pitch crane hook required to stay inside the 20 mm clearance form the steel
Handling fixtures
8 tons
6.5 tons

## Slide 19: TMS ready for the Cassettes
U,V detectors
Y detectors

## Slide 20: Cranes availability and working area
15 US tons
50 US tons
15 US tons crane on surface and 50 US tons underground
Pre-staging area on surface is limited and overbooked
The capacity of the crane and the area on surface are the limiting factor for proceeding faster
~ 60 critical heavy lifts required to lower the magnet and the support frame
With these parameters, we are assuming a sequential procedure where the individual steel plates flow continuously from the storage area to the cavern, with minimal prep before the lift
All the staging and pre-assembly work must be done underground

## Slide 21: Underground Assembly area
TMS is assembled at center of the cavern in four different phases
Each phase duration is 3 months
Push-pull with ND/LAr

## Slide 22: TMS frame at the end of the cavern

## Slide 23: TMS magnet assembly area

## Slide 24: TMS envelope in the cavern
TMS
ND/LAr
During the installation the ND/LAr and the TMS envelope are staggered along the cavern
Critical points:
  The back of TMS is < 2 ft from the wall of the cavern
  Limited crane coverage close to wall. Special lift beam required
  At the nominal position on the beamline, TMS is at 1ft from ND/LAr
Crane access

## Slide 25: Steel procurement
Baseline with Steel AISI 1006
Two potential suppliers:
  We have a budgetary quote of April 2021 from Ryerson
  We added the option of Nucor, large still supplier in US. No quote yet, current cost estimation based on Steel price/lbs as market commodity.
Concern on the final tolerances achievable, affecting the design
  Ryerson claims ±.125” for the profile edges
  Nucor willing to quote for tighter ASTM A6 tolerances (see spare slides)
  Considering of post-processing the plate with Waterjet cutting, + $600k, with an external vendor
  Complex Logistic of moving 800 tons of steel from the vendor site to FERMILAB:
    3.5 m is the size limitation of the flatbed truck
    Expecting ~ 50 trips, no plans special transports
Supplier’s final selection will be based on a combination of scoring factors : cost, availability, final tolerances, logistic

## Slide 26: Toward the PDR
I did not cover the design of the mezzanine(s), hosting the power supplies and the electronic racks. They will be structural part of the support frame. We need to converge on cabling routing and quantity and the location of the rack to allocate sufficient area
I did not address the concerns on the air gap for the cassette installation. The actual 40mm may turn out to not be enough.
  Need to keep the cassette thickness envelope tight < 25 mm
  Work with Steel supplier to investigate if possibility of getting tighter ASTM A6 specs ( ½ or ¼) is real but also cost and schedule impact
  Or increase the gap from 40mm to 45 mm
Reach a sufficient level of confidence on the magnetic forces results from the FE analysis
Continue the development of the mechanical details of connections and interlinks
Waiting the outcome of the detectors size and coverage, for finalizing the dimensions of the steel plates before launching new Magnetic and Structural FEA

## Slide 27: Toward the PDR - II
Although adjustment of the vertical space between the coils( 3.2 vs 3.6 m) won’t change the mechanical concept, we need to converge on the values, since at the PDR we must present a consistent overview: agreement between the FEA and the mechanical design dimensions
Continue the mechanical, thermal and electrical design of the coil
Continue working with I&I on crane access, special tool requires, storage and staging areas both on surface and underground
Not visible, a lot of work in the background, to finalize PRISM : Task Force with I&I, ND/LAr and TMS (represented by me) to develop common solutions for the most efficient motion system and its integration with the support frame

## Slide 28: SPARE SLIDES
ASTMS A6 tolerances
Coil design
PRISM design
Images of the ND detectors underground

## Slide 29: ASTM A6 tolerances

## Slide 30: ASTM A6 Tolerances - Thickness
40 mm
15 mm
± 380 um
± 760 um

## Slide 31: ASTM 6 Tolerances – Length and Width
19 mm
25.4 mm
28.6 mm
31.9 mm

## Slide 32: Low Carbon - Flatness
40 mm
15 mm
± 25 mm
± 22 mm

## Slide 33: Supplementary Requirements Flattness
The following standardized supplementary requirements are for use when desired by the purchaser.
Those that are considered suitable for use with each material specification are listed in the
specification. Other tests may be performed by agreement between the supplier and the purchaser.
These additional requirements shall apply only when specified in the order, in which event the
specified tests shall be made by the manufacturer or processor before shipment of the material.
40 mm
15 mm
± 12.5 mm
± 11 mm

## Slide 34: Summary - ASTM 6
 | 15 mm | 40 mm
Thickness | ± 380 um | ± 760 um
Length | 19 mm | 28.6 mm
Width | 25.4 mm | 31.9 mm
Flatness | 25.4 | 22 mm
Enhanced Flatness | 12.5 mm | 11 mm

## Slide 35: MINOS Planks Stack
Electric contacts require careful engineering.
The problem has been solved for MINOS
Single planks made of multiple conductors
Stack of planks for each coil segment
Single plank

## Slide 36: Coil Cooling Circuit
17m
21m
17m
ID15mm, 10 gpm
DP= 0.1 bar/m

## Slide 37: PRISM req.s
Move TMS across the beam line over a distance of 30m in < 8hr, including detector ramping down/up. Speed ~ 1-2 mm/s
Task Force to develop a common solution for TMS and ND/LAr
  Powered Roller
  Boogie
  Rack and Pinion