## Slide 1
Tom Diehl (FNAL), Greg Rakness (FNAL)
Friday 9am AD meeting
02-Aug-2024
Mu2e report
https://indico.fnal.gov/event/65732/

## Slide 2: Infrastructure issues that need work (1/2)
Sump pumps redundancy needs to be improved
  Will make request to ISD to improve electrical redundancy
Mu2e “dry pit” collects water
  The dry pit is used to catch/contain any water leaks in the hall
  Muon PPD Ops to synthesize data, evolve plan for monitoring
Need additional monitoring of temperature and humidity
  PPD Process Controls to add remotely monitorable sensors
Extinction Monitor room is dank
  Need to keep air temperature away from dewpoint

## Slide 3: Infrastructure issues that need work (2/2)
Water on floor at bottom of stairwell
  The fix has been in process for > 1 year
Air compressor at MC1 is short cycling
  … due to internal leak?
Automatic Transfer Switch failed at MC1
  Failure occurred during Feeder 24 power outage
    This is the second time the ATS has failed since 2021…
  Need to understand this and the implications
Fire sprinklers in DAQ room
  Lesson learned from NOvA: sprinklers should be set at 2000F