Global Reconstruction Update
Peter Lane
Illinois Institute of Technology
MICE Collaboration Meeting 36

---
Outline
- Background/Prior Progress
- Current Progress
- Drift Reconstruction Results
- Conclusions
- Next Steps

---
Background:
Polynomial Transfer Maps
Simulated
Test Particles
B
B
A
B
B
Polynomial Transfer Maps
Test Particle
P.S.V. at Detectors
Expand initial P.S.V. (t, E, x, Px, y, Py) of test particles into terms of a polynomial: Ai = (1, t, ...., t^2, tE, ..., py^2)i
B are the matrices formed from the P.S.V. at detector centers
Solve the matrix equation B = A CT → CT = (AT A)-1 AT B
For N linearly independent inputs, N = # polynomial terms
C is a coefficient matrix for polynomials that describe the evolution of the phase space coordinates
Transport phase space vectors with b = C a

---
Background:
Track Fitting Algorithm
Beam Start Plane Phase Space Vector Guess
Actual
Detector Hits
(Inputs)
Find initial phase space vector that minimizes χ2 -- the sum of the squares of the differences between the propagated guesses (Outputs) and the detector hits (Inputs).
  - weighted by the detectors' measurement uncertainties
Propagated Guess
Phase Space Vectors

---
Progress Prior to CM36:
Initial Fitting Tests
Tested with moderate success on MC truth and smeared MC inputs
  - MC truth was a check on the fitting algorithm
  - Smeared MC simulated detector resolutions
  - Drift and single quad configurations
  - Verified the linear order transfer maps using COSY INFINITY transfer matrices
  - CM34 track fitting output residuals plots

---
Progress Prior to CM36:
Excerpt of CM34 Track Fitting Residual Plots
MC Truth
Smeared MC Truth

---
Progress Prior to CM36:
Framework and Data Structure
Developed software framework for plugging in different optics models and fitting algorithms
  - Optics models: models used for generating transfer maps
    - Polynomial Approx., Runge-Kutta
  - Fitting Algorithms: χ2 minimization, Kalman Filter
Created flexible, simple to use data structure capable of storing complicated triggers and event topologies if needed.

---
Current Progress
- Using reconstructed detector data
  (“space points”) instead of smeared MC for track fitting inputs
- Using the new global recon data structure
- Verified track fitting inputs using a drift configuration of TOF0 and TOF1
- Improved/fixed track fitting algorithm
- Compared track fit input (space points) residuals with output (reconstruction) residuals for a 1,000 particle run

---
2 m Drift: TOF0 to TOF1
beam starts 1 meter upstream of TOF0
2 meters between the
centers of TOF0 and TOF1
TOF1 Plane 0
(vertical slabs)
TOF0 Plane 0
(horizontal slabs)
TOF0 Plane 1
(vertical slabs)
TOF1 Plane 1
(horizontal slabs)
Initial distribution chosen to light up all TOF1 slabs.

---
Geometry and
Longitudinal Beam Definition
Fire 1000 muons 1m upstream of TOF0
  - No decays. Mean energy loss only. Air.
2m drift between centers of TOF0 and TOF1
  - 1.950 m of air in between two 25 mm thick TOF scintillator planes
Longitudinal Parameters:
  - Gaussian distribution in Energy and Pz
  - Mean Pz: 200. MeV/c (Mean E: ~226. MeV)
  - σp: 25 MeV/c (MAUS default)

---
Transverse Beam Definition
Transverse Parameters:
  - Gaussian x, Px, y, Py with means = 0
  - RMS Emittance (x & y): 0.1 π mmּ rad
  - β0 (x & y): 1000. mm / rad
  - α0 (x & y): 2.
Initial dist. chosen to light up all TOF1 slabs
  - σx = 10mm (arbitrary) and
  - 3·σx' (99.73% of the particles) = x'max = ∆x/∆z

---
Caveats for Residuals
- Residuals: difference of p.s.v. and MC truth
- MC hits are registered by Geant4 when they enter the scintillating slab volume (upstream edge of TOF plane)
  - Use only plane 1 hit since z is at the center of the detector (same as space point z)
Uncalibrated MC time stamps
  - MC t0 is beam creation
  - Space point t0 is calibrated trigger time
  - Slight offset in the mean of the input time residuals

---
Muon Drift Track Fitting Input
TOF reconstruction gives time and pixel (ID of horiz. & vert. slabs that were hit)
  - pixel gives rough x & y
Note: 8.5% reduction in particles from
  - Rejection of events with multiple plane hits (3.2%)
  - Hits on TOF pixels without valid trigger calibration (5.3%)
- Energy & momenta set to reference particle's since they are unknown
- Generate residuals with MC truth to verify inputs are sane

---
Muon Drift Track Fitting Output
- Using linear order polynomial transfer maps
- Generate best fit track points with MC truth

---
TOF 0 Input/Output Residuals 1
Input
Output
t res. = 55ps
x res. = 11.55 mm
y res. = 11.55 mm

---
TOF 0 Input/Output Residuals 2
Input
Output
E res. ≈ 8 MeV
Px res. ≈ 1 MeV/c
Py res. ≈ 1 MeV/c

---
TOF 1 Input/Output Residuals 1
Input
Output
t res. = 53ps
x res. = 17.32 mm
y res. = 17.32 mm

---
TOF 1 Input/Output Residuals 2
Input
Output
E res. ≈ 8 MeV
Px res. ≈ 1 MeV/c
Py res. ≈ 1 MeV/c

---
Conclusions
TOF inputs verified
  - Time residual RMS are within TOF resolution
  - Time residual mean offset is understood
  - x/y residual RMS are close to transverse spacial resolution of TOF0/TOF1 slabs
Drift track fitting working well
  - RMS are improved overall
    - E & P RMS are close to estimated resolutions
  - Energy mean is much better, but still significantly different from zero
    - t0 compensation seems to help

---
Next Steps
- Add TOF2
- Add magnets
  - quads (focusing)
  - solenoid (transverse momentum)
  - dipole (longitudinal momentum)
Add tracker stations
  - PID possible once reconstruction available
Add other materials (Ckov, absorber, etc...)

---
End

---
Extra Slides

---
Transfer Map Generation
Calculate C from matrix of polynomial vector inputs (A) and a matrix of p.s.v. outputs (B)
  - Solve the matrix equation B = A CT
- The Moore-Penrose Pseudoinverse of A is the least squares solution
- The MPP takes the simple form (AT A)-1 AT if there are N linearly independent inputs
  - N = number of polynomial terms