## Slide 1
Rob Ainsworth
PIP-2 Accelerator Physics Meeting
10 September 2024
RR/MI Beam Loss Budget

## Slide 2: Loss budget
Loss budget follows 1W/m
MI & RR share the same enclosure of length 3.3km
  Combined loss <3.3kW
Typically, 1W/m applies to areas we want hands on access and so collimators are excluded
  All loss (controlled and uncontrolled) are included in this budget
PIPII requirements
  75E12 @ 1.2s
MI can ramp at 1.067s so we will consider loss budget for 75E12 @ 1.067s

## Slide 3: Slip-stacking
Significant source of DC beam
Either sent to abort in RR if in Inj gap
Captured in MI collimator

## Slide 4: RR loss (current)
Loss separated into
  DC beam from slip-stacking that makes it way to injection gap sent to abort
  Beam loss to ring (including collimators)
Typical pulse (~50E12@1.067s)
  DC beam loss - 485 W
  Ring loss – 190 W

## Slide 5: PIPII changes
Intensity per pulse 50E12 -> 75E12
  DC beam loss - 485 W -> 728 W
  Ring loss - 190W -> 285 W
20 Hz booster means larger slip-stacking separation
  Simulations show DC beam expected to drop by factor of 3
  DC beam loss - 728 W -> 243 W

## Slide 6: Typical RR loss pattern
Injection
Extraction
To Muon
Abort
RR->MI
Transfer
Collimation
High loss
Location

## Slide 7: Loss increase is not linear

## Slide 8: Emittance with intensity
Cristhian Gonzalez Ortiz

## Slide 9: Space charge tune shift

## Slide 10: Resonance correction efforts

## Slide 11: Ring loss at PIP2
Current power loss is at current highest intensity
  Assume incoming beam quality will be no worse for PIP2 i.e. <20 pi mm mrad
  New MI8 collimators in injection line will help with tails
  Resonance correction efforts should mitigate space charge effects
Assume linear beam loss from 50E12 to 75E12

## Slide 12: Main Injector
MI is 98.5% efficient
  Lose 1.5% beam
1% beam loss due to DC beam from Slipstacking
  Captured in MI collimators @9 GeV
0.25% beam loss to transverse scraping
  Mostly at collimation @9 GeV
0.25% beam loss at transition crossing
  @ 21 GeV

## Slide 13: Beam Loss for PIP2
For 75E12, DC beam loss at 1% is 1012 W
  20 Hz will drop DC beam by factor of 3
  Power loss is 337 W
Ring loss at 0.25% is 253 W
Transition loss at 0.25% is 590 W
  Gamma-t jump is expected to reduce this loss
    On-going sims including realistic errors suggest at least a factor of 3 reduction -> 197 W

## Slide 14: Beam loss budget for MI/RR (3.3kW)
 | Machine | Momentum (GeV) | Current loss scaled to 75E12 (W) | Mitigation | Power loss (W)
DC beam from slip-stacking | RR | 8.835 | 728 | 1680 Hz separation due to 20 Hz booster | 243
Ring loss | RR | 8.835 | 285 | MI8 collimators, Resonance correction | 285
DC beam from slip-stacking | MI | 9 | 1012 | 1680 Hz separation due to 20 Hz booster | 337
Ring loss | MI | 9 | 253 |  | 253
Transition loss | MI | 21 | 590 | Gamma-t jump | 197
Total |  |  | 2868 |  | 1315