## Slide 1
S. Newbry 15 November 2024
TMS Steel Structure Design Update
Preliminary

## Slide 2: Outline
Steel structure overview
Requirements summary
Preliminary FEA Results

## Slide 3: Overview – Context

## Slide 4: Mass Breakdown
From CAD model
  Steel plates: 711T
  Coils: 77T
  Steel structure: 65T
  Cassettes: 50T
  Brackets (fasten steel plates and coils): 38T
  Aluminum baseplates: 11T
  Estimate for mezzanine and cabling: 13T
Total: 965T
  900T supported on steel structure

## Slide 5: Steel Structure Overview
Standard size tubing
  https://www.saginawpipe.com/ jumbo-tubing/
  Uprights: 22” square, .875” wall
  Long Crossbars: 24” x 12”, .5” wall
  Short upper crossbars: 16” x 12”, .5” wall
  Short lower crossbars: 12” x 12”, .5” wall
  Large diagonals: 12” x 12”, .5” wall
  Small diagonals: 8” x 8”, .5” wall
Standard size W-beams
  36” x 330 lb/ft

## Slide 6: Requirements Summary
“TMS Frame Requirements” draft document
  900T mass to be supported
  Steel: A992 (W-beams), A36 (Tubes)
  Design code: AISC Steel Construction
  Minimum factor of safety of 2 vs yielding
Load cases for FEA:
  1 gravity (normal operation)
  1 gravity + 160T lateral load (roller lateral sliding)

## Slide 7: FEA Setup – Remote Mass
900T mass of steel plates, coils, and detectors

## Slide 8: FEA Setup – Elastomer Pads
8 places, 20T/mm spring constant

## Slide 9: Load Case – 1G Vertical

## Slide 10: Deflection – 1G Vertical
~5mm compression of elastomer pads
~3mm bending of W-beams

## Slide 11: Stress – 1G Vertical
Maximum stress is below 125MPa limit for A36 steel

## Slide 12: Stress – 1G Vertical
Maximum stress appears to be a stress singularity

## Slide 13: Load Case – 1G + 160T lateral load
Lateral load applied to 4 feet

## Slide 14: Deflection – 1G + 160T lateral load

## Slide 15: Stress – 1G + 160T lateral load

## Slide 16: Stress – 1G + 160T lateral load
Rerun with smaller mesh in high stress area
Maximum stress is below 125MPa limit for A36 steel
Maximum stress appears to be a stress singularity

## Slide 17: Stress – 1G + 160T lateral load
Rerun with smaller mesh in high stress area
Maximum stress is below 125MPa limit for A36 steel
Maximum stress appears to be a stress singularity

## Slide 18: End
June 2024
November 2024