## Slide 1: MQXFA20 coil dimensions
P. Ferracin, Dan Cheng, Jennifer Doyle, Katherine Ray, Michael Solis
on behalf of the MQXF collaboration
MQXFA20 Coils Acceptance Review
December 12th, 2024
LBNL, Berkeley, CA, USA

## Slide 2
About 146 we remove 6 points, so, 146**
We plot both the pre-loading and post loading 142, checking if the straight section is different

## Slide 3: Outline
Data taking and processing
Impregnated coil dimensional tolerances
Results (straight section)
  Arc length excess
  Outer radius profile deviation
  Inner radial deviations (coil blocks)
  Inner radial deviations (pole)
  Key slot deviations
  Best-fit outer radius
Appendix

## Slide 4: Outline
Data taking and processing
Impregnated coil dimensional tolerances
Results (straight section)
  Arc length excess
  Outer radius profile deviation
  Inner radial deviations (coil blocks)
  Inner radial deviations (pole)
  Key slot deviations
  Best-fit outer radius
Appendix

## Slide 5: Data taking and processing
Leica System
  AT960 with T-Probe
Data processed using
  Spatial Analyzer

## Slide 6: Post processing
Each cross section is treated separately.
  Coils cross-sections are measured in 15 different locations along the coil length, from 70 mm close to the lead end to 4426 mm close to the return end.
  The 12 so-called straight section locations, where the pole key slot is present, are from 465 mm close to the lead end to 4310 mm close to the return end.
  The strain gauge is at location 3965 mm.

## Slide 7: Outline
Data taking and processing
Impregnated coil dimensional tolerances
Results (straight section)
  Arc length excess
  Outer radius profile deviation
  Inner radial deviations (coil blocks)
  Inner radial deviations (pole)
  Key slot deviations
  Best-fit outer radius
Appendix

## Slide 8: Impregnated coil dimensional tolerances (for series coils)

## Slide 9: Impregnated coil dimensional tolerances Arc length excess (straight section)
The impregnated coil is accepted for use in MQXFA if its arc length excesses along the straight section are within the following tolerances: +0.150/-0.250 mm
The arc length excess, which is difference between the measured coil arc length and the nominal one, is determined by fitting outer radius and mid-planes points with the nominal profile, with equal weighting and imposing as symmetrical the two mid-planes offsets. The sum of the two measured mid-plane offsets provides the arc length excess

## Slide 10: Impregnated coil dimensional tolerances Arc length excess (ends)
At 260 and 300 mm (for the lead end) and at 4340 and 4380 mm (for the return end) the absolute value of the coil delta arc-length must not exceed 210 mm.
  The coil delta arc-length is the difference between the coil arc length at each location in the ends and the average coil arc-length in the straight section.

## Slide 11: Impregnated coil dimensional tolerances Outer radius profile deviation
The impregnated coil is accepted for use in MQXFA if its outer radius profile deviations along the straight section are within the following tolerances: +0.200/-0.250 mm
The outer radius profile deviation, which is given by the variation of each point on the outer radius with respect to the nominal outer radius, is determined by fitting outer radius and mid-planes points with the nominal profile, with equal weighting and imposing as symmetrical the two mid-planes offsets. Positive deviation indicates more material than nominal, negative indicates less material than nominal.

## Slide 12: Impregnated coil dimensional tolerances “Coil blocks” inner radius profile deviation
The impregnated coil is accepted for use in MQXFA if its “coil blocks” inner radius profile deviations (E-F in next slide) along the straight section are within the following tolerances: +0.150/-0.250 mm
The “coil blocks” inner radius profile deviations, which is given by the variation of each point on the inner radius with respect to the nominal radius, is determined by fitting outer radius and mid-planes points with the nominal profile, with equal weighting and imposing as symmetrical the two mid-planes offsets. Positive deviation indicates more material than nominal, negative indicates less material than nominal.

## Slide 13: Impregnated coil dimensional tolerances

## Slide 14: Impregnated coil dimensional tolerances “Pole” inner radius profile deviation
The impregnated coil is accepted for use in MQXFA if its “pole” inner radius profile deviations (C-E and D-F in next slide) along the straight section are within the following tolerances: +0.000/-0.250 mm*
The “pole” inner radius profile deviations, which is given by the variation of each point on the inner radius with respect to the nominal radius, is determined by fitting outer radius and mid-planes points with the nominal profile, with equal weighting and imposing as symmetrical the two mid-planes offsets. Positive deviation indicates more material than nominal, negative indicates less material than nominal.

## Slide 15: Impregnated coil dimensional tolerances
* Cross-section measurements shall be taken close to all possible bumper locations. In addition, data shall be taken on the surface surrounding the pole holes where bumpers are inserted and projected on the closest measured cross-section.

## Slide 16: Impregnated coil dimensional tolerances Pole key slot mis-alignment
The impregnated coil is accepted for use in MQXFA if its pole key slot mis-alignment along the straight section are within the following tolerances: +0.250/-0.250 mm
The pole key slot mis-alignment, which is the misalignment of the center of the pole key slot with respect to the nominal position, is determined by fitting outer radius and mid-planes points with the nominal profile, with equal weighting and imposing as symmetrical the two mid-planes offsets.
  View from LE, positive shift towards left

## Slide 17: Best-fit outer radius
The best-fit outer radius is determined by best-fitting only the outer radius points.
No tolerance is specified
  Used to monitor coil-to-collar contact surfaces (“LQ effect”)

## Slide 18: Outline
Data taking and processing
Impregnated coil dimensional tolerances
Results (straight section)
  Arc length excess
  Delta arc length excess straight section - ends
  Outer radius profile deviation
  Inner radial deviations (coil blocks)
  Inner radial deviations (pole)
  Key slot deviations
  Best-fit outer radius
Appendix

## Slide 19: Arc length excess

## Slide 20: Impregnated coil dimensional tolerances Arc length excess (straight section)
The impregnated coil is accepted for use in MQXFA if its arc length excesses along the straight section are within the following tolerances: +0.150/-0.250 mm
The arc length excess, which is difference between the measured coil arc length and the nominal one, is determined by fitting outer radius and mid-planes points with the nominal profile, with equal weighting and imposing as symmetrical the two mid-planes offsets. The sum of the two measured mid-plane offsets provides the arc length excess

## Slide 21: Delamination in coil 146

## Slide 22: Observations
Xsec1065
Xsec1865
Xsec3465
Upon incoming inspection coil 146 was found to have significant delamination along the mid-plane.
Xsec1465
Xsec3065
Xsec2265

## Slide 23: Observations
Upon incoming inspection coil 146 was found to have significant delamination along the mid-plane.

## Slide 24: Arc length excess straight section

## Slide 25: Arc length excess straight section

## Slide 26: Arc length excess straight section
Conclusions
  The difference in arc length in the straight section between coil 146, coil 146* (where 3 data have been removed) and coil 146** (where 6 data have been removed) is
    From -0.195 mm (146) to -0.185 mm (146*) to -0.156 mm (146**)
      5 um per mid-plane (from 146 to 146*)
      15 um per mid-plane (from 146 to 146**)
  So the maxim difference between the 3 mid-plane shim (per side) would be 20 um
Action items
  The coils will be shimmed on the mid-plane to compensate

## Slide 27: All coils

## Slide 28: Arc length excess straight section

## Slide 29: Arc length excess straight section

## Slide 30: Arc length excess straight section
Conclusions
  Coils 125, 254 with several points out of spec
Action items
  The coils will be shimmed on the mid-plane to compensate

## Slide 31: Outline
Data taking and processing
Impregnated coil dimensional tolerances
Results (straight section)
  Arc length excess
  Delta arc length excess straight section - ends
  Outer radius profile deviation
  Inner radial deviations (coil blocks)
  Inner radial deviations (pole)
  Key slot deviations
  Best-fit outer radius
Appendix

## Slide 32: Impregnated coil dimensional tolerances Arc length excess (ends)
At 260 and 300 mm (for the lead end) and at 4340 and 4380 mm (for the return end) the absolute value of the coil delta arc-length must not exceed 210 mm.
  The coil delta arc-length is the difference between the coil arc length at each location in the ends and the average coil arc-length in the straight section.

## Slide 33: Arc length excess full length

## Slide 34: Arc length excess LE

## Slide 35: Arc length excess RE

## Slide 36: Delta between arc length excess straight section and spacer-wedge transition
Red & dark blue markers: measured at 207 mm and 4426 mm
Orange & light blue markers: measured at 260-300 mm and 4340-4380 mm

## Slide 37: Delta between arc length excess straight section and spacer-wedge transition
The “min 260-300 mm is in average 0.035 mm smaller than the 207 mm value

## Slide 38: Delta arc length excess straight section - ends
Conclusions
  Coils 125, 146, 254 are out of spec
Action items
  “If Delta arc-length is slightly above 210 um, disposition may be to set minimum magnet preload > 80+ MPa”
  TLS will be used in the LE

## Slide 39: Outline
Data taking and processing
Impregnated coil dimensional tolerances
Results (straight section)
  Arc length excess
  Delta arc length excess straight section - ends
  Outer radius profile deviation
  Inner radial deviations (coil blocks)
  Inner radial deviations (pole)
  Key slot deviations
  Best-fit outer radius
Appendix

## Slide 40: Outer radius profile deviation

## Slide 41: Impregnated coil dimensional tolerances Outer radius profile deviation
The impregnated coil is accepted for use in MQXFA if its outer radius profile deviations along the straight section are within the following tolerances: +0.200/-0.250 mm
The outer radius profile deviation, which is given by the variation of each point on the outer radius with respect to the nominal outer radius, is determined by fitting outer radius and mid-planes points with the nominal profile, with equal weighting and imposing as symmetrical the two mid-planes offsets. Positive deviation indicates more material than nominal, negative indicates less material than nominal.

## Slide 42: Outer radius profile deviations straight section (min-max)

## Slide 43: Outer radius profile deviations straight section

## Slide 44: Outer radius profile deviations straight section
Conclusions
  All coils within spec
Action items
  No action items

## Slide 45: Outline
Data taking and processing
Impregnated coil dimensional tolerances
Results (straight section)
  Arc length excess
  Delta arc length excess straight section - ends
  Outer radius profile deviation
  Inner radial deviations (coil blocks)
  Inner radial deviations (pole)
  Key slot deviations
  Best-fit outer radius
Appendix

## Slide 46: Inner radial deviations (coil blocks)

## Slide 47: Impregnated coil dimensional tolerances “Coil blocks” inner radius profile deviation
The impregnated coil is accepted for use in MQXFA if its “coil blocks” inner radius profile deviations (E-F in next slide) along the straight section are within the following tolerances: +0.150/-0.250 mm
The “coil blocks” inner radius profile deviations, which is given by the variation of each point on the inner radius with respect to the nominal radius, is determined by fitting outer radius and mid-planes points with the nominal profile, with equal weighting and imposing as symmetrical the two mid-planes offsets. Positive deviation indicates more material than nominal, negative indicates less material than nominal.

## Slide 48: Coil blocks inner radial deviations straight section (min-max)

## Slide 49: Coil blocks inner radial deviations straight section

## Slide 50: Coil blocks inner radial deviations straight section
Conclusions
  All coils in spec
Action items
  No action items

## Slide 51: Outline
Data taking and processing
Impregnated coil dimensional tolerances
Results (straight section)
  Arc length excess
  Delta arc length excess straight section - ends
  Outer radius profile deviation
  Inner radial deviations (coil blocks)
  Inner radial deviations (pole)
  Key slot deviations
  Best-fit outer radius
Appendix

## Slide 52: Inner radial deviations (pole)

## Slide 53: Impregnated coil dimensional tolerances “Pole” inner radius profile deviation
The impregnated coil is accepted for use in MQXFA if its “pole” inner radius profile deviations (C-E and D-F in next slide) along the straight section are within the following tolerances: +0.000/-0.250 mm*
The “pole” inner radius profile deviations, which is given by the variation of each point on the inner radius with respect to the nominal radius, is determined by fitting outer radius and mid-planes points with the nominal profile, with equal weighting and imposing as symmetrical the two mid-planes offsets. Positive deviation indicates more material than nominal, negative indicates less material than nominal.

## Slide 54: Pole inner radial deviations straight section (min-max)

## Slide 55: Pole inner radial deviations straight section

## Slide 56: Pole inner radial deviations straight section
Conclusions
  Several out of spec positions, in all coils,
    Coil bumper thickness to be corrected to compensate
Action items
    Coil bumper thickness to be corrected to compensate

## Slide 57: Outline
Data taking and processing
Impregnated coil dimensional tolerances
Results (straight section)
  Arc length excess
  Delta arc length excess straight section - ends
  Outer radius profile deviation
  Inner radial deviations (coil blocks)
  Inner radial deviations (pole)
  Key slot deviations
  Best-fit outer radius
Appendix

## Slide 58: Key slot deviations*
  *View from LE, positive shift towards left

## Slide 59: Impregnated coil dimensional tolerances Pole key slot mis-alignment
The impregnated coil is accepted for use in MQXFA if its pole key slot mis-alignment along the straight section are within the following tolerances: +0.250/-0.250 mm
The pole key slot mis-alignment, which is the misalignment of the center of the pole key slot with respect to the nominal position, is determined by fitting outer radius and mid-planes points with the nominal profile, with equal weighting and imposing as symmetrical the two mid-planes offsets.
  View from LE, positive shift towards left

## Slide 60: Key slot deviations

## Slide 61: Key slot deviations

## Slide 62: Key slot deviations
Conclusions
  No coils out of spec
*See LBNL note and Record of Decision in Docdb-2844

## Slide 63: Outline
Data taking and processing
Impregnated coil dimensional tolerances
Results (straight section)
  Arc length excess
  Delta arc length excess straight section - ends
  Outer radius profile deviation
  Inner radial deviations (coil blocks)
  Inner radial deviations (pole)
  Key slot deviations
  Best-fit outer radius
Appendix

## Slide 64: Best-fit outer radius
The best-fit outer radius is determined by best-fitting only the outer radius points.
No tolerance is specified
  Used to monitor coil-to-collar contact surfaces (“LQ effect”)

## Slide 65: Best-fit outer radius deviations

## Slide 66: Best-fit outer radius deviations

## Slide 67: Best-fit outer radius deviations
Conclusions
  Data consistent with previous magnets

## Slide 68: Out of specs
Arc length excess
  Coils 125, 254 with several points out of spec
    The coils will be shimmed on the mid-plane to compensate
Delta arc length excess straight section – ends
  Coils 125, 146, 254 are out of spec
    “If Delta arc-length is slightly above 210 um, disposition may be to set minimum magnet preload > 80+ MPa”
    TLS will be used in the LE
Outer radius profile deviation
  All coils within spec
Inner radial deviations (coil blocks)
  All coils within spec
Inner radial deviations (pole)
  Several out of spec positions, in all coils,
    Coil bumper thickness to be corrected to compensate
Key slot deviations
  All coils within spec
Best-fit outer radius deviations
  Data consistent with previous magnets

## Slide 69: Outline
Data taking and processing
Impregnated coil dimensional tolerances
Results (straight section)
  Arc length excess
  Delta arc length excess straight section - ends
  Outer radius profile deviation
  Inner radial deviations (coil blocks)
  Inner radial deviations (pole)
  Key slot deviations
  Best-fit outer radius
Appendix

## Slide 70: Appendix

## Slide 71: 142 pre and post loading

## Slide 72: 142 pre and post loading

## Slide 73: 142 pre and post loading
Conclusions
  The difference in arc length in the straight section between coil 142_pre-loading and coil 142_post- loading is
    From -0.238 (142_pre-loading) to -0.094 (142_post-loading)

## Slide 74: 248 Operator I vs II (old tip)
Ave ss: -0.007 mm
Delta LE: -0.168 mm
Ave ss: +0.009 mm
Delta LE: -0.180 mm

## Slide 75: 248 Operator I vs II (new tip)
Ave ss: -0.007 mm
Delta LE: -0.168 mm
Ave ss: -0.004 mm
Delta LE: -0.195 mm

## Slide 76: 244 vs 248 I vs 248 II (old) vs 248 II (new)
Average ss after mid-plane shimming:
  -0004 vs -0.007 vs +0.009 vs -0.007 um
Average delta LE-ss after mid-plane shimming: -0.230 vs -0.168 vs -0.180 vs -0.195 um

## Slide 77: Measurements repeated 3 times

## Slide 78: Comparison FNAL-LBNL

## Slide 79: Comparison FNAL-LBNL