## Slide 1: 302.4.01 Magnets Vertical Test at BNL Weekly Status
Febin Kurian
02-Dec-2024

## Slide 2: MQXFA12b
Cooldown– started on 19th Nov.
Magnet reached 4.5K on 22nd Nov.
Spontaneous quench test started: Nov-26
Trip#1: IQ =14732 A, QI= 26.62 Miits (trips on the coil difference)
Quench#1: IQ =15283 A on Q3(Coil 225), QI= 26.03 Miits, Quench Location: 0.06 m from center towards LE
Quench#2: IQ =15783 A on Q3(Coil 225),
QI= 26.46 Miits, Quench Location: 0.91 m from center towards LE

## Slide 3: Second Top Hat Repair
  Heaters: All Passed Hi Pot
  V-taps:
    Passed: VT1, VT2, VT3, VT4, VT6
    Failed: VT5

## Slide 4: CRYOGENIC STATUS
CTI 4000 system status
  Running
Linde 1610 system status
  Running
Small delay in the morning due to Nash pump trip