## Slide 1
Proposed Smart Network R&D Investigations for ProtoDUNE NP02
Michael Wang (Jim Kowalkowski, Nik Sultana, and Wes Ketchum)
DUNE DAQ DS/PP Meeting
December 12, 2024

## Slide 2: Introduction
Smart networking technology (smart NICs in particular) emerged in the past decade in response to the ever-widening gap between network port speeds and the ability of CPUs to keep up with it
Their potential for HEP-DAQ applications has been recognized and investigated. See Roland’s talk: Evaluation of SmartNIC devices for use in Trigger and Data Acquisition Systems
Rapid development in this field resulting in enhanced hardware capabilities combined with significantly improved software programmability, warrants a fresh and closer investigation of how this technology can benefit DUNE’s DAQ system.
We propose looking at the following two technologies for DUNE:
  Smart P4-programmable network switches
  High performance smart NICs with DMA capability to accelerators (e.g. GPUs) programmable through high-level but efficient APIs

## Slide 3: Smart switch demo
Explore feasibility of replacing DUNE DAQ readout switches (between WIBs and RUs) with smart network switches in order to offload compute-intensive tasks like the TPG:
  Implement TPG algorithm using P4 (Programming Protocol-independent Packet Processors) network programming language for execution on the smart switch’s programmable ASIC
    We have a preliminary P4 implementation of the TPG tested using the BMv2 P4 switch simulator
  Test in real-world environment of NP02 ProtoDUNE to demonstrate proof-of-concept
  Use Caswell CAR-5056 programmable switch available at FNAL
    Can ship to CERN and install at NP02

## Slide 4: Prototype P4 Implementation of TPG
TPG algorithm in P4
Prototype developed by Nik Sultana (CS Dept., Illinois Institute of Technology)
References:
  S. Patel, R. Atsatsang, K. M. Tichauer, M. H. L. S. Wang, J. B. Kowalkowski, and N. Sultana, “In-network fractional calculations using P4 for scientific computing workloads,” in Proceedings of the 5th International Workshop on P4 in Europe, ser. EuroP4 ’22.
  N. Sultana, M. Wang, & J. Kowalkowski. “In-network DAQ functions”. Presentation at In situ processing for real time MMA in DUNE, Feb. 2023.

## Slide 5: Smart switch demo
smart readout switches
startTime
timeAboveThreshold
Trigger Primitive (TP)
Integral = charge
TP
stream
TP
stream
TP
stream
TP
stream
TP
stream

## Slide 6: Test platform for smart switch demo
Programmable smart network switch
Perform real time ML-based ROI finding
and signal processing on the FPGAs
Offload computationally-intensive data
processing tasks like the trigger primitive
generation algorithm to the P4-programmable ASIC
Caswell CAR-5056

## Slide 7: Smart NIC+GPU demo
Explore feasibility of replacing NICs on DUNE DAQ RUs with smart NICs
  To offload packet processing from CPU
  Perform new processing capabilities enabled by these NICs
    DMA transfers into GPU memory to perform online real-time AI inference
Test application: EmTrkMichelId ML model found in LArSoft for classifying LArTPC hits as tracklike, shower-like, or Michel electron-like
Hardware platform: Nvidia’s ConnectX series smart NICs and discrete GPU
  Nvidia IGX Orin Edge AI computing platform (with ConnectX 7 NIC and RTX A6000 GPU)
  Note: not proposing to replace DUNE RU with this platform. Goal is to investigate ConnectX NIC+discrete GPU available on IGX platform. If idea is feasible, ConnectX NICs also available as PCIe cards that can be used in existing DUNE RUs
Software platform: Nvidia’s HoloScan sensor processing software framework that abstracts away lower-level tools like DPDK

## Slide 8: Test app for Smart NIC+GPU demo: Real time AI inference with raw data
48
48
Michel electron
Track
Shower
Convolutional neural network-based classifier
48x48 pixel input images
Convolutional layer using 48 5x5 filters
1st fully connected layer with 128 neurons
2nd fully connected layer with 32 neurons
11.9 M parameters
time
wire
view of a LArTPC plane
EmTrkMichelId

## Slide 9: Test platform for Smart NIC+GPU demo: Nvidia IGX Orin
Data stream
from detector
Integrated smart-NIC unpacks
ethernet frames and writes directly into
GPU memory without CPU intervention
Discrete GPU performs inference in real time to
identify signals & reject radiological backgrounds
Low power CPU cores
with integrated GPU
Inference
results

## Slide 10: ProtoDUNE schedule

## Slide 11
Thank you!