## Slide 1: Linac Operations Report
Linac studies
  Longitudinal drift compensation
Beam output: Source: 54.5 mA
TO1IN: 27.8mA
D7TOR: 25.6 mA
Efficiency: 92 %
Monday
  KRF5 trips
    Klystron Collector H2O flow trips
      Replaced flow meter
      Cleaned filter strainer
    Filament low trips
      Raised filament voltage
Thursday
  KRF1 CS ignitron status trips
    Replaced ignitron firing circuit
Klystron Vernier cavity regulation problems persist, able to run in manual for now