## Slide 1: Protons in IOTA
1st ASTA User Meeting
Moses Chung/APC
With many inputs from
V. Shiltsev, A. Valishev, G. Stancari, S. Nagaitsev,
V. Scarpine, B. Hanna, J. Steimel

## Slide 2
Protons in IOTA: Stage III

## Slide 3
Protons in IOTA: Why?
Nonlinear integrable optics needs to be tested with beams with space-charge
Beam halo suppression by nonlinear integrable optics should be verified
Dedicated study on space-charge compensation using electron column is possible
Suppression of e-p instability in nonlinear lattice can be investigated
+ Many more ideas are welcome !

## Slide 4
Protons in IOTA: Basic requirements
1. Range of magnetic rigidity:
2. Availability of the proton beam:
Ion source, LEBT, and RFQ of the HINS program will be reused as a proton injector for the IOTA ring with an energy of 2.5 MeV and a nominal current of 8 mA
3. Non-negligible space-charge:

## Slide 5
Proton beam parameters from HINS:
~2.0 pi-mm-mrad vertical
~1.6 pi-mm-mrad horizonal
Estimated momentum spread
By Eliana Gianfelice-Wendt
By Vic Scarpine
Bunch width ~ 2 x 0.3 ns
(from fast Faraday cup by Vic)
Water-leak
for RFQ

## Slide 6
Part 1: Ion source + LEBT + RFQ + Beamline + Diagnostics
Part 2:
Klystron + Circulator
+ waveguides
(2MW 325 MHz)
Part 3:
Charging supply
+ modulator
+ pulse transformer
Current configuration of HINS at MDB

## Slide 7
HINS Beamline components
~ 4.7 m
dump
No 6 cavity for ITOA injection

## Slide 8
Circulator
Waveguide components
HINS RF components
Charging supply
2nd Kylstron has arrived from Toshiba (input from Jim Steimel)

## Slide 9
5 MW
for gun
2 x 0.3 MW
for CC1&2
5 MW for CM1  will eventually be superseded by
a 10 MW multi-beam klystron system to drive the 3 CM string.
Space to relocate HINS front end and RF system
Possible location
of the HINS front end
We may relocate whole HINS RF system
Or
Only relocate 325 MHz Klystron and
reuse (or share) modulator system
~ 36 m

## Slide 10
7.9 m
~5 m
Beam line for diagnostics
kicker
Possible configuration 1:
Single-turn injection of proton Some emittance growth and needs gap
Co-direction of electron injection  need to change dipole polarity
1.52 m

## Slide 11
Possible configuration 2:
Single-turn injection of proton Some emittance growth and needs gap
Counter-direction of electron injection  need to reroute beamline
~5 m

## Slide 12
Example of an experiment with proton
: Space-Charge Compensation
Electrons are created by beam-induced rest gas ionization, and confined by solenoid and electrodes  Gas focusing + Penning trap
How to maintain the stability of the beam-plasma system ?
(beam: e-p instability, plasma: radial expansion or growth of diocotron mode)
Proton beam shape
~ Trapped electron profile
Electron generation
by rest-gas ionization
1m
0.5 T

## Slide 13: IOTA proton-beam: better than Novosibirsk PSR
2.5 MeV
7000 G
5 cm
~5 m
up to 1000 µsec
0.2; 1 Hz
up to 8+ mA
0.56 MHz
Synergy with e-column
and nonlinear magnet
G. I. DIMOV and V. E. CHUPRIYANOV (1983)
Betatron tune = 3 ~ 5

## Slide 14: Conclusion
The combination of the IOTA ring with the HINS front-end will be a great asset to the advanced accelerator R&D community, in particular for the Intensity Frontier.
So far, we see no immediate technical show-stopper to inject a 2.5 MeV proton beam into the IOTA ring. But we need to investigate technical details with local experts and outside users.