## Slide 1: Beam Manipulation for Future Hard X-Ray FELs (that could be tested at ASTA)
John W. Lewellen
Quinn Marksteiner
Nikolai Yampolsky
AOT-HPE
24 July 2013

## Slide 2: Acknowledgements
Philippe Piot and FNAL colleagues and hosts (so you know who to blame if we’re late getting to lunch today…)
Colleagues at LANL – Petr Anisimov, Ron Barber, Bruce Carlsten, Pat Colestock, Leanne Duffy, Henry Freund, Frank Krawczyk, Steve Russell, Larry Rybarsik, Rich Sheffield
Collaboration with SLAC on structure and klystron design choices
Discussions with colleagues at LBNL
Michael Borland and Bob Soliday

## Slide 3: The Plan (subject to change)
MaRIE 1.0 baseline parameters
Issues with the baseline design
Some approaches for mitigating known issues:
  ESASE
  Deflector cavity chirp control

## Slide 4: For more information about MaRIE’s science missions:
MaRIE.lanl.gov
From here on, when I say “MaRIE” or “MaRIE LINAC” I mean the driver electron linac for the X-FEL

## Slide 5: What are the baseline assumptions and requirements?
Beam parameters for lasing
  12 GV beam energy
  100 pC bunch charge
  12 fs bunch duration
  3.4 kA peak current
  0.015% energy spread
  0.2 um rms emittance
LINAC parameters
  2.856 GHz operating frequency
  25 MV/m accelerating gradient
  10:1 compression ratio, BC1
  25:1 compression ratio, BC2
  1.5 us RF pulse duration
Other requirements
  Multiple bunches per RF macropulse
  2-nC bunches interleaved for radiography
  7-15
  150
  >50
  1-3
  0.01%
  > 0.3
“LCLS-like”

## Slide 6: What does the MaRIE LINAC look like?
300 fs (rms)
12 fs (rms)
12 GeV, < 0.2 um, <0.015%
3 ps (rms), 250 MeV
Introduce residual dispersion for LSC control

## Slide 7: Questions ASTA can Help Answer – Baseline Design
How effective is the residual-dispersion technique at ameliorating LSC?
hx (m)
d
No dispersion
With dispersion
Long. phase space @ 12 GeV
Dispersion along MaRIE linac

## Slide 8: Baseline Design Bottom Line
We think we can get these parameters using a more-or-less conventional design.
That said … it ain’t pretty.
  Large correlated energy spread from CSR mitigation techniques
  Residual dispersion in lattice from LSC mitigation techniques
Alternate techniques to avoid some of the problems in the first place:
  laser prebunching (ESASE) (Quinn Marksteiner) and
  deflectors for chirp control (Nikolai Yampolsky)

## Slide 9: Introduction to ESASE (laser bunching)
Conventional approach: bunch to ~12 fs / 3 kA, boost energy, lase
Problems: CSR, LSC; resistive wake in undulator
ESASE approach: bunch to ~ 70 fs / 600 A (reduced CSR), modulate,
boost energy, make small bunches @ 3-6 kA, lase
A. A. Zholents, Phys. Rev. ST Accel. Beams 8, 040701 (2005).

## Slide 10: Slippage effects in undulator
Total slippage between x-rays and electrons is ~ 30 nm
 Each small bunch can lase as a “long bunch”
Downside: half of the electrons are outside current peaks

## Slide 11: Microbunches help with resistive wake effects
DE(s) with conv. bunch
DE(s) with laser bunching

## Slide 12: Questions ASTA can Help Answer - ESASE
Does modulation survive acceleration? and
Are CSR models correct / adequate for the microbunches?
  Use laser modulator after 1 accelerator section, with chicane at end
  Use OTR diagnostics to characterize bunching
  Measure growth in emittance and energy spread from CSR
Are our space charge models correct?
  Use laser modulator and chicane after 1 accelerator section
  Measure growth in energy spread after 2nd and 3rd sections
How much does adding laser harmonics help with modulation?
  Modify laser modulator to use multifrequency modulation
  Measure results after acceleration

## Slide 13: Chirp Control with Deflector Cavities
z
x
Angular kicks depending on z-position
z
x
Opposite angular kicks depending on z-position.
Energy change depending on transverse position
z
x
Angular kicks to compensate the z-dependent focusing
Deflector cavities deliver longitudinal as well as transverse kicks:
Transverse kick depends on arrival time
Longitudinal kick depends on transverse position
Notes: Use transverse deflecting cavity (TDC) to change beam energy depending on its transverse position. Strong correlation between the transverse and longitudinal positions can be created with another TDC and vacuum drift.
Resulting value of the energy chirp is determined by the transverse beam size (can be made large through increasing drifts) in the middle rather than longitudinal beam size.

## Slide 14: Deflector-Based Chirp Control – 1st Order
Large compressing energy slew can be imposed if long drifts between the cavities are used
x-z matrix for a single deflecting cavity
x-z matrix for beamline

## Slide 15: Early Simulations with elegant
Typical parameters:
Beam energy 250 MeV
Emittance (normalized) 0.15 mm-mrad
bx,y 120 m
Bunch length (rms) 90 m
Erms 25 keV
RF frequency 2.85 GHz
RF gradient 22 MV/m
Cavity length 0.4 m
Drifts length 5 m
Echirp 1 MeV
Emittance growth 10 %
Energy spread growth 1 %
Increase of the 6D phase space volume vs the imposed energy chirp
Degradation check done at S-band and X-band; no optimization or nonlinear elements applied yet.

## Slide 16: Questions ASTA can Help Answer – Deflector-Based Chirp Control
Is this an effective method for controlling the chirp on a beam?
How linear is the chirp? Can we apply a nonlinear chirp?
Can we compensate the nonlinearities driving emittance growth?
  Verify scaling of emittance growth with applied chirp
  Characterize nonlinearities

## Slide 17: Closing Comments
The MaRIE X-FEL is a challenging design
Baseline design, as it stands, has very little margin for error
We are actively investigating – and seeking – ways to increase that margin, both within “typical” design space and with new ideas
ASTA provides an excellent platform for answering questions from both realms

## Slide 18: Backup slides follow
Double-reversed chicane geometry
Dispersion in lattice
Bunch after BC2 @ 1 GeV
SASE-ESASE comparisons
Effects of space charge

## Slide 19: CSR & LSC mitigation strategies:
Go to lower R56, smaller bends, longer drifts; under-compress; adjust focusing; use wakes to help remove residual energy spread
Go to a double reversed chicane to help reduce the “chevron”:
Introduce residual dispersion in the lattice to help “smear” out LSC (offset the last leg of the first compressor)

## Slide 20: In practice, what are we doing?
Extend the last leg on the last BC1 compressor, changing the bend angle to keep the same net R56
BC1
BC2
hx (m)

## Slide 21: After BC2 compressor (at 1 GeV)

## Slide 22: SASE vs. ESASE

## Slide 23: Effects of space charge – why we modulate at 12 GeV