## Slide 1: IOTA – Integrable Optics Test Accelerator Sergei Nagaitsev ASTA Users Meeting July 23-24, 2013

## Slide 2: ASTA : Downstream part (now)
beam dump
IOTA

## Slide 3
Experimental Proposals at IOTA Storage Ring
Integrable Optics Test (electrons and protons)
Optical Stochastic Cooling Experiment (electrons)
Space Charge Compensation in High Intensity Circular Accelerators (protons)
Electron Wave Function Size Measurements in IOTA Ring (electrons)

## Slide 4: IOTA at a glance
Parameter | Value | Unit
Circumference | 38.7 | m
Bending dipole field | 0.7 | T
RF voltage | 50 | kV
Electron beam energy | < 150 | MeV
Number of electrons | 2 109 | 
Transv. emittance r.m.s. norm | 2 | π m
Proton beam energy | 2.5 | MeV
Proton beam momentum | 70 | MeV/c
Number of protons | 8 1010 | 
Transv. emittance r.m.s. norm | 0.2 | π m

## Slide 5: Integrable Optics Test: Motivation
The main feature of all present accelerators – linear focusing lattice: particles have nearly identical betatron frequencies (tunes) by design.
  Hamiltonian has explicit time dependence
  All nonlinearities (both magnet imperfections and specially introduced) are perturbations and make single particle motion unstable due to resonant conditions
Stability depends on initial conditions
  Regular trajectories for small amplitudes
  Resonant islands (for larger amplitudes)
  Chaos and loss of stability (for large amplitudes)

## Slide 6: Consequences of linear focusing
Single-particle losses
  Losses are result of unstable particle dynamics under perturbations (magnetic fields, space-charge forces, beam-beam forces)
  All high intensity accelerators are beam-power-limited by losses (rings, cyclotrons, linacs)
Instabilities
  Instabilities are intrinsic to the way we build accelerators now – linear optics

## Slide 7
Report at HEAC 1971
Landau damping
Landau damping – the beam’s “immune system”. It is related to the spread of betatron oscillation frequencies. The larger the spread, the more stable the beam is against collective instabilities.
  The spread is achieved by adding special magnets -- octupoles
External damping (feed-back) system – presently the most commonly used mechanism to keep the beam stable.

## Slide 8: Does Focusing Need to be Linear?
Are there “magic” nonlinearities with zero resonance strength?
The answer is – yes (we call them “integrable”)
Search for a lattice design that is strongly nonlinear yet stable
  Orlov (1963) -- attempt failed (non-integrable)
  McMillan (1967) – first successfull 1-D example
  Perevedentsev, Danilov (1990 - 1995) – several 1D, 2D examples
  Cary and colleagues (1994) – approximate integrability
Our goal (with IOTA) is to create practical nonlinear accelerator focusing systems with a large frequency spread and stable particle motion.
  Danilov, Nagaitsev, Phys. Rev. ST Accel. Beams 13, 084002 (2010)

## Slide 9: Ideal Penning trap
An ideal Penning trap is a LINEAR and integrable system
  It is a harmonic 3-d oscillator

## Slide 10: Kepler problem – a nonlinear integrable system
Kepler problem:
In spherical coordinates:
Example of this system: the Solar system

## Slide 11: A roadmap to high-intensity rings
Develop the theoretical basis of beam instabilities with strong space charge in a highly-nonlinear focusing system
  What betatron frequency spread is required to make the beam stable?
Develop highly-nonlinear focusing lattices and elements with reduced chaos
  Reduce chaos in beam-beam effects
Ultimately, develop accelerators for super-high beam intensity
  Self-consistent or compensated space-charge
  Strong non-linearity (for Landau damping) to suppress instabilities
  Stable particle motion at large amplitudes

## Slide 12: Integrable Optics Collaboration
FNAL, SNS, JINR, Budker INP, BNL, JAI, U. of Colorado, TechX, UMD, U. of Chicago
Internal review (Feb 2012):
  https://indico.fnal.gov/conferenceDisplay.py?confId=5151

## Slide 13
Elements of Integrable Optics Concept
“Integrable Optics” solutions:
  Make motion regular, limited and long-term stable (usually involves additional “integrals of motion”)
Can be Laplacian (with special magnets, no extra charge density involved)
Or non-Laplacian (with externally created charge –e.g. special e-lens E(r) ~r/(1+r^2) – “McMillan type”
Both types will be tested in IOTA

## Slide 14
Integrable Optics at IOTA
Main goals for studies with pencil electron beam:
  Demonstrate a large tune spread of ~1 (with 4 lenses) without degradation of dynamic aperture ( minimum 0.25 )
  Quantify effects of a non-ideal lens and develop a practical lens (m- or e-lens)

## Slide 15
Concept: 2-m long
nonlinear magnet
SBIR Phase I Grant: Radiabeam Technologies

## Slide 16: Ideal case: single nonlinear lens
A single 2-m long nonlinear lens creates a tune spread of ~0.25.
FMA, fractional tunes
Small amplitudes
(0.91, 0.59)
Large amplitudes
0.5
1.0
0.5
1.0
νx
νy

## Slide 17: Experiments with electron lens
5-kG, ~1-m long solenoid
Electron beam: ~0.5 A, ~5 keV, ~1 mm radius
Example: Tevatron electron lens
150 MeV beam
solenoid
Electron lens
current density:

## Slide 18
Practical McMillan-type round electron lens
All excited resonances have the form k ∙ (x + y) = m
They do not cross each other, so there are no stochastic layers and diffusion
e-lens (1 m long) is represented by 50 thin slices. Electron beam radius is 1 mm. The total lens strength (tune shift) is 0.3
FMA analysis

## Slide 19
Space Charge Compensation:
Bringing Protons to IOTA
Allows tests of Integrable Optics with protons and realistic Space-Charge beam dynamics studies
Allows Space-charge compensation experiments
2.5 MeV RFQ HINS

## Slide 20: Space Charge Forces & Compensation
B=E
Z, beam
direction
r, across the beam

## Slide 21
Space-Charge Compensation in Circular Accelerators
Goal:
  Experimental demonstration of the space-charge compensation technique with electron columns/electron lenses at dQ_sc >1
Collaboration Team:
  Fermilab (M.Chung, V.Shiltsev, et al)
Why ASTA:
  Need 2.5 MeV high-current protons and IOTA – flexible lattice storage ring
Relevant accelerators:
  All current and future high intensity proton rings (Booster, MI, all LHC injectors, MC rings, etc)

## Slide 22
Optical Stochastic Cooling Experiment
Goal:
  Experimental demonstration of the optical stochastic cooling technique (1st – no optical amplifier, then with OPA)
Why ASTA:
  Need IOTA – low energy (150 MeV – minimal synchrotron radiation damping) flexible lattice e- storage ring
Motivation:
  Cooling for high energy accelerators (e.g. LHC, MC)

## Slide 23: Optical Stochastic Cooling
Suggested by Zolotorev, Zholents, and Mikhailichenko (1994)
OSC obeys the same principles as the microwave stochastic cooling, but exploits the superior band-width of optical amplifiers, ~1014 Hz
Pick-up and kicker must work in the optical range and support the same band-width as the amplifier
  Microwave pickups can not be scaled to µm
  Undulators were suggested
Initial experiments can be done without an amplifier but eventually we will need state-of-art optical amplifier
  High power
  Low delay

## Slide 24: Principles of OSC

## Slide 25: OSC experimental set-up (λ = 2 µm)
IOTA
Beam by-pass delay: ~4 mm

## Slide 26
Natural SR
damping rate:
~2 s-1
Main Parameters of IOTA OSC experiment

## Slide 27: Electron Wave Function Size Measurements
Collaboration: S. Nagaitsev, V. Danilov (SNS) and N. Vinokurov (Budker INP)
Initial experiments at VEPP-3 (1990-s)
  Unfortunately, the photomultipliers were slow – their response time was around 160 ps. The signal time difference from two photomultipliers was well within this number, therefore it was concluded that the wave function size is much shorter than that resolution.
Hanbury Brown – Twiss Interferometer

## Slide 28: Proposed experimental scheme
Having well-defined initial conditions and time structure, the radiation of a single electron may be a “standard candle” source for various kinds of quantum optics experiments with the high-order field correlation function. The experimental and theoretical investigation of the stationary state of the electron in a storage ring is useful for the development of non-perturbative methods of quantum electrodynamics, and, in general, the foundations of the quantum theory.
undulator
detector
electronics
photons in
visible range
IOTA
single circulating electron

## Slide 30: Summary
There are now 4 IOTA ring experiment proposals.
IOTA goals are well aligned with HEP investments in Intensity and Energy Frontiers
IOTA (and experiments) is a great project for post-docs and/or graduate students
  Interest from U of Chicago, U of Colorado, UMD
Unique opportunity for US PAS students and for FNAL-sponsored internships.