## Slide 1
High Bandwidth Transverse Feedback
within the
LHC Injector Upgrade Project
(LIU)
W. Hofle
CERN BE-RF-FB
10.06.2013

## Slide 2: CERN Accelerator Complex
LHC: 450 GeV to 7 TeV, protons
400 MHz
SPS: 26 GeV/c to 450 GeV,
protons for LHC
200 MHz, 800 MHz
PS: Protons 1.4 GeV – 26 GeV/c
future: 2 GeV – 26 GeV/c
3 – 10 MHz, 13 MHz, 20 MHz, 40 MHz, 80 MHz
bunch structure of 25 ns created
PSB: 50 MeV to 1.4 GeV,
future: 160 MeV to 2 GeV
0.6-1.7 MHz, 1.2-3.4 MHz
LINAC2 (protons), 200 MHz
to be replaced by LINAC4
(H- , under construction) 352 MHz

## Slide 3
Accelerator | Digital / analogue processing | Power / kicker / bandwidth | Status
PS Booster (protons) 50 MeV – 1.4 GeV kin. E. (future: 160 MeV to 2 GeV kin E) no ecloud, long bunches | multi turn injection from Linac 2 analogue beam offset signal suppression, analogue delay (cables & switches) | 100 W, 50 W stripline Limited to 13 MHz in operation But built for 100 MHz bandwidth, baseband | H-plane: used and required V-plane: beam stable w/o FB upgrade planned (LIU)
PS (protons, ions) 1.4 GeV – 25 GeV (kinetic E) (future injection at 2 GeV) ecloud observed when beam bunched at 25 ns Spacing, coupled bunch | digital system, synergy with LHC Damper for The low level digital processing 80 MHz clock frequency | 2 kW solid state power amplifier; 112 W stripline (0.9 m length), with ~30 MHz bandwidth in baseband, lower cut-off ~50 kHz | upgrade (LIU) commissioning started 2012 injection damping and feedback will be beneficial in particular for high intensity CNGS beams and LHC beams. Currently horizontal instabilities are cured by introducing coupling to the vertical plane which constrains the tunes
SPS (protons, ions) (14 – 450) GeV/c protons FT (26 – 450) GeV/c LHC beam ecloud observed and is a potential limitation for 25 ns spacing | digital notch filter and 1T-delay (Altera FPGA, 80 MHz clock) commissioned in 2000/2001 | tetrode amplifiers with two 30 kW tetrodes in push-pull directly coupled to a kicker (base band); feedback bandwidth ~10 kHz to 20 MHz | 2001 upgraded for LHC beams H-plane: used in operation V-plane: used in operation used and required for operation above 5x1012 protons (max ~5.5x1013 ppp accelerated) upgrade under way
SPS High Bandwidth Feedback | digital @ 4 – 8 GS/s clock | under development within LARP/LIU, GHz BW | CERN LIU Project Feedback Review end July 2013
LHC (protons, ions) protons: 450 GeV/c – 7 TeV/c ecloud observed and is a potential limtation for 25 ns spacing | digital notch filter and 1T-delay, built-in diagnostics 14 bit DAC / DAC Altera FPGA, 40/80 MHz clock 2 um rms resolution | tetrode amplifiers with two 30 kW tetrodes in push-pull directly coupled to kicker (base band) similar to SPS system 3 kHz -> 20 MHz | 2010 fully commissioned injection damping feedback used in ramp and physics, essential for LHC operations
Transverse Feedback Systems in LHC and its Injectors

## Slide 4: Intra-bunch Transverse Feedback
Analog
Front
End
Analog Back
End
Signal
Processing
BPM
Kicker
Power Amp
ADC
DAC
Beam
Active closed loop
Feedback
transverse
position
pre-processed
sampled
position
“slices”
calculated
correction data
correction
signal
pre-distortion
drive signal

## Slide 5: Intra-bunch Damping at Work: CERN PS Transverse Feedback
PS TFB ON
10 ns/div
PS TFB ON
10 ns/div
A. Blas et al.
IPAC’13, WEPME011
D. Perrelet (CERN BE-RF)
10 ns/div
PS TFB ON
10 ns/div
PS TFB OFF
1.4 GeV  26 GeV
Challenge:
Time of Flight Compensation
Fully digital implementation

## Slide 6
SPS Simulations with Feedback
K. Li et al., IPAC’13, WEPME042
ECI
TMCI
Bandwidth need at SPS injection 450 GeV/c
from simulation (2.7 ns bunch length)
ECI: 500 MHz
TMCI: 200 MHz
increasing FB gain
increasing FB gain
CERN Headtail Code

## Slide 7
S, DR, DV signals
E. Métral et al., 2003
S. Aumon, 2010
also candidate for cure by high bandwidth feedback
if it were / became a limitation
ecloud instability at PS extraction another candidate for high bandwidth feedback
Transverse Instability in PS at Transition

## Slide 8: Example of LHC 2012 Instability at the end of Squeeze
End of Squeeze
Indications of intra bunch motion
Operational optimum being searched using existing systems for cure (bunch-by-bunch damper, octupoles, chromaticity)
Review of Instability Diagnostics http://indico.cern.ch/conferenceDisplay.py?confId=234589
Internal Review on Performance Limitations
(September 2013)
Can a High Bandwidth Feedback
help in LHC ?
B. Salvant et al., 2013

## Slide 9
From established LHC Operation to
LHC High Luminosity Operation
Important for injectors:
two very different scenarios:
25 ns bunch spacing (ECI !)
50 ns bunch spacing (TMCI !)
LIU (“LHC Injector Upgrade”)
project addresses upgrades
in the injector chain
(LINAC)PSBPSSPS
to meet HL requirements
 | LHC 2012 OP | LHC nominal | HL-LHC 25 ns | HL-LHC 50 ns
Energy | 4 TeV | 7 Tev | 7 Tev | 7 Tev
# Bunches | 1380 | 2808 | 2808 | 1404
bunch spacing [ns] | 50 | 25 | 25 | 50
p/bunch [1011] | 1.55 | 1.15 (0.58A) | 2.2 (1.11 A) | 3.5 (0.88 A)
gex,y [mm] | 2.3 | 3.75 | 2.5 | 3.0
Peak lumi [1034] | 0.66 | 1.0 | 7.2 | 8.3
Lumi levelling | no | no | 5x1034 | 2.5x1034
#Pile up | 34 | 25 | 123 | 123
Status from May 2012 (L. Rossi @LARP CM18)
added: leveling to lower peak lumi at 50 ns
2014+
Future upgrade
today

## Slide 10
  Increase performance  higher brightness
    LINAC4 (H- linac) is being constructed
    raise of injection energy into PSB from 50 MeV to 160 MeV (LINAC4)
    increase injection energy into PS (space charge limits) 1.42 GeV
    SPS: RF upgrade (power), Q20 optics (lower gT)  TMCI
    vacuum chamber coating in SPS as part of ecloud mitigation
    high bandwidth feedback
    LLRF upgrades in PSB,PS,SPS with additional long./cavity feedbacks
    upgrades for beam transfer, collimation, scraping, instrumentation
  Increase reliability and lifetimes (exploitation until 2030+)
  Spares, radio-protection, replacement of aging equipment
  Project timeline: “baseline” completed after LS2 (long shutdown 2 of LHC)
  installations; LS1 started at end of 2012
LIU project: Goals and Means

## Slide 11
objective: cure transverse “single bunch” instability by feedback
two collective effects are limiting the
SPS performance as LHC injector
  e-cloud
  TMCI
  similarities: both effects cause vertical intra bunch instability
high chromaticity suppresses instability to a certain extent
feedback expected to permit running at low chromaticity and at intensities beyond which high chromaticity is an established cure
review of SPS mitigation strategy (ecloud / TMCI) around 2015/2016
Feedback important to maintain small transverse emittances
Also beneficial to provide enhanced stability for scrubbing beam (two bunchlets spaced 5 ns every 25 ns)
Complementary to existing coupled bunch feedback (20 MHz bandwidth)
Motivation for High Bandwidth Feedback in SPS

## Slide 12
RF, low radiation
special instrumentation
no RF infrastructure
extraction CNGS/LHC
injection
slow extraction
radiation high
current transverse FB
extraction LHC
LSS3 layout followed up
by working group under LIU
led by E. Montesinos (BE-RF)
alternative location
base line location
for wide band TFB
Implementation in SPS: Locations for transverse feedbacks in SPS

## Slide 13
New kickers – Tunnel Space
  Short (array of) striplines, slotted wave guides, cavities ?
  Location: dispersion supressor, flat vacuum chamber
  Frequency reach < 1.5 GHz
  Cabling / Infra-structure being prepared in LS1 (2013/2014)
Low attenuation, low dispersion
“smooth-wall” coax-cables 7/8”
installed in May 2013

## Slide 14: Time-Line: SPS Implementation of vertical High Bandwidth Feedback
Year 4
Year 3
Year 2
Year 1
Year 5
Phase 1:
2017
2014
2013
2012
2011
2015
2016
2018
Year 6
Year 7
demonstrator
power amplifiers for phase 2 tendering (s)
phase 2 beam tests
Phase 2:
review for
phase 2:
Phase 3:
Final implementation
go / no-go
phase 3:
2019
new pick-up design and construction
kickers design and construction

## Slide 15
CERN contributions
  Accelerator Physics Support: Simulations, integration studies for implementation in SPS (optics, aperture, impedance)
  Coordination, interface for potential contributions in Europe (for example kicker hardware from INF – Frascati)
  Project fully integrated within LHC Injector Upgrade Project (LIU)
    Engineering (FPGA and electronics development)
    Pick-up design and construction
    Fabrication of final system, vacuum structures, electronics
    Integration of components, vacuum testing, tunnel infra-structure, cabling
    Integration with Control System
    Machine Developments, Commissioning

## Slide 16
Summary
  SPS can profit from High Bandwidth Transverse Feedback in a number of ways: 25 ns and 50 ns upgrade variants (TMCI, ECI), and during scrubbing (scrubbing beam !)
  Interest and potential applications in PS and LHC  SPS is also a test-bed
  CERN committed to upgrade transverse feedbacks and high bandwidth transverse feedback in injectors within LIU Project frame
  2012 / 2013 Beam Tests with SLAC developed demonstrator hardware successful: Feedback loop closed with 3.2 GS/s digitization using a single bunch  confidence in digital technology
  Full exploration of demonstrator with beam requires new hardware be put in place to overcome bandwidth limitations of present kicker  down selection of kicker options ongoing, infrastructure put in place for installation of new kickers as early as at end of LS1, power amplifiers
  New pick-up design launched at CERN
  Full bandwidth tests in SPS between LS1 and LS2 mandatory to propose such a system for LHC as well as the final implementation for the SPS