## Slide 1: Laser stripping for CERN HP-PS
W. Bartmann, B. Goddard, R. Steerenberg
with a lot of input from V. Danilov and D. Johnson
3rd mini-Workshop H- Laser Stripping and Accelerator Applications 26-27 Sept 2013, Fermilab

## Slide 2: Outline
Introduction to HP-PS
Laser stripping concepts
  H- neutralisation
  H0 --> p+ stripping
Laser characteristics
Issues & Questions

## Slide 3
Introduction to HP-PS

## Slide 4: Present CERN Accelerator Complex
LINAC 2: proton source with ~ 1 Hz
Time sharing between experiments
LHC
SPS
PS
PSB
Experiments & Test Beams
LINAC 2
50 MeV

## Slide 5: Replacing LINAC2 by LINAC4
LHC
Double the brightness for existing accelerator complex
Also first stage of LP-SPL as injector for HP-PS
HP-PS in the framework of LAGUNA-LBNO study
Can pulse at 2 Hz, but ~ 1 Hz for the existing complex
SPS
PS
PSB
Experiments & Test Beams
LINAC 4
160 MeV

## Slide 6: Possible CERN Accelerator Complex with HP-PS
LHC
SPS
PS
PSB
Experiments & Test Beams
LINAC 4
LP - SPL
CN2PY
Target
2 MW
HP-PS
2 Hz
1 Hz
1 Hz
160 MeV
4 GeV
50 / 75 GeV
Inj. / Extr.
Collimation
Acceleration
3-fold Symmetry

## Slide 7: Low Power SPL parameters
Parameter | Values | Units
Kinetic Energy | 4 | [GeV]
Beam power | 0.144 | [MW]
Repetition rate | 2 | [Hz]
Beam pulse length | 0.9 | [ms]
Average pulse current | 20 | [mA]
Peak pulse current | 32 | [mA]
Protons per pulse | 1.13 x 1014 | -
Peak power per cavity | 0.5 | [MW]
Can be easily extended to required 2ms

## Slide 8: Beam temporal structure
Macropulse injection over ~2ms (500-600 turns)
SPL microbunch structure at 352 MHz

## Slide 9: Parameters HP-PS cf PS2
Parameter | 50 GeV |  | 75 GeV | Units | PS2
Inj. / Extr. Kinetic Energy | 4 / 50 |  | 4 / 75 | [GeV] | 4/50
Inj./ Extr. Beam power | 0.19/2 | 0.13/2 |  | [MW] | 0.05/0.35
Repetition rate | 1 |  |  | [Hz] | 0.5
frev / fRF @ inj. | 0.248 / 38.97 |  |  | [MHz] | 
RF harmonic | 157 |  |  | - | 
frev / fRF @ extr. | 0.255 / 40.08 |  | 0.255 / 40.09 | [MHz] | 
Bunch spacing @ extr. | 25 |  |  | [ns] | 
Total beam intensity | 2.5 x 1014 |  | 1.7x1014 | - | 1.1e14
Number of bunches | 147 |  |  | - | 168
Intensity per bunch | 1.7x1012 |  | 1.25x1012 | - | 6.3e11
Main dipole field inj. / extr. | 0.17 / 2.1 |  | 0.17 / 3.13 | [T] | 0.0667/1.7
Ramp time | 500 |  | 500 | [ms] | 
Dipole field rate dB/dt (acc. ramp) | 3.9 |  | 5.9 | [T/s] | 

## Slide 10: HP-PS lattice
One LSS for injection and extraction
Total length of LSS: 73.5 m
Triplet concept based on FNAL design
24 m for H- injection

## Slide 11: H- injection foil stripping
24 m

## Slide 12: Which parameters differ from PS2?
Number of injected turns
  500-600 turns needed instead of 200-300
  More foil hits, emittance blowup, foil heating
Beam loss and activation
Repetition rate
  1 Hz instead of 0.5 Hz
Target emittance
  13 um both planes (1 sigma rms normalised) instead of 2.5 um
Motivation to also look into laser stripping

## Slide 13
Laser stripping for H- injection

## Slide 14: Doppler shift of laser frequency
At 4 GeV:
n=2 can be reached with 47.5° between ion beam and laser
n=3 with 8.39 °

## Slide 15: H- neutralisation: Wiggler
Magnet with ∫B·dl
Vertical  no extra horizontal angular spread which would increase the laser power
Need at least 0.6 T to keep emittance growth small
Integration could be an issue

## Slide 16: H- neutralisation: Laser
No emittance growth
Easier integration than wiggler?
Numerical calculation of neutralisation degree
Laser micro pulse energy required for 99% neutralisation
60mJ per micropulse
with factor 1000 reduction from recycling
fRF=352MHz and Tinj =2ms
gives 42 J per macropulse

## Slide 17: H- neutralisation: Laser Feshbach resonance as alternative?
Feshbach resonance appears at 113.49 nm (10.93 eV) in the H- photodissociation spectrum
With 1064 nm laser accessible with intersection angle of 37°
To reach 99% neutralisation (crosssection~1.39e-15 cm2) a laser micropulse energy of 190 uJ is required
However: Δλ/λ~5.2e-6 while beam Doppler spread ~2e-3
Need another factor 5e2 for full beam neutralization, leads to a laser micropulse energy of 73 mJ

## Slide 18: H- neutralisation: Laser n=2 shape resonance as alternative?
The resonance at 112.95 nm for the reaction
  cross-section of 9.8e-17 cm2
Requires 2.8 mJ micropulse energy but with much larger linewidth of 1.8e-4 resulting in a total micropulse energy of 31 mJ
The H0 is then already in an excited state and can be resonantly excited from n=2 to n=3
Dual advantage of longer lifetime for spontaneous decay and shorter lifetime for stripping to p+ in magnetic field

## Slide 19: H0 --> p+ stripping
SNS scheme:
Resonant excitation of ground-state H0 in field free region
Stripping of excited electron in magnetic field
Large spread of effective resonance frequencies divergent beam
For excitation to n=2 or n=3: 360 and 92 uJ laser micropulse energy
Spontaneous decay reduces the efficiency:
1.7% of n=3 decay in 25 cm drift between laser interaction and stripping point

## Slide 20: Dispersion tailoring
Need a Dpx of about 2.0 rad
LSS has zero dispersion
Target emittance should not be significantly affected by injection process
Assuming a target emittance of ~13 um
Injected transv emittance: 0.4 um, emittance growth less than 0.3 - 0.5 um
Assuming a maximum acceptable dispersion of 0.2 m
Dpx < 0.05 rad

## Slide 21: Fringe field stripping – emittance growth
Lifetime in magnetic field depends on quantum state, B-field and ion momentum
Lifetimes of 4 GeV H0* in dependence of B and a simulated fringe field
numerically integrated to get rms angle error and hence emittance growth
n=3 gives Δε of 2 – 4 um for B = 1 T
Careful fringe field design needed!
Normalised emittance growth for different H0* quantum states as a function of peak magnetic field

## Slide 22: Stark broadening
Overcome Doppler broadening by placing interaction region in a magnetic field  large Stark-broadening of transition
Single frequency can excite the resonance for all atoms
To reach Doppler width of 2e-3 need 0.3 T for n=3 transition
Lifetime of H0* only 1e-10 s
Required laser micropulse energy slightly higher than previous method
Excitation takes place over ~0.5 m which introduces a large angle between injected and circulating protons  difficult integration
Stark-broadening of quantum levels vs B-field for 4 GeV H0

## Slide 23: Laser characteristics (H0 --> p+ stripping)
Parameter |  | n=2 | n=3
Wavelength | nm | 1064 | 1064
Laser/H- angle | deg | 47.50 | 8.39
Angular spread | deg | ±0.10 | ±0.42
Micropulse energy | uJ | 360 | 92
Macropulse length | ms | 2 | 2
Macropulse energy | J | 253 | 65
Peak power (single pass) * 3 (margin) | MW | 21.6 | 5.5
Average power (single pass) | kW | 43.2 | 11.0
Average power (mode-locking) | W | 760 | 193
Average power (Q=100) | W | 432 | 110
Vertical laser beam height (1 σ rms) | mm | 1.5 | 1.5
Linac pulse, 1 σ rms separated by 2.84 ns | ps | 15 | 15
Laser pulse shape required, rectangular | ps | 50 | 50
Laser repetition rate (max) | Hz | 1 | 1
Availability | % | 99 | 99

## Slide 24: Summary
Base line is foil stripping system
Foresee to combine it with a laser stripping system
Laser stripping base line:
  Wiggler for neutralisation
  Resonant excitation to n=3
    avoid large emittance growth
    Intersection angle 8.4°
    Precludes operation below 4 GeV
    Laser power remains main issue
  Final stripping in 3rd chicane dipole (careful fringe field design)
  Dispersion tailoring limited by emittance growth
Alternatives:
  n=2 shape resonance to neutralize H-
  resonant excitation from this level

## Slide 25: Issues & Questions
Feasibility of laser parameters
  Peak power?
  Which Q values to be expected from optical resonators?
  Mode-locking possible?
  Is the 2ms pulse length an issue?
300 J through vacuum window?
Combination of foil and laser system, 3- and 4- magnet bumps with dispersion closed?
Fringe field design of stripping magnet