## Slide 1: Fermilab Laser Stripping Effort
David Johnson
Accelerator Physics center
Fermilab
September 26, 2013

## Slide 2: Fermilab and Laser Stripping
Initial interest in laser assisted stripping injection was for 8 GeV injection into the Main Injector/Recycler.  Looks like this may be pushed off for many (???) years
Looked at 2 GeV injection during a brief ICD 2 configuration with a new RCS (2009).
Now, a potential utilization of laser stripping could be for an upgraded Booster multi-turn injection (again at 1 GeV) this relies heavily on SNS experience
Collaborate on SNS Laser Stripping Project
Other than collaborating with SNS, we are not actively involved in a Laser Stripping design for Fermi accelerators as we really don’t know (at this point) what we will be building, but we want to stay involved.
Develop laser expertise here through smaller laser projects

## Slide 3: Beam parameters for 8 GeV Recycler/MI Laser Stripping Injection
Linac Beam
  Bunch length corresponds to +/- 12mm (80 ps) with and rms of about 16 ps.
  Assuming phase jitter assume maximum bunch length of +/-20 mm (130 ps) with an rms of 26 ps worst case.
  Best case, if longitudinal tails can be removed, a distribution result from tracking without errors gave a 6ps rms distribution
  For this calculation assume rms bunch length of 20ps.
Transport line parameters
  Beta x 20 - 40 meters -6 sigma truncated Gaussian size between 5 and 8 mm
  Beta y 10 – 20 meters – 6 sigma truncated Gaussian size between 4 and 5 mm

## Slide 4: Excitation Efficiency
Peak power levels of the Laser stripping process using the standard 3 step process in the absence of a magnetic field for 8 GeV.
Timofey Gorlov

## Slide 5: Laser Power Estimates for 8 GeV laser Assisted Stripping
Wavelength [nm] | 1900 | 1064 | 1900 | 1064 | 1900 | 1064
 | elliptical |  | circular |  | Strong Field | 
Incidence angle [deg] | 49.8 | 94.6 | 49.8 | 94.6 | 49.8 | 94.6
Peak Power, P0 [MW] | 1.1 | 5 | 1.1 | 5.5 | 2.1 | 10
Micropulse energy [mJ] | 0.08 | 0.3 | 0.08 | 0.4 | 0.14 | 0.7
Power at 325 Mhz [kW] | 26 | 100 | 26 | 130 | 47 | 230
Power at 162.5 Mhz [kW] | 13 | 50 | 13 | 65 | 24 | 115
Micropulse duration (rms) [ps] | 29 | 28 | 29 | 28 | 27 | 28
X-rms size [mm] | 4.3 | 5.0 | 2.1 | 2 | 2 | 2
Y-rms size [mm] | 1.9 | 1.9 | 2.1 | 2 | 2 | 2
X’-divergence [mr] | 1.4 | 0.6 | 1.7 | .8 | 0 | 0
Y’-divergence [mr] | 0.9 | 0.6 | 1.7 | .8 | 0 | 0
*Timofey Gorlov (SNS)
Required Laser Parameters for 98% stripping Efficiency

## Slide 6: Booster Injection at 1 GeV
The current Project X RDR Stage 1 includes a 1 GeV CW linac to supply ~1MW to a Spallation Target Experimental area and modifications to the existing Booster to increase it’s injection energy to 1 GeV.

## Slide 7: Current Booster
15 Hz resonant magnet system
Inject 1-10 turns @2.2 us/turn
5E12 @7.5 Hz (upgrade to 15Hz now underway
2.4 kW injected beam power
No phase space painting
>380 ug/cm2 foil -> 99.9% stripping efficiency
New 3 magnet chicane (2005)
No injection absorber
Losses due to H0 & H- -> a few R on contact (2nd magnet)
24 FD0DF cell

## Slide 8: 1 GeV Booster Injection
Proton Intensity requirement 7.5e13 out of MI @120 GeV
Booster provides12 pulses of 6.5E12/15Hz per MI cycle
Assuming 95% efficiency inject 7E12/15Hz into Booster
  If beam run on all cycles 18 kW injected and 125 kW extracted
LINAC – 2.1MeV CW RFQ creates 162.5 MHz bunch train
Bunch-by-bunch chopper in the MEBT create extraction notch
Average current 1 mA (over 1 us) 3.8E7 H-/bunch (assuming all bunches are filled
HE end of linac 650 MHz superconducting elliptical cavities
  dE/E 0.025% (100% energy spread 0.25 MeV bunch length 3.8 ps
  Transverse rms normalized emittance 0.25 p and 0.3 p-mm-mr (H&V)

## Slide 9: Modifications to Lattice
Injection straight 6m between gradient magnets (no room to add an injection absorber -> increase in injection power X8)
  Reduce “D” gradient magnets on either side by 25% (keep bc same)
  Opens up straight by 12% (i.e. 0.72m)
  Introduces small beta and dispersion error (<5%) that can easily be corrected
Present chicane dipole design field 2.8 kG at 15 kA
  Capable of 30 mr at 1 GeV
  Lorentz stripping at 1 GeV and 2.8 kG -> loss rate ~10-8/m
  Could utilize existing magnets (with modifications to cross over buss)

## Slide 10: Potential Injection Configurations
Three or four bump chicane
Horizontal or vertical injection
Want to limit field in injection magnets that see H-
foil
H-
H0
H+
absorber
chicane
septum
foil
absorber
Horizontal Injection
Vertical Injection
Do we Need to employ Laser Stripping injection ?
Vertical Injection

## Slide 11: Transverse painting
Final 95% normalized painted emittance eR=20 p-mm-mr
Average injected 95% normalized emittance eL=1.7 p-mm-mr
Ratio eL / eR = 0.085 (compared to SNS 0.01 and JPRAC 0.0185)
Painting options:
  Painting both dimensions in ring – SNS
  Painting one dimension and steer in the other – JPARC
  Correlated or anti-correlated
Choice of painting scheme and bump motion important in determining number of hits.
Horizontal beam size factor 2 smaller than vertical so the closed orbit is moved off slower leading to a greater number of foil hits.

## Slide 12: Lattice Mismatch
J B-Wang,C. Prior SNS/BNL Note 080
Optimal positioning/orientation of injected beam in circulating beam ellipse.
In our case a ~ 0 for both ring and line (upright ellipse)
Injected beam proper aspect ratio (minimize hits)
Booster Lattice at Foil
Paint x & y
Paint x & steer y
Determines values for transport line lattice functions

## Slide 13: Foil heating
With no painting the average number of hits per particle on the foil is just Nt/2
  For Np = 7.4E12/cycle and Nt ~ 600 Total foil hits ~ 2.2E15
With painting and the foil the same size as the injected beam and assuming proper matching conditions the minimum number of hits can be estimated by
For parameters here: hmin ~ 6
Booster circ. sx= 3mm and sy= 6mm , linac beam sx= .5 mm sy=1 mm
Assume:
  Hit distribution similar to circulating beam distribution
  Use # hits/particle as 425 to give a total of 3.15E15 hits/ms (way over estimate)
  Maximum hit density in the central sq. mm is ~1014 /mm2/ms
  Ignore cooling from delta electrons
D. Raparia

## Slide 14: Foil Heating ANSYS Model
Assume :
total hit on foil 3.15E15 in 1 ms (~1E14 in central mm2)
sx=3mm sy=6mm gaussian
15 Hz rep rate
dE/dx = 1.94 MeV-cm2/g
Heating power 320W
Foil: r=2.2 g/cm2
k= 13.7 W/cm-K
e= 0.8
h=1.5 um
radius = 5 cm
circ. Fixed @ 300K
two surface radiate
include thermal conduction
( Zhijing Tang FNAL)

## Slide 15: Summary
Effort on 8 GeV injection has been put on the back burner.
A preliminary look at injecting into Booster at 1 GeV (18 kW injection) shows
  that if the straight section can be suitably modified, standard stripping foil technology could be utilized
  A dedicated injection absorber must be installed
  We should still investigate the potential for laser stripping.
We continue to support SNS efforts in the development of an operational Laser Stripping injection insert.