## Slide 1: Fermilab Linac Laser Notcher
David Johnson, Todd Johnson, John Sobolewski, Kevin Duel, Peter Prieto, Andrea Saewert

## Slide 2: Background
Booster utilizes multi-turn injection of H- ions where the Linac pulse length is determined by N*tREV .
A “notch” must be created in continuous Booster bunch structure to allow for the rise time of the extraction kicker.
Current technique is to use fast kickers in the Booster to remove a section of the Booster beam (50-60 ns out of ~2.2 ms) at an energy of 400 to 700 MeV and deposit it in a shielded absorber in the ring.
To minimize activation, it is advantageous to create the “notches” in the Booster beam at the lowest energy possible.
Even better to create notches outside the Booster tunnel at an energy below to coulomb barrier potential (i.e. 750 keV, the energy of the Linac RFQ)

## Slide 3: Laser Notching Experiment
In 2001, Ray Tomlin reported on a successful experiment to create notches in the CW linac beam in the H- 750 keV beam and have this notch survive at Booster injection.
He created a 25 ns notch utilizing a 200 mJ 5 ns laser pulse.

## Slide 4: Linac Bunch Structure
Choice:
laser with 60 ns pulse at 450 kHz with burst at 15Hz or
laser with 1.5 ns pulse at 201.25 MHz for 10 pulses and burst at 450 kHz and 15 Hz
24.2 us (~ 11 Booster turns)
2.2 us
67 ms
~22-25 us
5 ns (bunch spacing)
~1-1.5 ns bunch length
201.25 MHz bunch spacing
450.75 kHz “notch” spacing (Booster rev. freq.)
15 Hz macro pulse rep rate
MACRO
MINI (11 turns)
MICRO
2.2 us
10-12*5ns = 50 -60 ns

## Slide 5: Photoneutralization (1)
The fraction of electrons that are detached from the moving H- ions is:
The photon flux (generated by the laser)
in the lab frame [photons/cm2/sec]
The photon flux in the lab frame is transformed into the
rest frame of moving ion as:
The interaction (crossing) time is just the ion path length/ ion velocity
The neutralization factor for an ion crossing on axis
of the laser beam may be written in terms of lab frame parameters
For q ~ 90o term -> ~g

## Slide 6: Photoneutralization (2)
Rest frame energy 1.16 eV for
1064 nm laser
Cross section 3.66x10-17 cm2
To maximize the neutralization probability->maximize the product
fixed
To maximize
increase pulse energy -> minimize
reduce pulse length -> bunch length
reduce laser spot size -> ion size
To maximize t for a given H- ion energy
increase horizontal laser beam size or
increase the number of laser interactions
with the ion bunch
20-30 mJ
Assume:
Laser size 0.6x6mm
~1J

## Slide 7: Reduction of Pulse Energy
To reduce the required pulse energy we can effectively increase the interaction time by utilizing an optical cavity such that the laser interacts with the ion beam multiple times.
H-
Linear cavity (zig-zag)
Laser follows ion to interact many times (increase t)
Cavity length proportional to number of interactions
Laser pulse length = notch length
Cavity dimensions determined by ion velocity and bunch spacing
Reduces required laser pulse energy by ~ number of interactions
R. Shafer , 1998 BIW
2 mJ for 99.92%

## Slide 8: Expected Beam Dimensions
Phase space simulation at end of RFQ (figure 4.40 of 750 KeV Upgrade Plan)
Trace 3D back calculation of beam size at exit of RFQ based upon emittance measurement at 178 kW power August 9, 2012 CY Tan.
Laser beam vertical profile (1/e2) ~ 5 mm.
Initial design assumed that the vertical laser beam dimension of 1 cm.
Beam measurements indicate vertical laser size could be reduced to 6 mm
This is a variable parameter in the beam shaping optics.

## Slide 9: Location of Notcher
RFQ
MEBT

## Slide 10: Laser system (1)
Laser system is a MOPA design
Major components of system
  CW Seed source (100 mW Lumics)
  Mach-Zander 10 GHz EOM modulator (Photline)
  Arbitrary Waveform Generator
  Two stages of fiber pre-amplifiers (10 nJ/360 nJ) (PriTel)
  PCF based Fiber Amplifier (10 uJ) (Optical Engines) on order
  Free Space DPSS amplifier (>2 mJ) (Northrop Grumman CEO) FY14
  Beam shaping optics (current R&D effort)
  Beam delivery (FY14)
  Vacuum interface and optical cavity (in final design)
  Laser diagnostics (conceptual design) (FY14)
  Timing/controls system (conceptual design) (FY14)
We have set up the first three components and demonstrated the generation of temporally uniform optical pulses
In hand
OPG

## Slide 11: Burst mode seed pulses to Fiber Amplifier followed by Free Space Amp
l1=1064nm
120 mW CW
SW=0.1 nm
10 GHz Mach-Zehnder
Modulator
Pulse Generator
Amplifier, Timing
PM Fiber
Lins ~5dB
Li~1.8dB
15 Hz
Pockels cell
Updated 10/3/2012
Generate 24 us burst at 15 hz
TRANSPORT BEAM SHAPING OPTICS &
OPTICAL CAVITY
Fiber Pre-Amp
Fiber Amp 1
Fiber Amp 2
Free Space Amp
Output modulator/Input fiber pre-amp:
201.25MHz pulses (1.25 ns pulse), 458kHz burst
Clean up filter
Isolator
Line filter
Free
Space
Grumman CEO DPSS OEM
Diode + TC
controlled
*Notch 12 bunches -> 60 ns
10 notches/linac pulse
Measurement point
Not needed with a pulsed Fiber Amp 2
Laser System (2)

## Slide 12: OPG test results
450.75 kHz burst of 201 MHz pulses
One set of 201.25 MHz pulses
Individual 201.25 MHz temporally uniform pulses
Pre-distortion of EOM pulses
Yellow- AWG
Purple- RF Amp out
Green – signal form 1.2 GHz (free-space)PD laser pulses out of fiber pre-amplifier
AWG: Chase Scientific DA12000 & CG6000 module

## Slide 13: Beam Shaping
We would like to demonstrate > 99% neutralization efficiency for all ions in the bunch, therefore we would like all ions to “see” the same photon flux regardless of their transverse amplitude. (i.e roof-top laser profile)
  The vertical size of the laser beam should be ~> 6s of the ion bunch
  Squeezing the horizontal laser beam size increases the flux but also reduces the interaction time of the ions passing through (not a big effect due to multiple interactions) also, necessary for optical cavity geometry
Todd Johnson

## Slide 14: Beam shaping (2)
An elliptical laser profile with major/minor axis of roughly 6mm by 1 mm is created from the Gaussian output of the DPSS by a cylindrical matching telescope. (For testing purpose we use 532 nm diode)
Currently, this elliptical profile is matched into a refractive optical system (Galilean) which transforms a TEM00 profile into a collimated flattop (top-hat or uniform) profile through phase profile manipulations.
The device is called a pShaper (from AdlOprica GmbH)
Input
Output

## Slide 15: Beam Shaping (3) the layout
Input pShaper
Output pShaper
Output Anamorphic prism

## Slide 16: Beam Shaping (4) transport
Optical cavity ~ 40 cm from optical box
Optical path length in cavity ~ 35 cm
Clearly have issues propagating roof-top profile
We are investigating other techniques to resolve this issue
5 cm after the prism
50 cm after the prism
Camera scale ~5 x 7 mm (HxV)
Todd Johnson

## Slide 17: Optical Cavity
Attach to RFQ
Interface with MEBT
Laser IN
Laser OUT
Mirrors at 2.288o wrt H- beam
showing 21 interactions
John Sobolewski
H-
2”

## Slide 18: Optical Cavity (2)
We printed a 3D model to test design
This was very useful as it pointed out several
improvements/modifications to the design.

## Slide 19: Other Applications
Broad band laser chopper (see next slide)
Emittance carving
  Laser-controlled proton beam for medical imaging*(DOE/URA patent (U.S. PATENT NO. 5,760,395) Carol Johnstone
      Employ a laser to perform selective extraction of a proton beam from a larger, parent H- beam through the photodetachment of the outer electron.  raster the laser across a larger transverse uniform H- beam.
      Uses: proton radiography, proton cardiography, proton irradiation, and similar medical applications for the diagnosis and treatment of tumors
H- beam extraction technique using Nd:YAG laser
  Proposed for JPARC Experimental Transmutation facility
Clean up of bunch longitudinal tails
Other ????

## Slide 20: Laser Chopper (Example)
Could be for macro pulse or bunch-by bunch chopping
  Project X /PXIE requires a wide band chopper to create a flexible bunch pattern for distribution of beam to rings and experimental areas.
Current design of MEBT and choppers

## Slide 21: Chopping System Example
Estimate laser system required for previous chopping example:
  Laser wavelength: 1 micron
  Laser pulse length <~ 1 ns
  Laser pulse energy: 250-300 micro-Joules
  Number of reflections: 200
    This is pretty long . Depending on laser design, maybe install multiple sequential systems
  Zig-zag cavity insertion length: ~ 24 cm
  Neutralization fraction: 99.96%
  Average power at 162.5 MHz (CW): ~40 kW

## Slide 22: Summary
We have proposed to develop a Laser Notching system for the Fermilab Linac-Booster system.
This project is funded through the Proton Improvement Plan
We have a design for the laser system, beam shaping, and optical cavity that will neutralize > 99% of selected linac bunches.
We have the front-end laser system with the final fiber amplifier on order and are in the process of R&D on beam shaping and working on the final design of the optical cavity
The current plan is to install the system in Q2 of Fy15
This could be utilized as a demonstration or prototype for laser chopping….