## Slide 1
 | SNS | CERN | Fermilab | Laser Notcher
H- Energy (GeV) | 1 GeV | 4 GeV | 8 GeV | 750 KeV
H- Power (MW) | 1.2 – 3 MW | 0.19 MW | 340 KW | 4 W
Microbunch length | 50 ps | 40 ps | 60 ps | 1-1.5 ns
Microbunch frequency | 402.5 MHz | 352 MHz | 335 MHz | 201.25 MHz
Macropulse length (ms) | 1 ms | 2 ms | 4 ms | 22-25 us (50-60ns)
Macropulse rep. rate | 60 Hz | 1 Hz | 10 Hz | 15 Hz (450.75 KHz)
Stripping scheme | n=3 | n=3 | n=3 | Ionization
Laser wavelength | 355 nm | 1064 nm | ~1-2 um | 1064 nm
Micropulse energy | 50 uJ | 92 uJ | 80 uJ | 2 mJ
Macropulse energy | 20 J | 65 J |  | 20 mJ
Average power | 1200 W (20KW) | 65 W (33 KW) |  | 0.3 W (12 KW)
Optical cavity | 100 x | 100x | w/o cavity? | 21 reflections
Motivation | Loss control, radiactivation | Loss control, radiactivation, double turn # | Loss control, radiactivation | Loss control, radiactivation
Status | Ready for 10us experiment | Feasibility study | Feasibility study | Plan to install in Q2 2015

## Slide 2
Laser beam quality | critical if w/ optical cavity
Spectrum width (FT limited?) | Needs to study its impact on stripping The requirement determines laser type Nd:YAG gain bandwidth
Linewidth of individual longitudinal mode | affects buildup cavity. Should < frep/Finesse
Polarization needs to be linear | Polarized field is needed for stripping. Important for cavity development.

## Slide 3: Sarah’s Talk
SNS beam: 1 ms @ 60 Hz, 50 ps @ 402.5 MHz
Laser wavelength: 355 nm
Laser power: 1 MW
Challenges: 1 ms pulse width; cavity recycling
Status: Ready for the 10us@10Hz experiment
Questions: laser power attenuation, vibration simulation, interaction scheme, head-on will enable green light, commercial interest in laser stripping? Beam mismatch

## Slide 4: Timofey’s Talk
Hydrogen atom in electric field, 1GeV beam ground state needs 40T, 2nd 5T, 3rd state 1.5T
Why high gradient of magnetic field is important? Gradient will result in emittance of remainder particles
Laser power needed for 1-2 excitation is 6 times lower than that for 1-3 excitation
Magnetic field induces stark broadening
Particle beam energy spread requires laser frequency sweeping: 0.3 mrad divergence
Laser stripping computation model is implemnted in the PyOrbit code

## Slide 5: Walfgang Bartmann’s Talk
Laser stripping in CERN HP-PS
Linac 2, 50 MeV, proton source, 1Hz
Linac 4, 160MeV, 2Hz
LP-SPL, 4GeV to ring, 50/75GeV output from ring
Energy 4GeV, beam power 0.144 MW, 2Hz, 0.9 ms pulse width
Average pulse current 20 mA, peak pulse current 32 mA, protons per pulse 1.13x10^14, peak power per cavity 0.5 MW (?)
Macropulse injection over 2ms (500-600 turns)
SPL micropbunch 352 MHz, 15 ps
Motivation of looking into laser stripping: beam loss and activation, double number of injected turns from 200-300 to 500-600 turns
Doppler shift of laser frequency: at 4GeV, n=2 can be reached with 47.5 deg between ion beam and laser; at n=3, the angle becomes 8.39 deg, laser wavelength: 1064 nm
H- neutralization with laser: 99% yield, 60mJ per micropulse , assuming 1000 reduction from recycling, 352MHz, 2ms, 42 J per macropulse
N=2 shape resonance as alternative

## Slide 6: Walfgang Bartmann’s Talk
N=2 shape resonance as alternative
Hw+
112.9nm, 42 mJ/per micropulse
For excitation to n=2 or n=3, 92uJ per micropulse energy
Laser pulse
  360uJ/92uJ micorpulse width 50ps
  Macropulse length 2ms/2ms, energy 253J/65J,
  Mpeak power 21.6MW/5.5MW
  Averge power 43KW/11KW (760W/193W with temporal matching)
  Average power (Q=100 cavity) 432W/110W
Status: feasibility study, 5-10 years

## Slide 7: Dave Johnson’s Talk
Fermilab’s laser stripping: Originally interested in 8GeV injection; currently adjusted for an upgraded booster multi-turn injection (again at 1GeV), relying on SNS experience.
Have a preliminary conceptual design for 8GeV
Linac beam: bunch length 80ps with rms of about 16 ps; maximum 130ps with an rms of 26 ps worst case; assuming 20ps in this calculation.
For 8GeV beam, 3-step stripping, 1900 nm laser light needs 2 MW, while 1064 nm laser needs 10 MW for 99.5% stripping efficiency
Macropulse energy, 0.14 mJ (1900), 0.7 mJ(1064)
Average power
Current Project X RDR Stage 1 includes a 1 GeV CW linac to supply ~1MW
Current booster: 15Hz , inject 1-10 turns@2.2 us/turn, 5e12@7.5Hz, 2.4KW injected beam power, no phase space painting, >380 ug/cm^2 foile >99.9% stripping efficiency, 18KW injection can use standard foil technology
Motivation of looking at laser stripping: loss control
Status: no implementation in the near future

## Slide 8: Mark Notcutt’s Talk
First experiments with power buildup cavity at 355nm
Aim at 100 enhancement factor, achieved 25