## Slide 1: TLEP luminosity optimization and other topics
M. Koratzinos,
TLEP13 workshop
Fermilab, 25 July 2013

## Slide 2: Previous episodes
The aim is to see the progress since we last reported on this topic during the 4th TLEP workshop at CERN in April this year
This talk contains a hodge-podge of topics, revolving around the question: “what kind of performance can we expect from a circular collider?”

## Slide 3: Major limitations
The major limitations of circular colliders are:
  Power consumption limitations that affect the luminosity
  Tunnel size limitations that affect the luminosity and the energy reach
  Beam-beam effect limitations that affect the luminosity
  Beamstrahlung limitations that affect beam lifetimes (and ultimately luminosity)

## Slide 4: Energy reach
In a circular collider the energy reach is a very steep function of the bending radius. To make a more quantitative plot, I have used the following assumptions:
  RF gradient: 20MV/m
  Dipole fill factor: 90% (LEP was 87%)
I then plot the energy reach for a specific ratio of RF system length to the total length of the arcs
and

## Slide 5: Energy reach
Assumptions: 20mV/m, 90% dipole fill factor.
What is plotted is the ratio of RF length to total arc length
LEP2 had a ratio of RF to total arc length of 2.2%
Chart: Energy reach
| 94.247372358495895 | 133.28591220741205 | 163.24123740477759 | 188.49474471699182 | 210.7435312943316 | 230.85797187640267 | 249.35510898188321 | 266.57182441482416 | 282.74211707548778 | 298.03636013884255 | 312.58317159004378 | 326.48247480955524 | 339.81373361630466 | 352.64137696920039
5% RF | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000
2% RF | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000
1% RF | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000 | 11000 | 12000 | 13000 | 14000
TLEP175 sits comfortably below the 1% line

## Slide 6: Luminosity of a circular collider
Luminosity of a circular collider is given by
Which can be transformed in terms of
and
to:

## Slide 7: Luminosity of a circular collider
So, the maximum luminosity is bound by the total power dissipated, the maximum achievable beam-beam parameter (the beam-beam limit), the bending radius, the beam energy, , and the hourglass effect (which is a function of sigma_z and beta*)

## Slide 8: Beamstrahlung – a reminder
I am using the approach of Telnov throughout
The energy spectrum of emitted photons during a collision of two intense bunches (usual bremstrahlung formula) is characterized by a critical energy
Where ρ is the radius of curvature of the affected electron which depends on the field he sees
And the maximum field can be approximated by

## Slide 9: Beamstrahlung
So, the critical energy turns out to be
for the maximum field (it would be smaller for a smaller field)
Telnov’s approximation:
    10% of electrons see maximum field
    90% of electrons see zero field
constants

## Slide 10: Beamstrahlung
Electrons are lost if they emit a gamma with an energy larger than the momentum acceptance, η:
We define or otherwise
The number of photons with
So we see that η can directly be traded off by
Going up in energy aggravates the effect

## Slide 11: Beamstrahlung energy dependence
For a specific ring, power consumption, emittances and ξ:
Number of particles per bunch scales with gamma:
And u scales with γ2. This produces a steep drop in lifetime with increased energy

## Slide 12: Beamstrahlung limitation
Plot on left is if we run with a value of the beam-beam parameter of 0.1
Above ~180 GeV is difficult to run without opting for a more modest beam-beam parameter value (which would reduce the luminosity)
Chart: beam energy (GeV)
| 45 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200
Telnov | 0 | 0 | 0 | 0 | 0 | 0 | 13418546375.7779 | 142133842.3139 | 4353015.2273 | 281778.1853 | 31431.2285 | 5258.9532 | 1197.8707 | 346.5226 | 121.0025 | 49.1068 | 22.506
Telnov tuned | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 171565700090.3045 | 1300443855.5842 | 27891678.6805 | 1295040.724 | 106840.1935 | 13643.2359 | 2443.1191 | 570.7617 | 164.8462 | 56.5081
TLEP Latest parameter set, mom. acceptance 2.2%
Can even run at 250GeV with a beam-beam parameter of 0.05

## Slide 13: Comparison with simulation
The Telnov formula was checked against a realistic simulation (Guineapig – courtesy the ILC) at different energies
[work of M. Zanetti] and found to be pessimistic
Chart: TLEP-t comparison
| 0.02 | 2.5000000000000001E-2
TLEP-t Telnov | 13.3149 | 67.7332
Telnov tuned | 30.5282 | 297.2793
TLEP-t GuineaPig | 46.6 | 459.7
Chart: TLEP-H comparison
| 0.02 | 2.5000000000000001E-2
TLEP-H Telnov | 15.588 | 81.7085
Telnov tuned | 37.6239 | 382.4001
TLEP-H GuineaPig | 32.8 | 252.8
The ‘tuned’ model corresponds to an ad hoc tuning of the Telnov formula to fit the data better: instead of 10% of the electrons seeing a 100% field, 100% of electrons see a 70% field

## Slide 14: Beta* and hourglass
We are opting for a realistic β*y value of 1mm. σz beam sizes vary from 1mm to 3mm. In this range the hourglass effect is between 0.9 to 0.6
Chart: R for beta*_y of 1mm
| 4.5 | 4.4000000000000004 | 4.3 | 4.2 | 4.0999999999999996 | 4 | 3.9 | 3.8 | 3.7 | 3.6 | 3.5 | 3.4 | 3.3 | 3.2 | 3.1 | 3.0000000000000102 | 2.9000000000000101 | 2.80000000000001 | 2.7000000000000099 | 2.6000000000000099 | 2.5000000000000102 | 2.4000000000000101 | 2.30000000000001 | 2.2000000000000099 | 2.1000000000000099 | 2.0000000000000102 | 1.9000000000000099 | 1.80000000000001 | 1.7000000000000099 | 1.6000000000000101 | 1.50000000000001 | 1.4000000000000099 | 1.30000000000001 | 1.2000000000000099 | 1.1000000000000101 | 1.00000000000001 | 0.90000000000001001 | 0.80000000000001004 | 0.70000000000000995
R | 0.49065 | 0.49646 | 0.50244 | 0.50858 | 0.51489 | 0.52138 | 0.52807 | 0.53495 | 0.54203 | 0.54934 | 0.55687 | 0.56463 | 0.57264 | 0.58091 | 0.58946 | 0.59829 | 0.60742 | 0.61686 | 0.62663 | 0.63675 | 0.64724 | 0.6581 | 0.66937 | 0.68105 | 0.69317 | 0.70576 | 0.71882 | 0.73238 | 0.74645 | 0.76106 | 0.77621 | 0.7919 | 0.80815 | 0.82492 | 0.84218 | 0.85989 | 0.87794 | 0.89619 | 0.91444
Self-consistent sigma_z at different energies (latest values)

## Slide 15: Beam-beam parameter
The maximum beam-beam parameter is a function of the damping decrement:
where
Or, more conveniently:

## Slide 16: Maximum beam-beam
There is considerable debate as to the exact form of the function .
Assmann and Cornelis argue for
It is not the right time to debate what can be achieved in TLEP. However, we can use the above formulation since:
  It is conservative
  It fits well the LEP data it was derived from
  It has been tuned on 4 simultaneous IPs
  We end up with tune shifts that are not extremely large
Reference: Assmann and Cornelis, THE BEAM-BEAM INTERACTION IN THE PRESENCE OF STRONG RADIATION DAMPING, CERN - SL-2000 - 046 OP

## Slide 17: and tune shift
Beam-beam tune shift as function of beam-beam parameter for typical LEP tune.
There is a considerable deviation from the expression that is equal to the tune shift (which is true for low values only). For values of 0.1 and with the LEP optics, the deviation is 35%. There is also a considerable effect on β*y – in the case of LEP it changed from 5cm to 2.8cm at high beam-beam parameters.
Reference: W. Herr et al., IS LEP BEAM-BEAM LIMITED AT ITS HIGHEST ENERGY? Proceedings of the 1999 Particle Accelerator Conference, New York, 1999.
…to be pursued

## Slide 18: Variation of with energy
Chart: TLEP
| 45 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 175 | 180 | 190 | 200
 | 0.029509 | 0.033486 | 0.041676 | 0.050144 | 0.058859 | 0.067795 | 0.076931 | 0.086253 | 0.095746 | 0.1054 | 0.1152 | 0.12514 | 0.13522 | 0.15057 | 0.15575 | 0.16619 | 0.17674
Blue: Assmann &Cornelis on LEP data
Red: limit due to hitting a resonance
Green: same function, but normalised on KEKB achieved beam-beam parameter
In the absence of a definitive prediction for the moment, a value of around 0.1 for most energies can be assumed (except TLEP-Z)
Max. beam-beam parameter

## Slide 19: Expected luminosity vs energy
Chart: beam energy [GeV]
| 45 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200
 | 9.1786e+35 | 6.6912e+35 | 3.8722e+35 | 2.4385e+35 | 1.6336e+35 | 1.1473e+35 | 8.364e+34 | 6.284e+34 | 4.8403e+34 | 3.807e+34 | 3.0481e+34 | 2.4782e+34 | 2.042e+34 | 1.7024e+34 | 1.4342e+34 | 1.2194e+34 | 1.0455e+34
 | 4.5893e+35 | 3.3456e+35 | 1.9361e+35 | 1.2192e+35 | 8.168e+34 | 5.7366e+34 | 4.182e+34 | 3.142e+34 | 2.4201e+34 | 1.9035e+34 | 1.5241e+34 | 1.2391e+34 | 1.021e+34 | 8.5121e+33 | 7.1708e+33 | 6.0971e+33 | 5.2275e+33
Single IP luminosity of a circular collider of 9000m bending radius as a function of energy. Power loss is 100MW. ξy between 0.05 and 0.1

## Slide 20: Expected luminosity vs energy
Chart: beam energy [GeV]
| 45 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250
 | 9.1786e+35 | 6.6912e+35 | 3.8722e+35 | 2.4385e+35 | 1.6336e+35 | 1.1473e+35 | 8.364e+34 | 6.284e+34 | 4.8403e+34 | 3.807e+34 | 3.0481e+34 | 2.4782e+34 | 2.042e+34 | 1.7024e+34 | 1.4342e+34 | 1.2194e+34 | 1.0455e+34 | 9.0315e+33 | 7.855e+33 | 6.8744e+33 | 6.0504e+33 | 5.353e+33
 | 4.5893e+35 | 3.3456e+35 | 1.9361e+35 | 1.2192e+35 | 8.168e+34 | 5.7366e+34 | 4.182e+34 | 3.142e+34 | 2.4201e+34 | 1.9035e+34 | 1.5241e+34 | 1.2391e+34 | 1.021e+34 | 8.5121e+33 | 7.1708e+33 | 6.0971e+33 | 5.2275e+33 | 4.5157e+33 | 3.9275e+33 | 3.4372e+33 | 3.0252e+33 | 2.6765e+33
Single IP luminosity of a circular collider of 9000m bending radius as a function of energy. Power loss is 100MW. ξy between 0.05 and 0.1

## Slide 21: Published parameter set
 | TLEP Z | TLEP W | TLEP H | TLEP t
Ebeam [GeV] | 45 | 80 | 120 | 175
circumf. [km] | 80 | 80 | 80 | 80
beam current [mA] | 1180 | 124 | 24.3 | 5.4
#bunches/beam | 4400 | 600 | 80 | 12
#e−/beam [1012] | 1960 | 200 | 40.8 | 9.0
horiz. emit. [nm] | 30.8 | 9.4 | 9.4 | 10
vert. emit. [nm] | 0.07 | 0.02 | 0.02 | 0.01
bending rad. [km] | 9.0 | 9.0 | 9.0 | 9.0
κε | 440 | 470 | 470 | 1000
mom. c. αc [10−5] | 9.0 | 2.0 | 1.0 | 1.0
Ploss,SR/beam [MW] | 50 | 50 | 50 | 50
β∗x [m] | 0.5 | 0.5 | 0.5 | 1
β∗y [cm] | 0.1 | 0.1 | 0.1 | 0.1
σ∗x [μm] | 124 | 78 | 68 | 100
σ∗y [μm] | 0.27 | 0.14 | 0.14 | 0.10
hourglass Fhg | 0.71 | 0.75 | 0.75 | 0.65
ESRloss/turn [GeV] | 0.04 | 0.4 | 2.0 | 9.2
VRF,tot [GV] | 2 | 2 | 6 | 12
dmax,RF [%] | 4.0 | 5.5 | 9.4 | 4.9
ξx/IP | 0.07 | 0.10 | 0.10 | 0.10
ξy/IP | 0.07 | 0.10 | 0.10 | 0.10
fs [kHz] | 1.29 | 0.45 | 0.44 | 0.43
Eacc [MV/m] | 3 | 3 | 10 | 20
eff. RF length [m] | 600 | 600 | 600 | 600
fRF [MHz] | 700 | 700 | 700 | 700
δSRrms [%] | 0.06 | 0.10 | 0.15 | 0.22
σSRz,rms [cm] | 0.19 | 0.22 | 0.17 | 0.25
/IP[1032cm−2s−1] | 5600 | 1600 | 480 | 130
number of IPs | 4 | 4 | 4 | 4
beam lifet. [min] | 67 | 25 | 16 | 20
 | TLEP Z | TLEP W | TLEP H | TLEP t
Ebeam [GeV] | 45 | 80 | 120 | 175
circumf. [km] | 80 | 80 | 80 | 80
beam current [mA] | 1180 | 124 | 24.3 | 5.4
#bunches/beam | 4400 | 600 | 80 | 12
#e−/beam [1012] | 1960 | 200 | 40.8 | 9.0
horiz. emit. [nm] | 30.8 | 9.4 | 9.4 | 10
vert. emit. [nm] | 0.07 | 0.02 | 0.02 | 0.01
bending rad. [km] | 9.0 | 9.0 | 9.0 | 9.0
κε | 440 | 470 | 470 | 1000
mom. c. αc [10−5] | 9.0 | 2.0 | 1.0 | 1.0
Ploss,SR/beam [MW] | 50 | 50 | 50 | 50
β∗x [m] | 0.5 | 0.5 | 0.5 | 1
β∗y [cm] | 0.1 | 0.1 | 0.1 | 0.1
σ∗x [μm] | 124 | 78 | 68 | 100
σ∗y [μm] | 0.27 | 0.14 | 0.14 | 0.10
hourglass Fhg | 0.71 | 0.75 | 0.75 | 0.65
ESRloss/turn [GeV] | 0.04 | 0.4 | 2.0 | 9.2
VRF,tot [GV] | 2 | 2 | 6 | 12
dmax,RF [%] | 4.0 | 5.5 | 9.4 | 4.9
ξx/IP | 0.07 | 0.10 | 0.10 | 0.10
ξy/IP | 0.07 | 0.10 | 0.10 | 0.10
fs [kHz] | 1.29 | 0.45 | 0.44 | 0.43
Eacc [MV/m] | 3 | 3 | 10 | 20
eff. RF length [m] | 600 | 600 | 600 | 600
fRF [MHz] | 700 | 700 | 700 | 700
δSRrms [%] | 0.06 | 0.10 | 0.15 | 0.22
σSRz,rms [cm] | 0.19 | 0.22 | 0.17 | 0.25
 | 5600 | 1600 | 480 | 130
number of IPs | 4 | 4 | 4 | 4
beam lifet. [min] | 67 | 25 | 16 | 20
By definition, in a project like TLEP, from the moment a set of parameters is published it becomes obsolete and we now already have an improved set of parameters.
The new parameter set contains improvements to our understanding, but does not change the big picture.
IPAC13 TUPME040, arXiv:1305.6498 [physics.acc-ph]

## Slide 22: The improvements
Emittance scales as the third power of the cell length. So with a cell length of 30m (compared to the 78m assumed size up to now), horizontal emittance at 175GeV is as low as 0.2nm. This is 100 times smaller than the published values we have been using up to now.
For the improved set, we have conservatively used a cell length of 50m, which still gives a horizontal emittance of 2nm at 120GeV
The lower emittance gives considerably more flexibility in the design
We also now have a self-consistent bunch length taking into account the effect of beamstrahlung (derived analytically and in agreement with simulation results)

## Slide 23: New parameter set
 | TLEP-Z | TLEP-W | TLEP-H | TLEP-t | 
Ebeam [GeV] | 45 | 80 | 120 | 175 | 
beam current [mA] | 1440 | 154 | 29.8 | 6.7 | 
#e−/bunch [1011] | 4.0 | 1.0 | 3.7 | 0.88 | 7.0
horiz.,vert. emit. [nm] | 29.2, 0.06 | 3.3, 0.017 | 7.5, 0.015 | 2.0, 0.002 | 16.0, 0.016
β∗x,y [mm] | 500, 1 | 200, 1 | 500, 1 | 1000, 1 | 
σtotz,rms [mm] | 2.93 | 1.98 | 2.11 | 0.77 | 1.95
ESRloss/turn [GeV] | 0.03 | 0.3 | 1.7 | 7.5 | 
ξx,y/IP | 0.068 | 0.086 | 0.094 | 0.057 | 
/IP[1032cm−2s−1] | 5860 | 1640 | 508 | 132 | 104
beam lifetime [min] (rad. Bhabha) | 99 | 38 | 24 | 21 | 26
beam lifetime [min] (beamstrahlung, using Telnov formula with h=2%) | >1025 | >106 | 38 | 14 | 2 [12 if h=2.5%]
 | TLEP-Z | TLEP-W | TLEP-H | TLEP-t | 
Ebeam [GeV] | 45 | 80 | 120 | 175 | 
beam current [mA] | 1440 | 154 | 29.8 | 6.7 | 
#e−/bunch [1011] | 4.0 | 1.0 | 3.7 | 0.88 | 7.0
horiz.,vert. emit. [nm] | 29.2, 0.06 | 3.3, 0.017 | 7.5, 0.015 | 2.0, 0.002 | 16.0, 0.016
β∗x,y [mm] | 500, 1 | 200, 1 | 500, 1 | 1000, 1 | 
σtotz,rms [mm] | 2.93 | 1.98 | 2.11 | 0.77 | 1.95
ESRloss/turn [GeV] | 0.03 | 0.3 | 1.7 | 7.5 | 
ξx,y/IP | 0.068 | 0.086 | 0.094 | 0.057 | 
 | 5860 | 1640 | 508 | 132 | 104
beam lifetime [min] (rad. Bhabha) | 99 | 38 | 24 | 21 | 26
beam lifetime [min] (beamstrahlung, using Telnov formula with h=2%) | >1025 | >106 | 38 | 14 | 2 [12 if h=2.5%]
A new parameter set shown at the recent TLEP news. Lower horizontal emittances, larger bending radius, an RF frequency of 800MHz instead of 700MHz, smaller required momentum acceptance…
Work in progress!

## Slide 24: A possible upgrade path
At low energies (<120GeV beam), the number of required bunches is large, making necessary for different beam pipes for electrons and positrons
At high energies luminosities are limited by the beamstrahlung lifetime
Charge compensation, if it can be made to work to, say, 95% would mean that the number of bunches can be reduced by a factor 20. this would give a manageable number of bunches (4 at 120GeV) that can fit in a single beam pipe

## Slide 25: Number of bunches vs energy
The number of bunches is determined by the total power dissipation and the desire for achieving a specific beam-beam parameter.
Plot on the left for =0.1
Chart: beam energy [GeV]
| 45 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250
 | 52010.9941 | 30711.9719 | 12342.4527 | 5710.4131 | 2928.9219 | 1625.3436 | 959.7491 | 595.9287 | 385.7016 | 258.4883 | 178.4504 | 126.3867 | 91.5288 | 67.5948 | 50.792 | 38.7605 | 29.9922 | 23.4996 | 18.6228 | 14.9114 | 12.0532 | 9.8278

## Slide 26: ‘flipping’ magnets
So if the magnetic field of adjacent beam pipes can be switched, we can run with the following configuration:
This has the potential of a factor 10 in luminosity at high energies. It increases the cost of the magnets. Charge compensation should be investigated.
Electrons
only
Positrons
only
Electrons
positrons
Electrons
positrons
Low energy, many bunches
High energy, few bunches
TLEP dipole magnet
TLEP dipole magnet
Magn. field

## Slide 27: Conclusions
Circular colliders offer excellent luminosity prospects
There has been considerable progress in solidifying the TLEP concept design since the last workshop.
Much more work is needed for a design proper.
[Exotic schemes might offer even more luminosity, so they should be pursued at an early stage, as might have repercussions at the design]

## Slide 28: Thank you
end