## Slide 1
ELECTRO-MECHANICAL PROPERIES of 650 MHz β=0.92 5-cells Dressed Cavity
I. GONIN, T. KHABIBOULLINE
June 25, 2013

## Slide 2
MECHANICAL DESIGN OF 650 MHz β=0.9 CAVITY
IPAC 2013 WEPWO056

## Slide 3
Quantity | Old | New
G, Ω | 256 | 260
Rsh/Q0 max, Ω | 638 | 609
βopt | 0.95 | 0.97
Esurf/Eacc* | 2.08 | 2.04
Bsurf/Eacc*, mT/MV/m | 3.81 | 3.85
Kcouple, % | 0.75 | 1.29
Monopole HOM Qext | 1010 | 106
 | OLD | NEW
r | 50 | 59
R | 200.3 | 200.052
L | 107 | 97.555
A | 82.5 | 84
B | 84.5 | 90
a | 20 | 13
b | 39.5 | 28
α | 7° | 1.3°
 | OLD | NEW
r | 50 | 59
R | 200.3 | 200.052
L | 103.8 | 106.08
A | 82.5 | 85
B | 84 | 78
a | 18 | 20
b | 38 | 33
α | 5.2° | 1.9°
Regular half-cell
End half-cell
DIMENSIONS AND MAIN PARAMETERS OF β= 0.9&0.92 CAVIIES

## Slide 4
The Scope of EM-Mechanical Design Issues
Minimize a sensitivity to microphonics due to He pressure fluctuations (df/dP) and mechanical vibrations
Minimize a Lorentz Force Detuning (LFD) coefficient
Tunability: tuning for correct frequency & for field flatness
Compromise between microphonics detuning (df/dP, LFD, microphonic noise) and cavity tunability (stiffness)
Enough strength to withstand atmospheric pressure
Stress analysis of cool-down from RT to cryogenic temperaure
ES&H manual requires that the cavity is rated at MAWP of 4 bars at 2 K and 2 bars in RT
Incorporate the slow and fast tuners design.

## Slide 5
50mm
59mm
β=0.9&0.92 5 CELLS STRUCTURES AND HV’S MODIFIED MODEL
1030mm
1045mm
59mm
FIXED
SPRING CONSTANT
1042.9/1043.8
Li-i
Rreg
Rend

## Slide 6
df/dP vs. Tuner Stiffnes
Chart: df/dP, Hz/mbar vs Tuner Stiffness
| 0 | 5 | 10 | 20 | 40 | 60 | 80 | 100
0.9 Rend=Rreg=110 | -13.7642 | 0.214 | 4.553 | 8.115 | 10.535 | 11.476 | 11.976 | 12.307
0.92 Rend=Rreg=110 | -8.7 | 3.1 | 6.9 | 9.9 | 11.9 | 12.6 | 13 | 13.3
0.92 Rend=110 Rreg=120 | -12.9 | -4.9 | -0.8 | 3.3 | 6.7 | 8.1 | 8.9 | 9.4
Chart: Rreg, mm
| 110 | 115 | 120
 | 5.4 | 6.3 | 8
Stiffness of β=0.92 caviy kN/mmvs. Radius of the Regular stiffening ring
- Stiffness of β=0.9 cavity

## Slide 7
dF/dP vs. Bellows Radius, Rend=110mm, Rreg=110mm
Chart: df/dP, Hz/mbar vs. Tuner Stiffness
| 0 | 10 | 50 | 100
Bellow 115mm | -9 | 6.9 | 12.2 | 13.3
Bellow 135mm | 41 | 22.9 | 16.8 | 15.7
Bellow 165mm | 180 | 50.9 | 24.5 | 22
R=115mm
R=135mm
R=165mm

## Slide 8
FIELD FLATNESS vs. RADIUS OF THE REGULAR STIFFENING RING
FIXED
Cavity is deformed by tuner at 1 mm
Ring Radius, mm | Flatness %
110 | 1.1
120 | 1.8
Ez(z) along axis